## Slide 1: Proposal to Set Up the Head Restraints GTR Phase２ Examination WG
MLIT, JAPAN
Informal document No. GRSP-41-04
(41st GRSP,7-11 May 2007,agenda item 3.1.1)

## Slide 2
We propose to set up a “WG for the establishment of appropriate methods for testing and evaluating whiplash injury” as phase 2 and provide feedback to the Head Restraints GTR.
2. Background
1. Proposal to set up a new ＷＧ
The head restraints GTR Phase 1 was limited to static requirements.
As for appropriate dynamic tests, dummies with a high human-body fidelity are available, but it is still necessary to continue reviews including the improvement of reproducibility.
Regarding assessment, the insurance industry groups such as IIWPG have already started dynamic tests. Also EuroNCAP plans to introduce dynamic tests starting 2007. However, the testing and evaluating methods vary among them.

## Slide 3
(1) Test conditions： Test conditions that reflect the realities of accidents on the market
  Tests with actual vehicles or on sleds; the number and conditions of sled pulses
(2) Mechanism ： Theories on the mechanism of whiplash injury vary. We do not know yet which one is the best.
  It is necessary to clarify the mechanism by analyzing accidents and performing volunteer tests and simulations with human body FE models.
(3) Evaluation dummies ： We need dummies that reflect the above mechanism with a high fidelity to the human body and a high degree of perfection as a measuring instrument
  BioRID II is promising with its high fidelity to the human body, but still needs improvements in testing methods, structure, etc., because it has a problem in reproducibility.
  It is necessary to reduce the variation of results in initial sitting position of the dummy by improving the sitting method.
3. Subjects of Review and Tasks

## Slide 4
(4) Evaluation indicators ： Indicators of human body injury that reflect the above mechanism
  According to what we have found so far, it is necessary to measure the relative movements between the upper and lower parts of the neck and the forces applied to each of these parts.
(5) Reference values： Should be based on the results of injury risk analysis and feasibility study.
(6) Effect evaluation ： Evaluation of effects on reduction of injury and cost-effectiveness

## Slide 5
4. Schedule
Subjects of review
(1) Test conditions
Tests with actual vehicle or on sleds; the type and conditions of sled pulses
(2) Mechanism
Analysis of data on accidents on the market; Volunteer tests; FEM Simulations
(3) Evaluation dummies
Improvements in the structure of the dummy; assaying method; sitting method
(4) Evaluation indicators
Reflection of injury mechanism; Evaluation with injury values
(5) Reference values
Appropriate values based on injury risks feasibility studies
(6) Effect evaluation
Effect on the reduction of injury in accidents on the market; Cost effectiveness
Schedule
Publication of GRSP
WP29
Feedback to GTR as phase 2

## Slide 6
Thank You

## Slide 7
Supplementary Information

## Slide 8: 1. Mechanism of production of neck injury
Initial position
S-Shape
Hyper Extension
<Behavior of the passenger upon rear collision>
(1) Hyper extension of the neck（MacNab et al. 1964)
Detachment of vertebral disks upon hyper extension in a situation without head restraints
<Injury mechanism>
Rebound
Ramping-up

## Slide 9: S-Shape
(2) Pressure on the spinal neural ganglion due to a change of pressure in the spinal canal（Svensson et al. 1996)
The pressure and flow in the canal rapidly changes due to a change in the volume of the spinal canal, and this produces pressure on the spinal nerve.
(3) The synovial membrane folds of the facets are nipped as the turning center of the body of vertebra rises (Ono, Kaneoka． 1998)
The partial rotation of the body of vertebra in the lower cervical vertebra causes pressure on the facets and ligaments.
(4) Injury due to facet sliding (Yoganandan et al. 2001)
In the lower part of the cervical vertebra, the facets are locally compressed.
１．Mechanism of Production of Neck Injury

## Slide 10
1. Injury indicators - Injury indicators according to shock response
IIWPG
Folksam
ADAC
Euro NCAP
NIC
Bostrom
(Autoliv)
'96
IRCOBI
Represents change in pressure in the cervical canal due to the change of the neck in S
Nkm
Schmitt
(ETH)
'01
ESV
LNL
Heitplatz
(Ford)
'03
ESV
MIX
Kullgren
(Folksam)
'03
ESV
WIC
Muñoz
(CIDAUT)
'05
ESV
T1G
Fx
(upper)
Fz
(upper)
Outline
Adoption as injury indicators
Name
Proponent
Year
Source
Adopted as injury indicators before restriction with the head restraints
Calculated by combining the shearing load and the bending moment applied on the upper part of the cervical vertebra
Shearing load on the upper part of the cervical vertebra
Axial force on the upper part of the cervical vertebra
Not adopted because it does not correspond to whiplash injury some cases.
Adopted as injury indicators before restriction with the head restraints
Adopted as injury indicators before restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints
Calculated by combining the shearing load and the bending moment applied on the lower part of the cervical vertebra
Calculated by combining NIC and Nkm
Calculated by combining the bending moment on the upper and lower parts of the cervical vertebra
Deceleration on the first thoracic vertebra
Adopted as reference for the determination of the seat dimensions
Adopted as reference for the determination of the seat dimensions
Adopted as reference for the determination of the seat dimensions
Adopted as injury indicators during restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints
Adopted as injury indicators during restriction with the head restraints

## Slide 11
IIWPG
Folksam
ADAC
Euro NCAP
IV-NIC
Panjabi
(Yale Univ.)
'99
IRCOBI
Mobile range between vertebral bodies
VT1
Muser
(ETH)
'00
IRCOBI
NDC
Viano
(Saab)
'02
SAE
PWI
Mallory
(NHTSA)
'05
ESV
Rebound
Velocity
Adopted as an injury indicator after the completion of restriction with the head restraints
T
HRC
Adopted as reference for the determination of the seat dimensions
2. Injury indicators - Injury indicators according to shock response
Outline
Adoption as injury indicators
Name
Proponent
Year
Source
Velocity of the head center of gravity relative to T1
Mobile range of the head center of gravity relative to T1
Mobile range of the head relative to the torso
Rebound velocity of the head after the completion of restriction with the head restraints
Timing of contact between the head and the head restraints
Adopted as an injury indicator after the completion of restriction with the head restraints
Adopted as an injury indicator after the completion of restriction with the head restraints
Adopted as reference for the determination of the seat dimensions
Adopted as reference for the determination of the seat dimensions

## Slide 12: 3. Dummies for Whiplash Injury Evaluation
Hy-III
Bio-RID
THOR
RID-3D
Advantages
The relative relationship with human body is good in terms of the rotation angle of the head relative to the torso (NHTSA). Reproducibility and repeatability are good.
The neck is designed as a flexible multi-joint structure and can reproduce behaviors close to the human body.
-
Disadvantages
The neck is harder than the human body  Difference in passenger’ behaviors (deformation in S-form; Straightening of the vertebra)
Repeatability in the same dummy; Reproducibility between dummies; Reproducibility of sitting position; Standardization of calibration
Adoption
NHTSA (FMVSS202)
IIHS (US)
Thatcham (UK)
Folksam (Sweden)
ADAC (Germany)
-
-
The neck is designed as a flexible multi-joint structure and can reproduce behaviors close to the human body.
Originally developed for front collision evaluation; Results in smaller rotation angle due to the high bending rigidity of the neck.
The neck is too soft; the rotation angle of the neck is larger than that observed in volunteer tests (NHTSA).

## Slide 13: Problems in the Evaluation of Bio-RID
1. Repeatability and reproducibility
<Repeatability with the same dummy>
<Reproducibility among different dummies>
2 Reproduction of sitting position of the dummy
Backset when setting the dummy and variation of H-Point
3. Standardization of calibration
⇒Influences the difference of response among dummies

## Slide 14: Method and Criteria for Evaluation of Repeatability
X = Mean value of each dummy
S
d
＝
Standard deviation of each dummy
Method of evaluation
Comparison of coefficient of variation （CV）
Criteria Admissible level: CV≦10
Repeatability
C.V = 100 (%)
X
X
S
d
Cited from
presentation material
for 5th GTR Meeting

## Slide 15: Summary of Evaluation of Repeatability Based on CV
BioRID-II
Hybrid-III
For both of BioRID-II and Hybrid-III, the repeatability of the evaluation indicators was within the limit of tolerance.
Fｚ
Fx
T1 Acc.
HA-TA
Cited from
presentation material
for 5th GTR Meeting
Notes: Bio RID-II:
Those of HA-TA and My-Ext indicators which reach their maximum in the latter period of impact (before from the head restraint) show a large variance.
Indicators such as Fx and Fz, for which no requirements are set for calibration, also show a large variance.
T1 shows a certain variance due to a high response frequency owing to the vertebral structure.
But two dummies show CV of about 5% (acceptable).
Hybrid-III:
As a whole, they show a repeatability of about 5%.

## Slide 16: Method and Criteria for Evaluation of Reproducibility
S
B
X
S
X
G
Reproducibility
C.V = 100 (%)
SB =
n
1/2
MSB-MSW
XG = Mean value of 3 dummies
SB
MSB : Mean square among groups (dummies)
MSW : Mean square in a group (each dummy)
n : Number of repetitions of test
Method of evaluation
Comparison of coefficient of variation （CV）
Criteria
Admissible level: CV≦10
Cited from
presentation material
for 5th GTR Meeting

## Slide 17: Summary of Evaluation of Reproducibility Based on CV
BioRID-II
Hybrid-III
For Hybrid-III, the reproducibility of the evaluation indicators was within the limit of tolerance.
HA-TA
HA-TA
Fｚ
Fx
T1 Acc.

## Slide 18: Standardization of Calibration
To improve repeatability and reproducibility, it is necessary to:
・Ensure the proper maintenance and check required of dummies and standardize setting position, etc.
・Establish standardized calibration tests because the response of dummies varies depending on production lot.
・Reduce the variation of measurements of HRMD, used as reference for the reproduction of sitting position when setting the dummy.
- Develop a (detail) regulation on the calibration of dummies.
- Establish testing methods enabling the maintenance of product performance
  Clarify the design reference position to reduce the variations in setting position.

## Slide 19
Issues on Dummy Setting
Seat Fix Bolt
CG of Head
X
Z
(Ex.) Set dummy posture by using the Design HP and measure the x and z distance of CG of head from seat fix bolt.
Large head position variations during dummy
setting have been observed, depending heavily
on testing personnel factors and seat design factors.
Need to introduce measures to reduce head
position variations.

## Slide 20
4. Testing Method – Comparison of Dynamic Tests
IIWPG
FMVSS202a
FOLKSAM
Form of sled fixture
Fixed on the car
Sled pulse
Dummy used
Evaluation indicators
Fixed on the seat anchor
AM50% HY-III
BioRID II
(1)The backward rotation angle of the head relative to the torso ≤ 12
(2) HIC 15ms  500
(1)Seat Assessment
Time of contact between the head and
the head restraints ≤ 70 ms
T1G (G produced on the upper torso) ≤ 9.5G
(2)Neck Force
Fx and Fz divided into three stages
(1)NIC, (2)Nkm,
(3)Head rebound velocity
V =17.3 km/h
V =16km/h
Assessment in three grades using the total of three indicators and three pulses
Positioning
Legal test
Assessment
V=16 km/h 4.5G V=16 km/h 5.5G V=24 km/h 6.5G
ADAC
V=16 km/h 5 G V=25 km/h 7.3 G V=30 km/h 10 G
neck injury x 0.7 (1)NIC, (2)Nkm,
(3)Head rebound velocity
(4)Fx (5)Fz (6)T1G
(7)HRC (8)Geometry
  Seat Stability ×0.3
(1) Seatback angle
Assessment in five grades