## Slide 1
REGULATION No. 94
(Frontal collision)
Proposal for draft amendments
Proposal submitted by France
Informal Document No. GRSP-42-31
(42nd GRSP, 11-14 December 2007,
agenda item 17(b))

## Slide 2: Aim
The expert from France announced that at the next session he will present a proposal for draft amendments to Regulation N°94 taking into account the outcome of the research on barriers carried out by the EEVC Working Group 15 “Frontal impact and Crash compatibility“
Aim
  reinforce passive safety performance of modern vehicles
  harmonise front-end force of the future fleet

## Slide 3: Background
In 1997 Directive 96/ 79/ CE (Frontal collision) was first introduced (Regulation N°94 alignment in 1998), the European Commission wanted to review certain technical aspects, especially the test speed and the barrier design after a period of implementation.
In 2000, EEVC WG16 (frontal impact) :
  recommended “not to raise the test speed to 60 km/h until there is a better understanding of compatibility”.
  reported: "barrier instability for new generation of car and a barrier stiffness too low for modern vehicles (as they bottom out the barrier), was not the original intent".
In 2007, EEVC WG15 (frontal impact and compatibility):
  recommended, "the test speed of the current offset test (Regulation N°94) must not be raised to 60 km/h without modification of the current test procedure".
  added: "the current test speed for regulation cannot be increased using the existing UNECE Regulation N°94 barrier without increasing the existing discrepancy in frontal stiffness and aggressiveness for the vehicle fleet".

## Slide 4: Today
Current Barrier problems in Regulation N°94, (listed in EEVC WG15 final report):
  Barrier instability for new generation of car, stiffness of barrier too low for modern vehicles.
  Test severity increases with car mass with constant test speed and makes force matching unreachable.
  Self-protection level depends on the vehicle size and mass.
  Difficult to assess force levels with this barrier type and configuration with constant speed tests (bottoming out of barrier causes undesired inertial loads for measurement of a cars frontal force).
  No structural interaction is potentially possible because of load spreading in the barrier and subsequent barrier bottoming out.
Proposed changes:
  Test parameters: test speed, overlap and barrier ground clearance.
  Obstacle: new barrier design (PDB).

## Slide 5
Overlap and ground clearance
The 50 per cent overlap and 150 mm ground clearance ensures that the full front of the vehicle is in direct contact with the barrier when tested in offset conditions.
Relative position of the vehicle front end structure in front of the barrier (side members and lower load paths):

## Slide 6
Structural database of the "Vehicle Crash Compatibility" project (VC‑Compat)
validated by EEVC WG15 and presented on informal document GRSP‑41‑25 (41st GRSP session)

## Slide 7: Comparison of the two deformable elements
Current ECE R94 barrier with constant stiffness
Proposed barrier with Progressive Stiffness

## Slide 8: Test severity: Self protection level
 NEED TO HARMONISE TEST SEVERITY
 NEED TO IMPROVE SELF PROTECTION OF LIGHT CARS
TEST SEVERITY
Current ECE R94
LIGHT CAR
1000 kg
HEAVY VEHICLE
2000 kg
EES: 50 km/h
EES: 44 km/h
Self protection level depends on the vehicle mass / size
Notes:   While test configurations already exist for self-protection, pedestrians and reparability, the same does not apply for compatibility.
  In order to avoid to many test configurations , © we may consider that self protection at 64 km/h ODB test could serve for assessment of compartment force.
  However this is necessary but not enough, because currently everybody knows the need of good structural interactions between front unit. ©
  For this reason, we propose filling this gap with an assessment approach that put under control the non aggressiveness of the front unit.
  This energetic approach associated with this assessment proposal should be the only one way to satisfy both self and partner protection.

## Slide 9: Test severity
New approach
Increase the test severity for light vehicles without changing heavy one’s.
Test severity for all vehicle mass range will be harmonised

## Slide 10: Front crush force
Better force harmonisation between light and heavy vehicles
Current barrier @ 60 kph
New approach @ 60 kph
Current barrier @ 56 kph

## Slide 11: Current Self protection level
INFLUENCE ON VEHICLE FRONT END STIFFNESS |  | 
 | LIGHT | HEAVY
TEST SPEED EFFECT 56 km/h >> 60 km/h | + | + +
DEFORMABLE ELEMENT EFFECT Current barrier >> PDB | + | - -
GLOBAL EFFECT | ++ | =
 LIGHT CARS SELF PROTECTION IS IMPROVED
 HEAVY VEHICLES ARE NOT PENALISED
Notes:   While test configurations already exist for self-protection, pedestrians and reparability, the same does not apply for compatibility.
  In order to avoid to many test configurations , © we may consider that self protection at 64 km/h ODB test could serve for assessment of compartment force.
  However this is necessary but not enough, because currently everybody knows the need of good structural interactions between front unit. ©
  For this reason, we propose filling this gap with an assessment approach that put under control the non aggressiveness of the front unit.
  This energetic approach associated with this assessment proposal should be the only one way to satisfy both self and partner protection.

## Slide 12: Definition of deformable barrier Characteristics of the deformable barrier
The PDB barrier is composed of the following components:
(1) One back plate,
(2) One back deformable core,
(3) Two intermediate plates,
(4) One progressive deformable core,
(5) One front deformable core,
(6) One contact plate,
(7) One outer cladding,
(8) Blind rivets,
(9) Epoxy resin.

## Slide 13: Definition of deformable barrier Barrier validation
Adhesive bonding procedure
Construction
Mounting
Conformity of production (dynamic tests)

## Slide 14: Potential for the future
Compatibility
  Criteria assessment still in progress in EEVC
Application to N1 and M1 vehicles greater than 2,5 tonnes
  Research in progress for light truck with NHTSA
  >> world wide harmonisation possibility
Possible future applications to MDB

## Slide 15: Conclusion
France proposes to set up a new informal group on this subject and is ready to take the lead of this group

## Slide 16
REGULATION No. 94
(Frontal collision)
Proposal for draft amendments
Proposal submitted by France

## Slide 17: Test severity: Energy distribution
 HEAVY VEHICLE IS TWO TIME PENALISED: MASS + TEST CONFIGURATION
 NEED TO INCREASE SELF PROTECTION OF LIGHT CARS
FORCE
LIGHT CAR
1000 kg
HEAVY VEHICLE
2000 kg
FORCE
% OF KINETIC ENERGY ABSORBED
0%
50%
100%
HEAVY
(2000 kg)
LIGHT
(1000 kg)
VEHICLE
BARRIER
Notes:   While test configurations already exist for self-protection, pedestrians and reparability, the same does not apply for compatibility.
  In order to avoid to many test configurations , © we may consider that self protection at 64 km/h ODB test could serve for assessment of compartment force.
  However this is necessary but not enough, because currently everybody knows the need of good structural interactions between front unit. ©
  For this reason, we propose filling this gap with an assessment approach that put under control the non aggressiveness of the front unit.
  This energetic approach associated with this assessment proposal should be the only one way to satisfy both self and partner protection.

## Slide 18
Rigid barrier
Deformable
barrier

## Slide 19
To compensate the severity for heavy vehicles
2 solutions
V fixed
 variation on test speed (V)  Variation on
if m >>> severity

## Slide 20
To compensate severity for heavy vehicles
2 solutions
V fixed
 variation on test speed (V)  Variation on
if m then EES
Politically unacceptable