## Slide 1
10-11 April 2007
Lion
Proposed changes to the EEC UN Regulations 29
Russian Federation
GRSP-INF-CS/7

## Slide 2
Front part strength testing (Test A)
Pendulum energy:
for N1 Category – [25] kJ
for N2 Category – [30] kJ
for N3 Category – 40 kJ
Pendulum:
- dimensions: h=600 mm; l=1000 mm
weight m = 1000-1500kg
Pendulum position:
c=50±5mm ( 50±5 mm below point H (R)),
chain-hanged pendulum, L≥3500 mm, b≥800 mm, a=30 mm
Test A may be skipped for N1 cargo vehicles
based on an already tested model that fulfills
the requirements of the EEC UN Regulations
#94 (or equivalent regulatory documents).
Russian Federation

## Slide 3
Roof strength testing (Test B)
Static load
P =[К]х PCH≤10т,
where PCH – full load of the vehicle that falls to the front axle;
K – dynamic load coefficient.
Test B may be skipped for N1 cargo vehicles
based on an already tested model that fulfills
the requirements of the EEC UN Regulations
#94 (or equivalent regulatory documents).
Russian Federation

## Slide 4
Back part strength testing (Test C – A-pillar test)
Pendulum energy:
- for N1 Category – [15] kJ
- for N2 Category – [20] kJ
- for N3 Category – 30 kJ
Pendulum:
- dimensions: h=500 mm; l=1600 mm
weight m = 1000kg
Pendulum position:
the center of the strike must coincide with the central axial plane of the back wall and be located in the middle between the floor and the roof of the cabin;
- chain-hanged pendulum, L≥3500 mm, b≥800 mm
Russian Federation

## Slide 5
Thanks
for
attention!