| UNITED NATIONS |  | ST |
| --- | --- | --- |
|  | Secretariat | Distr. GENERAL ST/SG/AC.10/C.4/2008/3 8 April 2008 Original: ENGLISH |

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the Globally

# Harmonized System of Classification

# and Labelling of Chemicals

# Fifteenth session,

# Geneva, 9-11 July 2008

# Item 2 (b) of the provisional agenda

UPDATING OF THE SECOND REVISED EDITION OF THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELLING OF CHEMICALS (GHS)

Health hazards

Proposal for amendment of Chapter 3.8 (Decision logics)

Transmitted by the expert from Germany */

A. 	Introduction

1.	As the GHS is already implemented in some countries and will be implemented in several regions in the year to come, it appears that comprehensibility and feasibility are prerequisites to establish harmonized procedures in classification and labelling.

2.	In the course of gaining experience with the GHS criteria, a problem was identified when using the decision logics in chapter 3.8. of the GHS. It was recognized that narcotic effects and respiratory tract irritation (i.e. Category 3 STOT after single exposure) depict different hazards compared to Categories 1 or 2 and therefore Category 3 cannot be a consequence of Categories 1 or 2. In this respect the decision logics need to be amended.

3.	This document contains the proposal for amendment to the respective decision logics of chapter 3.8

B. 	Background

4.	Using the decision logics given in chapter 3.8.5 of the second revised edition of the UN GHS (2007), the following procedure is assumed:

(a)	Is it Category 1? if yes, apply it. If not, check for Category 2.

(b)	Is it Category 2? if yes, apply it. If not, check for Category 3.

(c)	Is it Category 3? if yes, apply it. If not, no classification needs to be applied.

In fact, effects to be taken into account for STOT after single exposure Category 3 classification are entirely different from effects resulting in Category 1 or 2. This might lead to application of both, Category 1 or 2 STOT after single exposure AND Category 3 of the same hazard class. Consequently the effects for Category 1 or 2 and Category 3 need to be assessed separately and the decision logic need to be amended as proposed hereafter.

C. 	Proposal

5.	Amend decision logics 3.8.1 and 3.8.2 in sub-sections 3.8.5.1 and 3.8.5.2 of chapter 3.8 of the GHS to read as follows (changes visible as grey arrows. Current introductory text under 3.8.5 remains unchanged):

3.8.5.1	Decision logic 3.8.1

3.8.5.2	Decision logic 3.8.2 		Footnotes,

-------------------------

# Footnotes

*/ In accordance with the programme of work of the Sub-Committee for 2007-2008 approved by the Committee at its third session (refer to ST/SG/AC.10/C.4/24, Annex 2 and ST/SG/AC.10/34, para. 14).

See 3.8.2 of this Chapter and “The use of cut-off values/concentration limits” in Chapter 1.3, para. 1.3.3.2.

See 3.8.3.4 and Table 3.8.2 for explanation and guidance.

# Text boxes

No

Category 3

Warning

Yes

Not classified

No

No

Yes

Category 2

Warning

Category 3

Warning

Does the mixture contain one or more ingredients classified as a Category 3 specific target organ toxicant at a concentration ( 20% ?

See 3.8.3.4.5. Care should be exercised when classifying such mixtures.

Yes

Category 1

Danger

No

No

Does the mixture contain one or more ingredients classified as a Category 2 specific target organ toxicant at a concentration of 1:

(a) ( 1.0%?

(b) ( 10%?

See Table 3.8.2 for explanation of cut-off values/concentration limits 2.

Category 2

Warning

Does the mixture contain one or more ingredients classified as a Category 1 specific target organ toxicant at a concentration of 1:

( 1.0 and  < 10%?

See Table 3.8.2 for explanation of cut-off values/concentration limits 2.

Yes

Yes

No

Does the mixture contain one or more ingredients classified as a Category 1 specific target organ toxicant at a concentration of 1 :

(a) ( 1.0% ?

(b) ( 10% ?

See Table 3.8.2 for explanation of cut-off values/concentration limits 2.

Yes

Can bridging principles, as in 3.8.3.3, be applied?

Classify in appropriate category

No

(Cont’d on next page)

Yes

Not classified

Following single exposure,

Can the substance or mixture produce narcotic effects or respiratory tract irritation?

See 3.8.2 and 3.8.3 for criteria. Application of the criteria needs expert judgment in a weight of evidence approach.

Yes

No

Yes

Does the mixture as a whole have data/information to evaluate specific target organ toxicity following single exposure?

Category 1

Danger

See decision logic 3.8.2

Classification not possible

No

Yes

Following single exposure,

Can the substance or mixture, be presumed to have the potential to be harmful to human health on the basis of evidence from studies in experimental animals?

See 3.8.2 for criteria and guidance values. Application of the criteria needs expert judgment in a weight of evidence approach.

No

Category 2

Warning

Yes

No

Following single exposure,

(a) Can the substance or mixture produce significant toxicity in humans, or

(b) Can it be presumed to have the potential to produce significant toxicity in humans on the basis of evidence from studies in experimental animals?

See 3.8.2 for criteria and guidance values. Application of the criteria needs expert judgment in a weight of evidence approach.

Yes

Mixture: Does the mixture as a whole or its ingredients have data/information to evaluate specific target organ toxicity following single exposure?

Classification not possible

No

Substance: Does the substance have data and/or information to evaluate specific target organ toxicity following single exposure?