| United nations |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/SC.3/WP.3/2008/3 24 December 2007 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

Inland Transport Committee

Working Party on Inland Water Transport

Working Party on the Standardization of Technical 
and Safety Requirements in Inland Navigation

Thirty-second session

Geneva, 5-7 March 2008

Item 4 (a) of the provisional agenda

Amendments of the Recommendations on Harmonized 
Europe-Wide Technical Requirements for Inland Navigation Vessels (annex to resolution No. 61): Chapter 2, “Procedure and rules for the inspection of inland navigation vessels”

Amendments to Section 2.7, “Official Number”

Note by the secretariat

## Introduction

The Working Party on Inland Water Transport (SC.3) at its fiftieth session asked the Working Party on the Standardization of Technical and Safety Requirements in Inland Navigation (SC.3/WP.3) to prepare amendments to section 2-7 “official number” in order to harmonize its content with the forthcoming provisions on unique European Identification Number of the EC Directive 2006/87/06 (ECE/TRANS/SC.3/174, para. 39). During its thirty-first session in June 2007, SC.3/WP.3 took note of the latest proposal on the revision of Articles 2.17 and 2.18 of the Directive under consideration by the EU member states and asked the secretariat to prepare, based on the proposal, a draft of the revised section 2.7 for the SC.3 fifty-first session (ECE/TRANS/SC.3/WP.3/62, para.19).

At its fifty-first session, the Working Party on Inland Water Transport considered the draft (ECE/TRANS/SC.3/2007/3), noting that the proposed amendments to the EC Directive 2006/87/EC had not yet been adopted. It also discussed whether the official number should remain invariable throughout the existence of the vessel with no exception, which would entail deleting the second and the third phrases in point 2-7.3. The Working Party on Inland Water Transport asked SC.3/WP.3 to reconsider these draft changes to section 2-7 with particular attention to point 2-7.3 and to prepare a new document for its the next SC.3 session (ECE/TRANS/SC.3/178, para. 17).

SC.3/WP.3 may wish to consider the draft changes to section 2-7, proposed in part II of this document, which were prepared on the basis of the comments regarding point 2-7.3 received from Governments. In doing so, it may also wish to take note of the latest proposal of the requirements of Annex II of the Directive and of the Rhine Vessel Inspection Regulation concerning the European vessel number, prepared by the EC/CCNR Joint Working Group, reproduced in the annex to the document.

## Draft Amendments to section 2-7

To modify section 2-7 “Official Number” as follows (Additions to the original text are highlighted in bold and the text to eliminate is highlighted in strike-through):

“2-7   	OFFICIAL NUMBER

2-7.1	The competent authority issuing a certificate shall enter on that certificate the official number assigned to that vessel by the competent authority of the State in which the vessel has been registered or has its home port.

2- 7.2	The official number shall consist of eight Arabic numerals, as follows:

The first two or three digits shall indicate the country and place where the official number was assigned competent authority of the State in which the vessel has been registered or has its home port and which assigned the number.  For this purpose the following key shall apply:

001-019	France

020-039	Netherlands

040-059	Germany

060-069	Belgium

070-079	Switzerland

83		Poland

86		Hungary

88 		Romania

89		Bulgaria

91		United States of America

92		Russian Federation

93		Ukraine

94		Slovakia

95 		Czech Republic

96		Croatia

97		Serbia

98		Republic of Moldova

99		Other states

080-099	reserved for craft from countries that are not party to the Mannheim Convention and for which a Rhine Vessel certificate has been issued before 01.04.2007

100-119	Denmark Norway

120-139	Finland Denmark

140-159	Greece United Kingdom and Northern Ireland

160-179	Ireland

160-169	Iceland

170-179	Ireland

180-199	Italy

180-189	Portugal

190-199	reserved

200-219	Luxembourg

220-239	Austria Finland

240-259	Portugal Poland

260-279	Sweden

260-269	Estonia

270-279	Lithuania

280-299	Spain

280-289	Latvia

290-299	reserved

300-319	United Kingdom and Northern Ireland

300-309	Austria

310-319	Liechtenstein

320-329	Czech Republic

330-339	Slovakia

340-349	Hungary

350-359	Croatia

360-369	Serbia

370-379	Bosnia and Herzegovina

380-399	Hungary

400-419	Russian Federation

420-439	Ukraine

440-449	Belarus

450-459	Republic of Moldova

460-469	Romania

470-479	Bulgaria

480-489	Georgia

490-499	reserved

500-519	Turkey

520-539	Greece

540-549	Cyprus

550-559	Albania

560-569	The Former Yugoslav Republic of Macedonia

570-579	Slovenia

580-589	Montenegro

590-599	reserved

600-619	Italy

620-639	Spain

640-649	Andorra

650-659	Malta

660-669	Monaco

670-679	San Marino

680-699	reserved

700-719	Sweden

720-739	Canada

740-759	United States of America

760-769	Israel

770-799	reserved

800-809	Azerbaijan

810-819	Kazakhstan

820-829	Kyrgyzstan

830-839	Tajikistan

840-849	Turkmenistan

850-859	Uzbekistan

860-869	Iran

870-999	reserved

The next five or six digits of the official number shall indicate the serial number in the register kept by the competent authority.

2-7.3		The official number shall remain invariable throughout the existence of the vessel.  However, if that vessel is registered in another State or if its home port is transferred there, the official number shall no longer be valid.  The ship’s certificate shall then be submitted to a competent authority on the inspection of vessels which shall delete the official number that has ceased to be valid and, if necessary, shall enter the new official number.”

Annex

## The agreed text/ for the requirements of Annex II of the Directive and of the Rhine Vessel Inspection Regulation concerning the European vessel number according to the discussions in the CCNR/EC Joint Working Group meeting of 29 October 2007

Annex II of the European Directive on Technical Provisions 
for Inland navigation Vessels

1.	Articles 2.17 and 2.18 are to be changed as follows:

"Article 2.17

Register of Community certificates

1.	Competent authorities shall assign an order number to the Community certificates they issue.

They shall keep a register in accordance with the model set out in Annex VI of all the Community certificates they issue.

2.	Competent authorities shall keep the original, or a copy of all the Community certificates they have issued, shall enter on these any information and alterations, together with any Community certificate cancellations and replacements, and shall update the register set out in section 1 accordingly.

3.	In order to perform administrative measures for maintaining safety and ease of navigation and for implementation of Articles 2.02 to 2.15 read only access to the register in accordance with the model set out in Annex VI will be granted to competent authorities of other Member States, Contracting States of the Mannheim Convention and, as far as an equivalent level of privacy is guaranteed, to third countries on the basis of administrative agreements.

Article 2.18

European Vessel Identification Number

1.	The unique European Vessel Identification Number (ENI), in the following referred to as European Vessel Identification Number, consists of eight Arabic numerals according to Appendix III.

2.	The competent authority having issued a Community certificate shall enter on that Community certificate the European Vessel Identification Number. Unless the craft possesses a European Vessel Identification Number at the time of issue of the Community Certificate it shall be assigned to that craft by the competent authority of the Member State in which the craft has been registered or has its home port.

As far as craft from countries where an assignation of a European Vessel Identification Number is not possible are concerned the European Vessel Identification Number to be entered on the Community certificate shall be assigned by the competent authority issuing that Community certificate.

3.	Only one single European Vessel Identification Number can be assigned to one craft. The European Vessel Identification Number is issued only once and remains unchanged throughout the whole lifetime of the craft.

4.	The owner of a craft, or his representative, shall apply to the competent authorities for assignment of the European Vessel Identification Number. The owner or his representative shall also be responsible for affixing the European Vessel Identification Number entered in the Community certificate to the craft.

5.	The Member States shall notify the competent authorities responsible for assigning the European Vessel Identification Number to the European Commission. The European Commission keeps a register of competent authorities, including competent authorities notified by third countries, and makes it available to the Member States. On request this register is also made available to competent authorities of third countries.

6.	The competent authorities responsible for assigning the European Vessel Identification Number make all necessary arrangements in order to inform all competent authorities responsible for assigning the European Vessel Identification Number of each newly assigned European Vessel Identification Number as well of data necessary for the identification of the vessel in accordance with Appendix IV. These data may be made available to competent authorities of other Member States, Contracting States of the Mannheim Convention and, as far as an equivalent level of privacy is guaranteed, to third countries on the basis of administrative agreements in order to perform administrative measures for maintaining safety and ease of navigation and for implementation of Articles 2.02 to 2.15 and Article 2.18 section 3."

2.	After Appendix II a new Appendix III is inserted as follows:

"Appendix III

Model of the European Vessel Identification Number

| A | A | A | x | x | x | x | x |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Code of competent authority that assigns the European Vessel Identification Number | Serial Number |

AAA	three digit code of the competent authority according to the following number ranges

xxxxx	five digit serial number

Number Ranges for Competent Authorities

001-019	France

020-039	Netherlands

040-059	Germany

060-069	Belgium

070-079	Switzerland

080-099	reserved for craft from countries that are not party to the Mannheim 		Convention and for which a Rhine Vessel certificate has been issued 		before 01.04.2007

100-119	Norway

120-139	Denmark

140-159	United Kingdom

160-169	Iceland

170-179	Ireland

180-189	Portugal

190-199	reserved

200-219	Luxembourg

220-239	Finland

240-259	Poland

260-269	Estonia

270-279	Lithuania

280-289	Latvia

290-299	reserved

300-309	Austria

310-319	Liechtenstein

320-329	Czech Republic

330-339	Slovakia

340-349	reserved

350-359	Croatia

360-369	Serbia

370-379	Bosnia and Herzegovina

380-399	Hungary

400-419	Russian Federation

420-439	Ukraine

440-449	Belarus

450-459	Republic of Moldova

460-469	Romania

470-479	Bulgaria

480-489	Georgia

490-499	reserved

500-519	Turkey

520-539	Greece

540-549	Cyprus

550-559	Albania

560-569	The Former Yugoslav Republic of Macedonia

570-579	Slovenia

580-589	Montenegro

590-599	reserved

600-619	Italy

620-639	Spain

640-649	Andorra

650-659	Malta

660-669	Monaco

670-679	San Marino

680-699	reserved

700-719	Sweden

720-739	Canada

740-759	United States of America

760-769	Israel

770-799	reserved

800-809	Azerbaijan

810-819	Kazakhstan

820-829	Kyrgyzstan

830-839	Tajikistan

840-849	Turkmenistan

850-859	Uzbekistan

860-869	Iran

870-999	reserved"

3.	After Appendix III a new Appendix IV is inserted as follows:

"Appendix IV

Data necessary for the Identification of a Vessel

1. 	Unique European Vessel Identification Number according to Article 2.18 (Annex V, Part 1, Section 3 and Annex VI, 5th Column)

2. 	Name of the Vessel (Annex V, Part 1, Section 1 and Annex VI, 4th Column)

3. 	Type of Craft according to Article 1.01 (Annex V, Part 1, Section 2)

4. 	Length over all according to Article 1.01 Section 70 (Annex V, Part 1, Section 17a)

5. 	Breadth over all according to Article 1.01 Section 73 (Annex V, Part 1, Section 18a)

6. 	Draught according to Article 1.01 Section 76 (Annex V, Part 1, Section 19)

7. 	Source of Data = Community Certificate

8. 	Deadweight (Annex V, Part 1, Section 21 and Annex VI, 11th Column) for cargo vessels

9. 	Displacement according to Article 1.01 Section 60 (Annex V, Part 1, Section 21 and Annex VI, 11th Column) for vessels other than cargo vessels

10.	Operator

11. 	Issuing Authority (Annex V, Part 1 and Annex VI)

12. 	Number of Community Certificate (Annex V, Part 1 and Annex VI, 1st Column)

13. 	Expiration Date (Annex V, Part 1, Section 11 and Annex VI, 17th Column)

14. 	Creator of Dataset

As far as available the following data shall be provided additionally for purposes of Directive 2005/44/EC on harmonised river information services (RIS) on inland waterways in the Community:

1.	National number

2.	Type of Craft in accordance with the Technical Specification for Electronic Ship Reporting in inland navigation

3.	Single or double hull according to ADN/ADNR

4.	Height according to Article 1.01 No. 75

5.	Gross tonnage (for maritime vessels)

6.	IMO Number (for maritime vessels)

7.	Call Sign (for maritime vessels)

8.	MMSI Number

9.	ATIS Code

10.	Type, Number, issuing authority and expiration date of other certificates"

___________

# Footnotes

/	Reservation made by the delegation of German.