## Slide 1
Enterprise and Industry Directorate General
European Commission
An Introduction to the New Vehicle Safety Regulation
Automotive Industry Unit
Enterprise and Industry Directorate-General
European Commission, Brussels
Informal Document No. WP.29-145-08
145th session, 24-27 June 2008, agenda item 6.

## Slide 2: Current situation
Over 50 base Directives covering vehicle safety and environmental issues
Plus over 100 amending Directives
Some Directives over 35 years old
Many duplicate UNECE Regulations

## Slide 3: Proposed Regulatory Structure
2 & 3
wheelers
Tractors
Framework
Dir. for Type
Approval
(all motor
vehicles incl.
HDV &
buses
)
Framework
Directive
Euro VI
Regulation
Impl
. Reg.
Euro VI
Regulation
Impl
. Reg.
Euro 5 & 6
Regulation
Impl
. Reg.
Euro 5 & 6
Regulation
Impl
. Reg.
Advanced
safety
features
and tyres
Impl
. Reg.
General
Vehicle Safety
Impl
. Reg.
Impl
. Reg.
MAC
Dir
.
Impl
. Reg.
Basic
Regulation
Impl
. Reg.
Basic
Regulation
Pedestrian
Protection
Impl
. Reg.
Pedestrian
Protection
Impl
. Reg.
Hydrogen
Impl
. Reg.
Hydrogen
Impl
. Reg.
Recyclability
Directive
Impl
. Reg.
Recyclability
Directive
Impl
. Reg.
Motor Vehicles (4 wheels++++)

## Slide 4: New Regulation on General Vehicle Safety
Proposal by the Commission in May 2008 will cover the following areas:
Regulatory Simplification
Advanced Vehicle Safety
New Requirements on Tyres.

## Slide 5: Regulatory Simplification
In line with the recommendations of the Cars 21 report
Will involve the repeal of 50 base Directives and over 100 amending Directives
To promote wider harmonisation, reference will be made to international regulations (UNECE) wherever possible.

## Slide 6: Advanced Vehicle Safety
Regulation will include the following technologies:
Electronic Stability Control (mandatory on all new vehicles)
Advanced Emergency Braking and Lane Departure Warning (mandatory initially on heavy duty vehicles)

## Slide 7: Electronic Stability Control
Notes: Physical testing is the ideal approval method, but can be expensive (and dangerous). Computer simulation can offer an alternative, but simulation methods need to be validates to ensure they are representitive.

## Slide 8: Electronic Stability Control
Technical Standards based on UNECE Regulation 13 or UNECE Regulation 13H (adopting the GTR requirements)
Will apply to new vehicle types from 2012
Will apply to all new cars from 2014 (later for some heavy vehicles)

## Slide 9: Heavy Vehicle Safety
Advanced Emergency Braking and Lane Departure Warning mandatory for new types of heavy duty vehicles from 2013, existing types from 2015
Optional on light duty vehicles
Technical standards to be agreed through UNECE route.

## Slide 10: Advanced Emergency Braking System
Radar or Laser systems detect if vehicle in front is too close
Brakes may be applied automatically if necessary

## Slide 11: Lane Departure Warning
System warns when driver is crossing road markings
Can also warn when there is a vehicle in the adjoining lane.

## Slide 12: Various Safety Features - Projected Savings for EU 27

## Slide 13: New Requirements on Tyres
Reduction in noise limits - by average of 3 db (A)
New limits on rolling resistance (for reduction of CO2)
Type Pressure Monitoring Systems to be mandatory (for CO2 reduction and safety)
New wet grip requirements

## Slide 14: Tyre noise proposals
Tyre noise standards originally introduce in 2001
Proposed new requirements propose further reductions of up to 4 dB(A)
Requirements will apply to new tyre types from 2012 and all new tyres from 2016

## Slide 15: Tyre noise proposals
Tyre class | Limit value db(A) |  | 
 | old | new | difference
C1A (≤ 185mm) | 72 | 70 | 2
C1B (185-215mm) | 73 | 71 | 2
C1C (215-245mm) | 74 | 71 | 3
C1D (245-275mm) | 75 | 72 | 3
C1E (> 275mm) | 76 | 74 | 2
C2 | 75 | 72 | 3
C2 traction | 77 | 73 | 4
C3 | 76 | 73 | 3
C3 traction | 78 | 75 | 3
Notes: The difference may be greater than that indicated in the final column since the category boundaries have changed slightly

## Slide 16: Tyre Rolling Resistance
New limits on rolling resistance introduced for the first time
Limits to apply in two stages, from 2012 and 2016
Technical test procedures to be included in UNECE Regulations
CO2 reduction Contribution of around 3.9 g/km for typical car

## Slide 17: Tyre Rolling Resistance
Tyre category | Max. Rolling Resistance (Kg/Tonne) | 
 | Stage 1 | Stage 2
C1 | 12 | 10.5
C2 | 10.5 | 9
C3 | 8 | 6.5
Notes: C1 = car tyres, C2 =light commercial tyres, C3 =heavy commercial tyres

## Slide 18: Tyre Pressure monitoring systems
TPMS alert the driver when the tyres are at a low pressure, affecting safety and fuel consumption
TPMS will be required on new car types from 2012 and existing types from 2014.
We intend to agree technical standards via the UNECE
CO2 reduction contribution of around 3.2 g/km for a typical car

## Slide 19: Tyre wet grip requirements
Introduced to ensure that safety standards are maintained
Based on the requirements in UNECE Regulation 117
Will apply to new car tyre types from 2012 and existing types from 2014
Will be extended to tyres for larger vehicles when standards have been finalised

## Slide 20
Enterprise and Industry Directorate General
European Commission
THANK YOU
for your attention
Automotive Industry Unit
Enterprise and Industry Directorate-General
European Commission