## Slide 1
AFS Main Beam (Driving Beam) Improvements
Presentation to WP29 - 146th Session
November 2008
Informal document No. WP.29-146-21 146th WP.29, 11-14 November 2008, agenda item 3.5.3.)

## Slide 2
Introduction
Technological progress now provides the possibility to produce an adaptive driving beam
GTB considers that such a system can be introduced into ECE regulations by amendments to Regulations Nos. 48 and 123.
GTB wishes to clarify the current provisions to avoid differing interpretations and consequential debate between the contracting parties regarding acceptability.

## Slide 3
2. 7. 28. " Adaptive front lighting system " (or "AFS") means a lighting device type-approved according to Regulation No. 123, providing beams with differing characteristics for automatic adaptation to varying conditions of use of the dipped-beam (passing beam) and, if it applies, the main-beam (driving-beam);
ECE R48

## Slide 4
TRANS-WP29-GRE-48-inf28e
Page 14

## Slide 5
AFS is available
related to dipped and main beam
applications currently focused on dipped beam
AFS dipped beam solves the problem of :
Bend situation
Adverse weather situation
Town situation
Motorway situation
Current AFS Situation

## Slide 6
The AFS dipped beam does not completely solve the problem of providing sufficient forward illumination.
It does not provide a complete answer to ensuring adequate visibility in the case of the random presence of other vehicles.
Current AFS Situation

## Slide 7
How to increase viewing distance without causing discomfort to other road users?
Problems to Overcome
Main beam as it exists today glares oncoming traffic in many situations and cannot be used.
The separation distance between vehicles means that the dipped beam will not provide sufficient forward illumination.
Drivers have a reluctance to operate the main beam and frequently select the dipped beam too early as recent research by LLAB shows.

## Slide 8
No Opposing Traffic
Full Main Beam Operated
Dipped Beam operated when opposing or preceding vehicles are present.
Frequently drivers operate the dipped beam earlier than necessary
Problems to Overcome

## Slide 9
The Adaptive Driving Beam
The following diagrams are intended to show the general principle of the automatic adaptation of the main beam to different traffic conditions.
They do not attempt to represent the actual beam distributions that can be achieved.
They only consider the case of a straight , flat road although the adaptive main beam responds to all road geometries.
The Solution

## Slide 10
No Opposing Traffic – Full Main Beam Operated
Main Beam light distribution adapted to avoid glare to oncoming vehicle
Opposing Traffic
The Solution

## Slide 11
No Preceding Traffic – Full Main Beam Operated
Main Beam light distribution adapted to avoid glare to preceding vehicle
Preceding Traffic
The Solution

## Slide 12
VIDEO 1

## Slide 13
VIDEO 2
VIDEO 2

## Slide 14
The system evaluates the road scene ahead of the vehicle and automatically adapts the light distribution according to the position of the preceding and oncoming traffic.
Normal dipped beam
The Solution
Increased Observation Distance
Adapted Main Beam
Preceding Vehicle Situation
Opposing Vehicle Situation

## Slide 15
This is a driver assistance system.
The driver remains responsible for deciding when it is appropriate to operate the main beam
The Safety Benefit

## Slide 16
Improvement of the observation distance to:
Reduce driver fatigue
Enhance the chances of detecting pedestrians and other hazards
Avoid discomfort to other drivers
The Safety Benefit

## Slide 17
GTB taskforce established
Prototype systems demonstrated to GRE in October 2008
Feedback from GRE experts
Proposals for amendments to ECE R48 and R123 expected to be approved by GTB in May 2009
Proposals expected to be introduced to GRE in October 2009
Introduction Programme

## Slide 18
Thank you for your attention
Your comments
will be greatly appreciated