## Slide 1: On-road Heavy-duty Engine Off-cycle Emissions gtr (OCE gtr) Status Report for AC.3
Report from the United States
24th Session of Executive Committee AC.3
13 November 2008
Informal document No. WP.29-146-23 146th WP.29, 11-14 November 2008, agenda item 17.6.)

## Slide 2: Overview
Background
Key Elements
Performance Requirements
Remaining Issues
Acknowledgements
Next Steps

## Slide 3: OCE gtr: Background
Informal group of technical experts under GRPE
  Regular meetings since 2002
    21 Plenary sessions
    6 Editorial sessions
June 2008
  The gtr was submitted as an Informal Document to GRPE
    (ECE-TRANS-WP29-GRPE-56-inf14e)

## Slide 4: OCE gtr: Key Elements
The OCE gtr complements the WHDC gtr
  On-cycle control
  Off-cycle control
World-harmonized Not-to-Exceed (WNTE) “Control Area”
  Large operating zone within which the WNTE emission limits apply
  WNTE emission limits are stated as a function of the WHDC emission limits
    WNTE emission limits are slightly higher than the corresponding WHDC emission limits
Statement of OCE Compliance
  The manufacturer must provide a statement that attests to compliance with the provisions of the OCE gtr
OCE Laboratory Test Procedure
  An optional laboratory test procedure is included
  Contracting Parties may choose to require testing to verify OCE compliance prior to type approval
The gtr does not include specifications for in-use vehicle testing or on-vehicle emission measurement equipment
  But, the WNTE was developed to allow for testing of compliance during in-use, on the road operation of the engine
  Individual countries and regional authorities may specify their own in-use testing requirements to enforce WNTE

## Slide 5: OCE gtr: Performance Requirements
Emission strategies shall be designed to enable compliance with the gtr
  A “base emission strategy” shall not discriminate between test cycle operation and other operation and provide lesser emission control during operation not included on the test cycle
  An “auxiliary emission strategy” shall not reduce emission control unless
    It operates on test cycles, including the WNTE
    It provides protection to the engine
    It operates only on starting or warming up
    It trades control of one pollutant for another while maintaining acceptable emission control
An emission strategy that fails to meet the performance requirements is a “Defeat Strategy”
  Defeat strategies are prohibited by the gtr

## Slide 6: OCE gtr: Remaining Issues
There remain no outstanding issues with the current gtr
The absence of in-use testing procedures may represent an opportunity for future gtr action.

## Slide 7: OCE gtr: Acknowledgements
As sponsoring country, the United States wishes to thank all those that have contributed to development of the OCE gtr.
Particular thanks to the following for continued support and hosting of meetings
  European Commission
  The Netherlands
  The German government
  The Japanese government and JASIC
  The UK government
  Environment Canada
  Engine Manufacturers Association

## Slide 8: OCE gtr: Acknowledgements
The United States wishes to recognize the valuable contributions made by representatives of the following organisations
  Environment Canada
  European Commission DG Enterprise
  Joint Research Centre
  Federal Ministry of Transport, Germany
  Federal Environmental Agency, Germany
  RWTUEV Fahrzeug GmbH, Institute for Vehicle Technology, Germany
  TÜV NORD Straßenverkehr GmbH, Germany
  Institute for Transport Sciences, Hungary
  International Organization of Motor Vehicle Manufacturers
  International Organization for Standardization
  Ministry of Land, Infrastructure and Transport, Japan
  Ministry of the Environment, Japan
  National Traffic Safety and Environment Laboratory, Japan
  Japan Automobile Research Institute
  Japan Automobile Standards Internationalization Center
  Japan Automobile Manufacturers Association
  Netherlands Ministry of the Environment
  Korea Automobile Testing & Research Institute
  Swedish Environmental Protection Agency
  Department for Transport, United Kingdom
  Engine Manufacturers Association

## Slide 9: OCE gtr: Next Steps
January 2009
  The OCE gtr will be submitted on 15 January to the 57th GRPE
March 2009
  The US is optimistic that the OCE gtr will be submitted as an Informal Document to the 25th AC.3