## Slide 1: gtr for Tyres: Update
November 2008
Transmitted by the representative of ERTRO
Informal document No. WP.29-146-29
(146th WP.29, 11 - 14 November 2008,
agenda item 17.9.)

## Slide 2: The GTR objective (3y working programme)
<number>

## Slide 3
Road map for TYRE GTR – Technical Programme - PC tyres
Step 1:
Step 2:
Step 3:
Step 4:
2007 1Q
2007 2Q
2007 3Q
2007 4Q
2008 1Q
2008 2Q
2008 3Q
Feb 2008
GRRF
25-28Sept 2007
GRRF
Feb 2007
GRRF
Sept 2008
GRRF
2007/1/15
ver3
MARKING
PLUNGER ENG &
BEAD UNSEATING
TYRE ENDURANCE
LOW PRESSURE
Preliminar DRAFT
Final DRAF
HIGH SPEED
DIMENTION
Ad-hoc meeting
2008 4Q
2009 1Q

## Slide 4: Scope – GRRF Chairman’s compromise
<number>
Harmonization of radial PC tyres (UNECE Reg30 and USA FMVSS139)
Include C type tyres (UNECE Reg.54) and LT tyres, exactly as in the present USA FMVSS 139 as Contracting Party option
Covers tyres fitted to light vehicles of max mass 4536kg or 10.000 pounds, exactly as in the present USA FMVSS 139

## Slide 5: Radial PC tyres - Harmonisation
<number>
Hamonisation established for:
  The physical dimensions test metho
  The high speed test between UNECE R30 and USA FMVSS 139
All others tests are unique:
  From USA FMVSS139: endurance/low pressure - breaking energy - bead unseating
  From UNECE R117: noise and wet grip

## Slide 6: C and LT tyres - status
<number>
Two different High Speed tests and two different Endurance tests need to be harmonized (from UNECE R54 and USA FMVSS139)
Generally the test requirements (tyre’s loads, inflations and/or speeds) are adjusted based on the tyre technical parameters
Difficult issues:
For C tyres, the UNECE Reg.54 is referring to Speed Symbol and Load Index (e.g. 121 = 1450kg) for fixing testing conditions
For LT tyres, the USA FMVSS 139 is referring to Load Range (letter C to E) for fixing testing conditions

## Slide 7: C and LT tyres - status
<number>
Load Index and Load Range : there is NO correlation between them and therefore they are NOT harmonized parameters
An ad-hoc Tyre Industry project will be developed to harmonise the Industry Standards (Load Range versus Load Index)
Consequentially will be developed the harmonisation project of tests from UNECE R54 and FMVSS 139
Another 3 years of work is foreseen, with major resources to be dedicated to the tests’ harmonisation (high speed and endurance)
Working plan will be presented at next GRRF Feb.09

## Slide 8: Scope
<number>
This Regulation covers new radial pneumatic tyres designed [primarily] for vehicles in category 1-1, 1-2 and 2*, all with a mass limit of 4.536 kg.
*As defined in Special Resolution Number 1.
This regulation will include harmonized requirements for new radial pneumatic passenger car tyres.
The regulation will also include non-harmonized provisions for light truck / commercial type tyres as a first step towards full harmonization. The time table for completing the harmonization of requirements for all tyres covered by this gtr is [three] years from [?]

## Slide 9: Marking
<number>
The wording “Tubeless” must remain
The wording “Radial” will disappear
UNECE Type Approval marking and USA DOT Tyre Identification markings will be combined in a unique global tyre type identification marking sequence
GLOBAL marking (logotype) to identify a tyre in compliance to the gtr provisions is also proposed – need for further assessment

## Slide 10: GTR framework proposal – 1° step
<number>
Current UNECE Reg.s
PC tyres
  R30, R117
    Physical dimensions
    High Speed
    Noise
    Wet grip
C tyres
  R54, R117
    Physical dimensions
    High Speed
    Endurance
    Noise
In the gtr
PC and C + LT tyres
  Harm. Physical dimensions
  Harm. High Speed (PC)
  High Speed + Endurance (C – UNECE R54)
  High Speed + Endurance (LT – USA FMVSS139)
  Endurance (PC)
  Low Pressure Endurance
  Noise
  Wet grip (PC)
  Breaking Energy
  Bead Unseating

## Slide 11: Remaining Technical Tasks
<number>
Include C and LT tyres
  Define how to do it, taking into account Load Range and Load Index differences
  Harmonise the tests (High Speed + Endurance)
    No existing database
    Considerable resources to be allocated
    Estimated to take 3 years (to be confirmed)

## Slide 12: GTR framework proposal – 2° step
<number>
Current UNECE Reg.s
PC tyres
  R30, R117
    Physical dimensions
    High Speed
    Noise
    Wet grip
C tyres
  R54, R117
    Physical dimensions
    High Speed
    Endurance
    Noise
In the gtr
PC and C + LT tyres
  Harm. Physical dimensions
  Harm. High Speed (PC)
  Harm. High Speed (C + LT)
  Harm. Endurance (C+ LT)
  Endurance (PC)
  Low Pressure Endurance
  Noise
  Wet grip (PC)
  Breaking Energy
  Bead Unseating

## Slide 13: Thank you for your attention.
<number>