## Slide 1
        Informal document No.GRB-47-4
        (47th GRB, 19-21 February 2008
        Agenda item 3 (a)
CLEPA presentations supporting justifications of informal documents GRB-47-2 and GRB-47-3, proposing amendments to R51 and R59.

## Slide 2
1. Absorbing fibrous materials
2. Noise reduction systems with variable geometry
3. New driving-by test of R51 in R59
4. Particularities for automatic transmission
5. Static noise test
Content

## Slide 3
1. Presentation on absorbing fibrous materials.
Introduction of the concept of component design family. Influence of the various silencer characteristics on the fibrous material life expectancy.

## Slide 4: Current legislation
Exhaust systems containing fibrous materials
Wool retention should be demonstrated by:
  Continuous road operation for 10.000 km
  Conditioning on a engine bench
  Conditioning by pulsation (2500 cycles)

## Slide 5
Continuous road operation for 10.000 km
    The vehicle should be representative of the type in respect of which type approval is requested
Conditioning on a engine bench / Conditioning by pulsation (2500 cycles)
    The engine should be of at least the same cylinder capacity and rated power maximum.
Current legislation

## Slide 6: Test data : Conditioning by pulsation
Gas temperature about 540°C

## Slide 7: Temperature resistance fibrous materials
Fibrous materials used in exhaust systems may have different temperature resistance characteristics :
Type A | 570°C
Type B | 650°C
Type C | 650°C
Type D | 780°C
Type E | 725°C
Type F | 650°C
Type G | 600°C
Limit of use

## Slide 8: Conditioning by pulsation
The result of the test may depend on the type of the fibers used (e.g. basalt wool, E type wool, Biosil wool, etc)

## Slide 9: Conditioning by pulsation
Further parameters which could influence the result of the test :
  Binder material specifications
  Average fiber dimensions (thickness, length)
  Minimum bulk material packing density (kg/m³)

## Slide 10: Pulsation resistance fibrous materials
The exhaust gasses in contact with the fibrous material have or have not a net gas flow through this material
  Straight-through flow silencer
  Silencer with flow through the fibrous material

## Slide 11: Conditioning by pulsation
The presence of a net gas flow through the fibrous materials may influence the test result.

## Slide 12: Proposal
Definition of the concept of a «component design family» based on the above mentioned relevant design characteristics.
        °°°°°°°°°°°°°°°°°°°°°

## Slide 13
2. Presentation on the concept of
« noise reduction systems with variable geometry »
with regards to the implications of ASEP within R59. This includes data on the potential effects of valves in exhaust systems.

## Slide 14: Valves in exhaust systems : general overview of possible acoustical efficiency improvements
Flow noise
Engine noise
Back pressure
Passive exhaust systems
Exhaust systems with a valve
Passive exhaust systems
Exhaust systems with a valve

## Slide 15: Example of a silencer equiped with an auto-actuated valve
Valve closed at low exhaust gas volume flow
valve opens automatically at high exhaust gas volume flow

## Slide 16: Example 1: FLOW NOISE REDUCTION (engine noise and backpressure unchanged)
6 dB
Valve opens here
Passive exhaust system
Exhaust system with a valve

## Slide 17: Example 2: ENGINE NOISE REDUCTION (flow noise and backpressure unchanged)
Valve opens here
Passive exhaust system
Exhaust system with a valve

## Slide 18: Example of an exhaust system equipped with an auto-actuated valve and with BY-PASS OF THE REAR SILENCER
Valve
by-passing the rear silencer
at high rpm’s
Catalytic
converters
Front silencer
Rear silencer

## Slide 19: View on the measured prototype exhaust system
Valve
by-passing the rear silencer
at high rpm’s
Catalytic
converters
Front silencer
Rear silencer

## Slide 20: Test results
by pass closed
by pass open
Switch point

## Slide 21: Test results
Campbell diagram: colours indicate sound level
frequency [Hz]
Engine speed [rpm]
by pass closed by pass open
frequency [Hz]
dB(A)
70
20
dB(A)
70
20
6000
1000
0 5000
0 5000

## Slide 22
Conclusions
The examples clearly show that the technology of noise reduction systems with a variable geometry may have a very positive contribution to exhaust noise abatement.
But, by inversing the valve commands in the example which was shown, a very negative result could also be achieved.
CLEPA proposes that for replacement exhaust systems, containing components with variable geometry, the technical service may request to verify the acoustic noise reduction functionality by performing the ASEP tests.

## Slide 23
Conclusions
A large number of passive replacement exhaust systems (fixed geometry) are currently under test. So far all test results have shown remarkable compliance with the ASEP requirements. These results will be shown during the meeting. The testing program continues and CLEPA will report on the conclusions in the ASEP working group.
        °°°°°°°°°°°°°°°

## Slide 24
3. Recall of the presentation given by CLEPA on the application in R59 of the new driving by test method of R51.

## Slide 25: Conditions of measurement
Tyres
  The use of special noisy tyres is not allowed in the comparison test because of the potential acoustical masking effect on the exhaust noise. Only tyres in line with the legal requirements for in traffic use are acceptable for the comparison test.
Environmental temperature
  No limitation on the minimum environmental temperature has been set. The influence of temperature on exhaust noise contribution being minimal.

## Slide 26: Conditions of measurement
Measurement accuracy
  The current R59 regulation results in some practical inconsistensies and confusions with regard to the measurement accuracy and rounding off practice to the nearest integer dB(A) value.
  CLEPA proposes a simplified and uniform rule, taking into account the 1 dB(A) measurement inaccuracy.
Test vehicle acceptability
  A vehicle is acceptable as a test vehicle if it satifies the requirements for COP. This rule will bring R59 in line with directive EC 70/157.

## Slide 27: Conclusion
The new driving-by test method R51.03 and the current test method R51.02 show practically identical relevance when applied to the comparison test between OE and replacement parts in R59.
        °°°°°°°°°°°°°°°°°°°°°°°°°°°°°

## Slide 28
4. Presentation about the particularities of automatic transmission for the drive-by test in R59.

## Slide 29: Automatic transmission
In Par. 3.1.2.1.4.2 of R51 concerning vehicles with automatic transmission tested with non-locked gear ratios, it is indicated that it is permitted for the car manufacturers to establish and use electronic and/or mechanical devices to prevent a downshift. This is unpractical for replacement parts approval tests.
The following results show that a comparison test allowing a downshift gives similar comparison results as a test without downshift.

## Slide 30
5. Justification for the CLEPA amendment proposal of the static noise test procedure in R51/R59.

## Slide 31: Static noise test
The following graph illustrates the poor reproducebility of the current static noise test. This results in problems with in use compliance testing. A slightly modified testing procedure will prevent this inconsistency.

## Slide 32: STATIC NOISE OEM TYPE APPROVAL TESTS