## Slide 1: Some recent experiences with Tyre noise measurements
Prepared for GRB Feb 2008
Issued by the Netherlands
Informal document No. GRB-47-9
(47th GRB, 19-21 February 2008
Agenda item 8.)
Transmitted by Netherlands

## Slide 2: Results from a session on 26 C1 tyres

## Slide 3: Results 2005 relatively high compared to earlier results

## Slide 4: Change of ISO test track over time
ISO 10844 requires texture > 0,4 mm
Should be checked every year
No requirement on maximum allowable texture
Reconstruction of test track

## Slide 5: Effect of reconstruction of test track on the noise of these 26 C1 tyres
Up to 4 dB(A) reduction due to reconstruction of ISO test track

## Slide 6: Discussion and conclusion
Tyre noise levels depend very much on the actual status of the ISO test track
Currently ISO 10844 has no upper boundary on texture nor on a maximum (acoustical) lifetime
Due to wear of the test track the texture may increase significantly
This may result in a spread in noise levels up to 4 dB(A) depending on the tyre and track
Tighter requirements on ISO 10844 are necessary; including an upper boundary on texture. An ISO committee has nearly finished an update including such requirements.
The future specification of ISO 10844 has significant effect on future noise levels (and thus on the possible limits)