## Slide 1: ECE R41 revision
Outline of main modules with
crossreference to draft amending text
Presentation by Data Expert Group to R41WG
19 February 2008
Informal document No.GRB-47-11
(47th GRB, 19-21 February 2008
Agenda item 2)
Transmitted by the expert from IMMA

## Slide 2: Actions since 9/R41WG
DEG continued discussions; still some ASEP issues to check
DEG documents have been sent to UN for uploading on ECE website; origin of motorcycles added to noise level database
01-R41WG-08 (draft amendment) has been updated (see Informal Document No)
This presentation shows how the amendment is linked to past decisions of R41WG

## Slide 3: Modular structure – “the package”

## Slide 4: TA test
Problem
  No required acceleration and potential perverse consequences (longer gearing in test = lower rpm = lower noise but also lower gears used in real life = higher rpm = higher noise)
  No relationship between test conditions and actual use conditions, meaning reduced effectiveness of noise reduction measures in real life
New TA test

## Slide 5: TA test
Proposed solution / benefits
  Essentially same method as for cars but with higher target accelerations and without acceleration limit
    Prescribed target acceleration rate related to vehicle acceleration capability – level playing field
    Accurate simulation of noise source distribution (intake, exhaust, engine/gearbox, …) in relation to most relevant motorcycle operation – effective noise reduction measures
    Independent of vehicle design to allow future propulsion technologies to be tested – vehicle speed and acceleration instead of engine speed
Remaining tasks
  Limits
Where in 01-R41WG-08
  Annex 3 section 1 (test method) + Annex 6 (limits)
New TA test

## Slide 6: ASEP
Problem
  Base TA test provides only “snapshot” of noise emission behaviour
  Noise levels below and above TA test conditions may increase inappropriately
ASEP

## Slide 7: ASEP
Proposed solution / benefits
  Definition of operating range below and above TA test conditions within which noise emission should not deviate significantly from what one would expect from the base TA test results – control beyond TA “snapshot”
  Manufacturer declaration of conformity with possibility for TA authority to perform checks – limited testing burden at time of TA
Remaining tasks
  Limits (slopes and tolerance)
Where in 01-R41WG-08
  Paragraph 6 and Annex 7
ASEP

## Slide 8: Roadside enforcement
Problem
  Stationary noise test with reference noise level by itself is only able to capture crude illegal systems and rough manipulations
Proposed solution / benefits
  Maximum WOT drive-by test result for lowest gear from TA test made available as additional reference data for roadside enforcement – better enforcement capability with drive-by noise test as additional tool next to stationary noise test
Remaining tasks
  Alignment with ISO 5130 (stationary noise test)
Where in 01-R41WG-08
  Annex 3 section 3
Pass-by test for roadside enforcement

## Slide 9: Anti-tampering
Problem
  No prescriptions related to easily modifiable and manually adjustable multi-mode mufflers
Proposed solution
  Legal language to prevent approval of mufflers designed for tampering
  Performance requirements for multi-mode mufflers (test all modes)
Remaining tasks
  /
Where in 01-R41WG-08
  Paragraph 6
Anti-tampering / contructional requirements

## Slide 10: 01-R41WG-08 structure
SCOPE ............................................... 3
DEFINITIONS, TERMS AND SYMBOLS ...................... 3
APPLICATION FOR APPROVAL ............................ 7
MARKINGS ............................................ 7
APPROVAL ............................................ 7
SPECIFICATIONS ...................................... 10 TA test ASEP Anti-tampering
7. MODIFICATION AND EXTENSION OF THE APPROVAL OF THE MOTORCYCLE
TYPE OR OF THE TYPE OF EXHAUST OR SILENCING SYSTEM(S). 11
CONFORMITY OF PRODUCTION ............................ 12
PENALTIES FOR NON-CONFORMITY OF PRODUCTION .......... 12
PRODUCTION DEFINITELY DISCONTINUED .................. 13
NAMES AND ADDRESSES OF TECHNICAL SERVICES
RESPONSIBLE FOR CONDUCTING APPROVAL TESTS,
AND OF ADMINISTRATIVE DEPARTMENTS .................. 13
TRANSITIONAL PROVISIONS ............................. 13
ANNEXES
Annex 1 - Approval communication
Annex 2 - Arrangements of approval marks
Annex 3 - Methods and instruments for measuring the noise made by motor cycles TA test Pass-by enforcement test
Annex 4 - Test track specifications
Annex 5 - Exhaust system (silencer)
Annex 6 - Maximum limits of sound level (new motor cycles) TA test
Annex 7 - Additional sound emission provisions (new motor cycles and new exhaust or silencing systems) ASEP

## Slide 11: Proposed next steps
Initial discussion at 10/R41WG
Reporting to 47/GRB
R41WG/GRB member comments to Italy by 31 May
Consideration of comments by 11/R41WG on [2/3] July
12/R41WG on 1 September (PM)
Discussion at 48/GRB (amended text and limit values)