## Slide 1: some observations on the base of the ASEP dBase
Prepared by the Netherlands
ASEP meeting jan 2008 USA

## Slide 2: Rough comparison of proposals
Both the FD and UBA proposal are based on vehicle speed and engine speed. The NL proposal is based on vehicle speed and vehicle acceleration.
UBA and FD limit curves look similar
  UBA is often, but not always, the most stringent
For majority of vehicles NL limit is quite in line with UBA and FD, but for some vehicles significantly different
  NL tends to be more liberal for vehicles with high acceleration and tighter for vehicles with slow acceleration
  NL tends to be more liberal in high gear ratios and tighter in low gear ratios
The limit curves of al three proposals can be tuned in order to (dis)approve certain vehicle behavior

## Slide 3: Rough comparison of proposals
Al three proposals are proven to be practicably executable
Remaining issues
  NL sometimes shows some scatter in limit values; especially in cases of automatic gearboxes which are shifting between AA’ and BB’
  FD and UBA contain a subtraction of tyre noise, which can cause big uncertainty in case of dominant tyre noise contribution
  FD and UBA require an engine speed; some vehicles may not have an engine speed and can not be tested
Practical solution can be found for these issues
The principal choice is:
  acceleration
    design independent and in line with annex 3 philosophy
  engine speed
    reflects natural understanding of noise generation
    often more stable to measure
    applicable for most of the current technologies
    only not applicable for types without engine speed like plug in hybrid (are such vehicles a concern for ASEP?)

## Slide 4: Looking in detail to all sheets
The next slides show some detailed information gathered from the dBase

## Slide 5: In many cases everything is “as expected”
Noise curve is linear
Maximum expected noise level around 80 dB(A) (diesel) to 85 dB(A) (petrol)
Limits of NL, FD and UBA are close together
Measured noise is well below limit

## Slide 6: In some cases not everything is “as expected”
Noise curve is not linear
Maximum expected noise level far beyond 80 dB(A) (120 dB(A)??)
Limits of NL, FD and UBA are more than 10 dB apart
Measured noise is approved by one method, disapproved by the second and partly approved by the third (only within the boundary conditions)

## Slide 7: Statistics on “approvals”
Vehicles in dBase:
  124 different vehicles
  139 records; 15 are in twice with different analysis methods
Limit now (R51.02)
  44 exceed pure limit
  24 exceed limit by more than 1,9 dB(A)
If limit R51.03 annex 3 is 72/73/75
  24 exceed pure limit
  17 exceed limit by more than 0,4 dB(A)
ASEP with these settings of the limit values
  33 exceed NL limit
  17 exceed FD limit
  35 exceed UBA limit
  13 have an obvious jump or non linearity in the noise curve

## Slide 8: Vehicles of concern 1
Criteria:
  Exceed limit R51.02 by more than 1,9 dB(A)
  Pass limit R51.03 annex 3 + 0,4 dB(A)
7 out of 124 vehicles in dBase fulfill these criteria
Non of these vehicles are disapproved unanimously by all ASEP proposals
  NL: 2
  FD: 2
  UBA: 6
See examples in later sheets

## Slide 9: Vehicles of concern 2
Criteria:
  Disapproved by all ASEP proposals (for this criterion the ASEP boundary conditions have not been taken into account)
  Fulfills R51.02 limit +1,9
  Fulfills annex 3 limit + 0.4
4 vehicles fulfill these requirements
Those 4 shows all significant jumps or non linearity's
See examples in later sheets

## Slide 10: Vehicles with obvious non linearity's
13 vehicles
See examples in later sheets

## Slide 11: All measured data points of all vehicles
Are there data points obviously beyond “normal behavior”, which should be detected by ASAP?

## Slide 12: Vehicles of concern 1
R51.02 = 77,1 Annex 3 = 73,3
Vehicle is approved by all ASEP proposals

## Slide 13: Vehicles of concern 1
R51.02 = 77,0 Annex 3 = 72,4
Vehicle is disapproved in ASEP only by UBA prop

## Slide 14: Vehicles of concern 1
R51.02 = 79,5; Annex 3 = 70,4
Vehicle is disapproved in ASEP only by FD proposal
NB. Is limit for engine speed high enough?

## Slide 15: Vehicles of concern 1
R51.02 = 76,0 Annex 3 = 71,4
Vehicle is approved according to all ASEP proposals

## Slide 16: Vehicles of concern 1
R51.02 = 76,7 Annex 3 = 71,4
Vehicle is generally approved according to ASEP
  Note: NL spread in limit values

## Slide 17: Vehicles of concern 1
R51.02 = 81,1 Annex 3 = 71,7
Vehicle is disapproved in ASEP only according to UBA prop

## Slide 18: Vehicles of concern 1
R51.02 = 78,1 Annex 3 = 73,5
Vehicle is disapproved in ASEP only by UBA prop

## Slide 20: Vehicles of concern 2
R51.02 = 75,2 Annex 3 = 71,9

## Slide 21: Vehicles of concern 2
R51.02 = 74,7 Annex 3 = 72,8

## Slide 22: Vehicles of concern 2
R51.02 = 70,0 Annex 3 = 70,3

## Slide 23: Vehicles of concern 2
R51.02 = 76,0 Annex 3 = 70,1

## Slide 25: Vehicles with non linear behavior

## Slide 26: Vehicles with non linear behavior

## Slide 27: Vehicles with non linear behavior

## Slide 28: Vehicles with non linear behavior

## Slide 29: Vehicles with non linear behavior

## Slide 31: Question to the group:
The NL proposal was intended to be design independent: the vehicle is seen as a black box moving with a vehicle speed and a vehicle acceleration. What is causing its propulsion is not important.
Could engine speed based ASEP proposals be design restrictive?

## Slide 32: Exercise: change PMR from 67 to 100 kW/t
Basic vehicle:
  2 liter engine 100 kW 6000 rpm
  Weight: 1500 kW
Options to change
  Increase capacity to 3 liter
  Add turbo
  Increase rated speed to 9000 rpm
  Hybrid: Add electric engine
  Reduce weight to 1000 kg
  Other?
How will this effect noise values?
  In annex 3
  In annex 10
  In traffic