## Slide 1: Reproducibility of NL ASEP proposal
Prepared by the Netherlands
ASEP meeting jan 2008 USA

## Slide 2: Spread in limit values NL approach automatic gearbox
Example 2: 6 dB spread in NL limit value

## Slide 3: Spread in limit values NL approach manual gearbox
Example 1: 2,5 dB spread in NL limit value

## Slide 4: Reason for spread in NL limit value:
LimitNL,ASEP = Limitannex 3 +
4*(aASEP test –aurban,annex 3) +
0,3*(vBB,ASEP test - 50)
spread in measured acceleration values (aASEP test) causes spread in limit values

## Slide 5: Accelerations as we expected
  Nearly independent from engine speed
  PP-BB max 10% higher than AA-BB
  Good reproducibility

## Slide 6: Accelerations as we see them
AT; delay and shifting behind PP
MT: PP-BB lower than AA-BB
MT: spread PP-BB 10%, spread AA-BB 30%
MT: AA-BB 40% lower than PP-BB

## Slide 7: Why is there spread in acceleration?
Potential reasons:
No flat torque curve
Acceleration delay in track (esp Turbo and automatics)
Shifting of automatic gearboxes
Too little pre-acceleration
Too late depressing of accelerator
Too early releasing of accelerator
Errors in alignment of lines AA’, PP’ and BB’
  Place of light barriers
  Length of vehicle

## Slide 8: Possibilities to improve reproducibility of acceleration measurements
Always take aPP-BB instead of aAA-BB
Prescribe overdoses pre-acceleration to be sure that the vehicle indeed uses its full acceleration potential (and check)
Set boundaries to difference aPP-BB - aAA-BB