## Slide 1: SWOT Analysis of Different Approaches for an Environmentally Friendly Vehicle (EFV) OICA Presentation to EFV Informal Group 6 June 2008
Working paper No. EFV-01-02
(GRPE Informal Group on EFV,
First Meeting, 6 June 2008.)

## Slide 2: Investigated concepts
  Life-Cycle Assessment (LCA) of vehicles
  Well-to-Wheel Analysis
  CO2 Regulation Reference Approach
  Environmental Rankings
  Green Vehicle Certification

## Slide 3
Product Life-Cycle
Eutrophication
Potential
Global warming
Potential
Summer smog
Potential
Acidification
Potential
CO2
∑
CH4
∑
NOX
∑
……
∑
VOC
∑
NOX
CO2
CH4
CO2
VOC
CO2
NOX
CO2
CO2
NOX
Life-Cycle Inventory
Impact Assessment
Full LCA on Passenger Vehicles
Energetic and mineral resources

## Slide 4: Requirements for a LCA according to ISO 14040/44
      Comparative Assertions disclosed to the public:
        Weighting of different environmental aspects/categories or single scores shall not be applied
        Critical Review by independent 3rd party

## Slide 5: Full LCA on Passenger Vehicles
EXECUTING A FULL VEHICLE LCA:
  enables to evaluate cars regarding different environmental aspects
  is standardized by ISO 14040/14044 and therefore international accepted
LCA SUPPORTS SUSTAINABLE PRODUCT DEVELOPMENT BY:
  comparing alternative concepts regarding ecological aspects
  identifying connections between causes and consequences within the product lifecycle
  supporting concept decisions by statements on ecological advantages and disadvantages according to economical and technological aspects
LCA STUDIES OF DIFFERENT PRACTITIONERS VARY IN RELEVANT CRITERIAS:
  goal and scope
  system boundaries
  cut off criteria
  allocation methods
  basic data sources
  LCA software tools and data collection / sorting software

## Slide 6: LCA on passenger vehicles - SWOT
Strength
  LCA can be a suitable method within product development to support environmentally friendly product design if simplified for internal purposes
  Internationally accepted method (ISO 14040/44)
  Integration of all actors along the value chain into the environmental discussion possible (Supply-Chain, OEM, Mineral Oil Industry, Costumer)
Weakness
  No EFV definition in itself / delivers only data that can be used for EFV definitions
  High effort for executing a LCA (time, costs, data). LCAs for passenger vehicles require several simplifications / data estimates
  Comparability given only within one study, i.e. not suitable for EFV definition
  Too complex information input and output
Opportunity
  Third party certification possible
Threat
  Complex LCA information may lead to confusion and mis-leading conclusions by customers and regulators
  Aggregation of LCA results to a single-score done although not allowed according to ISO14040 (no scientific basis for single-score/biased weighting)
  Due to complexity work may concentrate more on LCA method details than on product improvements.

## Slide 7: Well-to-Wheel Analysis - Concept
  Life-Cycle Perspective is considered only as use-phase + fuel chain, without vehicle production and EoL phase
  Only Greenhouse Gas Emissions and Energy demand is calculated
  Other environmental aspects such as HC/NOx/CO (Summer smog / Acidification,…) were not addressed
  The approach is well known and widely accepted
  The EUCAR-CONCAWE-JRC study is limited to a generic vehicle

## Slide 8: Well-to-Wheel Analysis - SWOT
Strength
  Widely accepted approach
Weakness
  No EFV definition in itself / delivers only data that can be used for EFV definitions.
  High effort for execution / update.
  Environmental discussion is reduced to one single parameter (Energy/GHG).
  Well-to-wheel analysis deal with different fuel options instead of EFVs.
Opportunity
  Other environmental aspects such as emissions can be integrated.
  Streamlined Life-cycle Approach (only fuel chain is additionally considered).
  Third party certification possible.
Threat
  High additional expenditure for the inclusion of other environmental aspects.

## Slide 9: CO2 Regulation Reference Approach - Concept
Determine CO2 emissions (g CO2/km tailpipe) of the individual vehicle
Calculate the distance to legal target in the region
Reflect any CO2 credits linked to the vehicle
Note: relative or absolute approaches possible
An EFV could be a vehicle having lower CO2 emissions than required
If necessary additional criteria could be added that are important in the region (e.g. emission standard)
40
60
80
100
120
140
160
180
200
220
500
1000
1500
2000
2500
3000
Vehicle mass kg (EU) (US: footprint, in other regions other parameters)
target g CO2 / km
light duty passenger vehicles
1
2
vehicle with CO2 below target = EFV
vehicle with CO2 above target

## Slide 10: CO2 Regulation Reference Approach - SWOT
Strength
  Adoptable to regional conditions (regulatory targets different)
  Easy to establish
  Relating to existing regulation i.e. harmonized with and supporting legislation
Weakness
  EFV definition different in various regions.
  No EFV definition if no regulation exist.
  Environmental discussion is reduced to one aspect.
  Missing life cycle perspective.
Opportunity
  WTW CO2-values and other items (such as emissions) or approaches can be easily included
Threat
  Long debates how much EFVs need to be better than target line by x g/km

## Slide 11: ECO Ranking (Consumer associations) - Concept
Determine CO2 emissions, noise and emission standard of the individual vehicle
fixed allocation of emission standards to “environmental impact categories” (approved by IFEU, UBA)
fixed weighting of CO2, noise and “impact categories”
Calculate eco points
An EFV is a vehicle having highest score
per category or overall Top Ten

## Slide 12
ECO Ranking (Consumer associations) - Concept
Determine vehicle specific and manufacturer specific data:
vehicle: - fuel consumption on road and
NEFZ - emission standards, noise
- equipment: start/stop, CO2 calculator, indoor emissions
manufacturer/production: energy per vehicle, painting, use of recycled mater., natural fibres, elv and environmental system, ...
fixed weighting of all categories
Environmental certificate only for best in class (90 from 100 pts).

## Slide 13: ECO Ranking (Consumer associations) - SWOT
Strength
  Easy to establish and third party verification
  Top Ten results / Labeling
  Methods with more than CO2 and emission standards
Weakness
  Multi Criteria / impact category approach with questionable “scientific” approved weighting.
  Criteria with less benefit for environment are included, but no WTW / lifecycle-data.
  Biased methods.
Opportunity
  WTW and other items can be easily included
Threat
  Due to non-stable and non-scientific method changing criteria and weightings over time  confuse customer, moving development targets.

## Slide 14: Green Vehicle certification (China) - Concept
  There are at least four „Green Vehicle“ certifications in China by different organizations
  The “Green Vehicle“ certificates are based on a set of requirements
  All four certificates include the evaluation factors “Emission control (OBD)“ and “Fuel consumption“
  Additionally they include at least one of the following criteria:
    CO2 emission
    Curb mass
    Exterior and interior noise
    inner vehicle air quality
    ELV RRR rates, Banned materials, EMI, non-CFC materials in AC system, non-asbestos material, max. vehicle speed, acceleration and climbing ability
  Often References to GB / GB/Ts given
  Implementation of two “Green Vehicle“ certifications in China (2005 and 2006)

## Slide 15: Green Vehicle certification (China) - SWOT
Strength
  Transparent, understandable, easy to establish
  Mainly criteria that are anyhow in the development focus, legal base
  Relating to existing regulation i.e. harmonized with and supporting legislation
Weakness
  All depending on criteria selection, limit values
  Adoption to regional conditions  further market fragmentation
  Development efforts on issues out of customer focus
Opportunity
  If EFV definition can be globally agreed on the basis of legislation this could foster a global harmonization of legislations
Threat
  Different schemes create market fragmentation

## Slide 16: CONCLUSIONS & NEXT STEPS
EFV definition needs to investigate the complete variety of possible approaches (only few examples presented here).
So far no approach identified as useful or acceptable.
Further work is required to analyze approaches (additional approaches, deepening of SWOT).
However, first fundamental questions need to be clarified to conduct a SWOT (EFV definition for what purpose (tax, GPP, development targets, …?), target audience (engineers, fleet customer, private customer, etc.)) as this determines strengths and weaknesses (customer clinics and regional studies might be required).
It is recommended to first agree on the questions and then to develop a working plan.

## Slide 17
Thank you for your attention