## Slide 1: Well-to-Wheels analysis of future automotive fuels and powertrains in the European context
A joint study by EUCAR / JRC / CONCAWE
EFV GENEVA
Friday 06/06/2008
WTW
Version 2c
Working paper No. EFV-01-08
(GRPE Informal Group on EFV,
1st Meeting, 6 June 2008)
Notes: 05/25/00
1
CONCAWE
EUCAR = European Council for Automotive R&D

## Slide 2: Study Objectives
Establish, in a transparent and objective manner, a consensual well-to-wheels energy use and GHG emissions assessment of a wide range of automotive fuels and powertrains relevant to Europe in 2010 and beyond.
Consider the viability of each fuel pathway and estimate the associated macro-economic costs.
Have the outcome accepted as a reference by all relevant stakeholders.
   Focus on 2010+
   Marginal approach for energy supplies
Notes: 05/25/00
1
CONCAWE

## Slide 3: Well-to-Wheels Pathways
Resource
Crude oil
Coal
Natural Gas
Biomass
Wind
Nuclear
Powertrains
Spark Ignition:
Gasoline, LPG, CNG, Ethanol, H2
Compression Ignition:
Diesel, DME, Bio-diesel
Fuel Cell
Hybrids: SI, CI, FC
Hybrid Fuel Cell + Reformer
Fuels
Conventional Gasoline/Diesel/Naphtha
Synthetic Diesel
CNG (inc. biogas)
LPG
MTBE/ETBE
Hydrogen (compressed / liquid)
Methanol
DME
Ethanol
Bio-diesel (inc. FAEE)
Notes: 05/25/00
1
CONCAWE

## Slide 4
MJ non renewable primary input / MJ in the tank
GHG(g) in CO2 eq. / MJ in the tank
WTT Pathways Decomposition
Notes: 05/25/00
1
CONCAWE

## Slide 5: Tank-to-Wheels Matrix
Notes: 05/25/00
1
CONCAWE

## Slide 6: Vehicle Assumptions
Notes: We set the study in a '2010+' timeframe consistent with the EC discussion on fuel substitution at the 2020 horizon.
This focus on 2020 also led to use of a marginal approach for the WTT study

## Slide 7: Tank-to-Wheels study Vehicles Performance & Emissions
Time lag for 0-100 km/h
[s]
< 13
> 30
Gradeability at 1 km/h
[%]
> 180
> 600
Range
(20 km ZEVRange)
[km]
Top speed
Continuous
[km/h]
Time lag for 0-50 km/h
[s]
Time lag for 80-120 km/h
in 4th gear
[s]
Acceleration
[m/s²]
< 4
< 13
> 4.5
Minimum Vehicle Performance Set
All technologies fulfil at least minimal customer performance criteria
“Vehicle / Fuel” combinations comply with emissions regulations
  The 2002 vehicles comply with Euro III
  The 2010+ vehicles comply with EU IV
Notes: We set the study in a '2010+' timeframe consistent with the EC discussion on fuel substitution at the 2020 horizon.
This focus on 2020 also led to use of a marginal approach for the WTT study

## Slide 8: Vehicle Assumptions
Simulation of GHG emissions and energy use calculated for a model vehicle
  Representing the European C-segment (4-seater Sedan)
  Not fully representative of EU average fleet
No assumptions were made with respect to availability and market share of the vehicle technology options proposed for 2010+
Heavy duty vehicles (truck and buses) not considered in this study
Notes: We set the study in a '2010+' timeframe consistent with the EC discussion on fuel substitution at the 2020 horizon.
This focus on 2020 also led to use of a marginal approach for the WTT study

## Slide 9
Version 2c Technology Up-dates
Notes: We set the study in a '2010+' timeframe consistent with the EC discussion on fuel substitution at the 2020 horizon.
This focus on 2020 also led to use of a marginal approach for the WTT study

## Slide 10: CNG fuel consumption maps
CNG bi-fuel
  Fuel consumption map calculated from
    “% comparison” map (NG v. Gasoline)
    Combined with the reference 1.6 l gasoline PISI map
  The bi-fuel engine achieves slightly higher efficiency on CNG than on gasoline, because the ECU calibration can be adjusted to take advantage of the higher octane.
CNG dedicated
  fuel consumption map calculated
    New efficiency map of the bi-fuel engine
    Efficiency increased by 3 points v. bi-fuel version to account for higher compression ratio
  For the dedicated engine, it is possible in addition to increase the compression ratio, giving a further efficiency improvement

## Slide 11: 2002 CNG vehicle performance
CNG Bi-fuel is still not meeting all performance criteria
GHG TTW reductions (v. gasoline)
  CNG BF vehicle: - 21 % (performance criteria not met)
  CNG Dedicated: - 23 % (performance criteria met)

## Slide 12: Compressed Natural Gas (CNG)

## Slide 13: Stop & Start
On the NEDC, fuel consumption during vehicle stop is calculated
It represents 7.5 % of the total fuel consumption
Remarks
  Energy to restart the engine is not taken into account
  The slight modification in engine warm up is not taken into account
The maximum potential can’t be fully retained for “real life” configurations
  3 % is a more realistic figure, Potentially applicable on all 2010 ICE configurations

## Slide 14: Hybrid optimisation
As previously reported in the study, the hybrid technology, when applied to standard size power trains, has the potential to improve the fuel economy by around 15 %
However, further improvements may be expected through additional optimisation of the power ratio between the thermal and electric motors
A theoretical evaluation was carried out in the up-date in order to address this issue
Objective: “adjust” the thermal engine/electric motor power ratio
  To decrease fuel consumption and CO2 emissions
  While still meeting all standard performance criteria

## Slide 15: Results for the “optimised” hybrid configuration
Fuel consumption and CO2 emissions decrease by approximately 5%

## Slide 16: Hybrid configuration optimisation
Thermal Engine / Displacement Optimisation:
  1,6 litre  1,28 litre
  Fuel consumption reduction: about 5 %
  Fully complying with performance criteria
Electric Motor / Power Optimisation:
  14 kW  30 kW (still 1,28 l PISI ICE)
  Fuel consumption reduction: 1 to 2 %
  Fully complying with performance criteria

## Slide 17: Hybrid configuration optimisation: outcome
Theoretical hybrid power train simulations (thermal and electric motors) indicate that some 6% additional fuel economy improvement is potentially achievable from the basic 2010 hybrid PISI gasoline vehicle
This additional potential 6% improvement is assumed to be applicable to all power trains and fuel types covered by the study
This potential has been recognised by an increase of the variability range for hybrid fuel consumption

## Slide 18: Hydrogen from NG : ICE and Fuel Cell
Source: WTW Report, Figures 8.4.1-1a/b & 8.4.1-2a/b
Notes: In the short term, natural gas is the only viable and cheapest source of large scale hydrogen.
The WTW energy use / GHG emissions are higher for hydrogen ICE vehicles than for conventional fuels and CNG vehicles
Liquid hydrogen is more energy intensive than compressed hydrogen
If hydrogen is produced from NG, GHG emissions savings only achieved with fuel cell vehicles
- but hybrids come close

## Slide 19: Hydrogen from NG : ICE and Fuel Cell
Source: WTW Report, Figures 8.4.1-1a/b & 8.4.1-2a/b
If hydrogen is produced from NG, GHG emissions savings are only achieved with fuel cell vehicles
Notes: In the short term, natural gas is the only viable and cheapest source of large scale hydrogen.
The WTW energy use / GHG emissions are higher for hydrogen ICE vehicles than for conventional fuels and CNG vehicles
Liquid hydrogen is more energy intensive than compressed hydrogen
If hydrogen is produced from NG, GHG emissions savings only achieved with fuel cell vehicles
- but hybrids come close

## Slide 20: Overall picture: GHG versus total energy
Hydrogen
Most hydrogen pathways
are energy-intensive
2010+ vehicles

## Slide 21: Hydrogen: Key Points
Many potential production routes exist and the results are critically dependent on the pathway selected.
Electrolysis using EU mix electricity results in higher GHG emissions than producing hydrogen directly from NG
Renewable sources have a limited potential for the foreseeable future and are at present expensive
More efficient use of renewables may be achieved through direct use as electricity rather than road fuels application
On-board reforming could offer the opportunity to establish fuel cell vehicle technology with the existing fuel distribution infrastructure
The technical challenges in distribution, storage and use of hydrogen lead to high costs. Also the cost, availability, complexity and customer acceptance of vehicle technology utilizing hydrogen technology should not be underestimated.

## Slide 22: Cost of fossil fuels substitution and CO2 avoided
Some cost elements are dependent on scale (e.g. distribution infrastructure, number of alternative vehicles etc)
As a common calculation basis we assumed that 5% of the relevant vehicle fleet (SI, CI or both) converts to the alternative fuel
  This is not a forecast, simply a way of comparing each fuel option under the same conditions
  If this portion of the EU transportation demand were to be replaced by alternative fuels and powertrain technologies, the GHG savings vs. incremental costs would be as indicated
Costs of CO2 avoided are calculated from incremental capital and operating costs for fuel production and distribution, and for the vehicle
The costs, as calculated, are valid for a steady-state situation where 5% of the relevant conventional fuels have been replaced by an alternative. Additional costs are likely to be incurred during the transition period, especially where a new distribution infrastructure is required.

## Slide 23: Additional cost of alternative 2010+ vehicles
Base: Gasoline PISI

## Slide 24
Overall picture: GHG mitigation Costs

## Slide 25: General Observations: Costs
A shift to renewable / low carbon sources is currently costly
  However, high cost does not always result in high GHG emission reductions
  At comparable costs GHG savings can vary considerably
The cost of CO2 avoidance using conventional biofuels is around
  150-300 €/ton CO2 when oil is at 25 €/bbl
  50-200 €/ton CO2 when oil is at 50 €/bbl
Syn-diesel, DME and ethanol from wood have the potential to save substantially more GHG emissions than current bio-fuel options at comparable or lower cost per tonne of CO2 avoided.
  Issues such as land and biomass resources, material collection, plant size, efficiency and costs, may limit the application of these processes

## Slide 26: General Observations: Costs
For CNG, the cost of CO2 avoided is relatively high as CNG requires specific vehicles and a dedicated distribution and refueling infrastructure
  Targeted application in fleet markets may be more effective than widespread use in personal cars
The technical challenges in distribution, storage and use of hydrogen lead to high costs.
  The cost, availability, complexity and customer acceptance of vehicle technology utilizing hydrogen should not be underestimated

## Slide 27
Alternative use of primary energy resources - Biomass
Wood gasification or direct use of biomass for heat and power offers greatest GHG savings
Potential for CO2 avoidance from 1 ha of land
Reference case:
2010 ICE with
Conventional fuel
CO2 savings per hectare are better for advanced biomass than ethanol or biodiesel
Using biomass for electricity generation offers even greater savings

## Slide 28: Conclusions
A shift to renewable/low fossil carbon routes may offer a significant GHG reduction potential but generally requires more energy. The specific pathway is critical
No single fuel pathway offers a short term route to high volumes of “low carbon” fuel.
  Contributions from a number of technologies/routes will be needed.
  A wider variety of fuels may be expected in the market
  Blends with conventional fuels and niche applications should be considered if they can produce significant GHG reductions at reasonable cost
Transport applications may not maximize the GHG reduction potential of renewable energies
Optimum use of renewable energy sources such as biomass and wind requires consideration of the overall energy demand including stationary applications
  More efficient use of renewables may be achieved through direct use as electricity rather than road fuels applications

## Slide 29
JEC Study History
Version 1: 2001 – 2003
Version 1 published December 2003
Workshop at JRC 2004 to review and start of updates
Version 2: 2004 – 2005
Version 2a published May 2006
Biomass availability workshop May 2006
Version 2b published December 2006
Version 2c published May 2007 after small corrections
Version 3: 2007 – 2008
Publication expected summer 2008
Version 4: 2008 – 2010
Expected end 2010

## Slide 30: What this type of WTW study can bring in the debate ?
Ways to encourage the fuels performances in term of sustainability are curently analyzed (Europe-California-UK:Carbon Reporting under the Renewable Transport Fuel Obligation).
As shown in the study, conventional pathways (Gasoline/Diesel) present WTT GHG emissions in a relatively low range, around 15 % of the WTW emissions. Road TTW GHG emissions are prevalent. The GHG reduction at WTT fuels side is helping, but in a limited way.
When playing with Bio/Renewable fuels, WTW thinking is mandatory, as the «road side» emissions are the same (e.g. Diesel vehicle fuelled by fossil Diesel or BioDiesel). Only the WTW assessment is taking into account the CO2 loop.

## Slide 31: What this type of WTW study can bring in the debate ?
The results regarding Hydrogen applications are a good example to look at possible future « Fuels Certifications ». The study is clearly showing that there are various way to generate and use hydrogen for vehicles propulsion, including the dirty one’s.
When H2 will be sold on the road, certificates could be adopted, constraining the producers to comply with GHG emissions limits
GHG (gr CO2 eq.)
MJ of Energy Sold
Certified

## Slide 32: Well-to-Wheels analysis of future automotive fuels and powertrains in the European context
The study report will be available on the WEB:
http://ies.jrc.cec.eu.int/WTW
For questions / inquiries / requests / notes
to the consortium,
please use the centralised mail address:
infoWTW@jrc.it
Notes: 05/25/00
1
CONCAWE