## Slide 1
October 2008
Evaluation of
Hybrid System and Plug-in Hybrid System
In Japanese Fuel Efficiency Regulation
Akihiko HOSHI
Deputy Director
Environment Division
Road Transport Bureau
Ministry of Land, Infrastructure, Transport and Tourism
Working paper No.: EFV-02-04
(GRPE Informal Group on EFV,
2nd Meeting, 30/31 October 2008)

## Slide 2: Agenda
Top Runner Approach for FE regulation
Fuel Efficiency regulation for HDVs ・ Simulation Test Method ・ for HD HEV Test
Fuel Efficiency Regulation for LDVs ・ Conventional Test Method ・ for LD HEV Test ・ Challenge for PHEV Evaluation
IPT Bus : PHEV for HDVs

## Slide 3: Maximum improvement: “Top runner approach”
Base Year
Target Year
Average
now
Top-Runner
now
Target Standard Value in Target Year
Year
＋α：positive factors
－β：negative factors
Positive Factors: Technological Improvement
Negative Factors: Exhaust Emission Regulations, etc. (trade-off relation with fuel economy)
vehicles future
vehicles now
○ By target year, average fuel consumption must be higher than the best fuel efficiency in the base year.
○ Standard should be high but reachable because target values are already achieved by actual vehicles in the base year.
○ Particular types of cars such as HEVs and MT mounted cars are excluded from top runner

## Slide 4: “Top runner approach”: Positive factor (+α)
Conventional fuel efficiency improvement technologies (2 – 4 % in total)
  Engine compression ratio increase, Friction reduction, Weight reduction,
  Reduction of vehicle travel resistance, Low rolling resistance tires
  Optimizing overall control of engine
Engine improvement [Gasoline engine]
  4 valves (1%), 2 valves and 2 ignitions (2%), Variable valve system (1 – 7 %)
  Direct-injection stoichiometric engine (2%), Direct-injection lean-burn engine (10%)
  Variable cylinder (7%), Miller cycle (10%)
  High volume EGR (2%), Roller cam follower (1%), Offset crank (2%), Variable compression ratio (10%)
Engine improvement [Diesel engine]
  4 valves (1%) , Electronically controlled fuel injection device (1.5%) , Common rail (2.5%), Direct-injection diesel engine (8%), High pressure injection (1%), Supercharger and supercharger efficiency improvement (2 – 2.5%), Intercooler (1%), EGR (0.5 – 1%), Roller cam follower (1.5%), Offset crank (2%)
Auxiliary equipment
  Electric power steering (2%), Charge control (0.5%)
Driving system improvement
  Idle-neutral control (1%), AT with more gears (1 – 4%), Switch to CVT (7%), Switch to automated MT (AMT/DCT) (9%), Switch to MT (9%)
Introduction of fuel-efficient vehicles
  Hybrid vehicles (15 – 70%), Diesel vehicles (20%) , Idling stop vehicles (4 – 7%)

## Slide 5: “Top runner approach”: Negative factor (-β)
Exhaust emission regulations (▲3 to ▲7.5% in total)
  Caused by technologies used on diesel vehicles and direct-injection lean-burn vehicles in response to the 2009 exhaust emission regulations.
  Technologies considered were engine body improvement (NOx reduction by improving EGR, PM reduction by high pressure injection, etc.) and aftertreatment devices such as NOx occlusion reduction catalyst and continuous regeneration type DPF, etc.
Safety regulations (▲0.1 to ▲1.4% in total)
  Caused by increased weight and travel resistance as a result of measures against/for offset crash, pedestrian protection, ISO-FIX, etc.
Noise regulations(▲0.1% in total)

## Slide 6: Maximum improvement: “Top runner approach”
2015 New Target Standard Values
Current Fuel Economy Performance and Level of 2015 Target Standard Values
* Example (passenger vehicle: 4 weight categories between 971kg and 1420kg)
* Fuel economy values on this table are measured by JC08 mode.
2004 Average Fuel Economy
Hybrid Vehicles
(excluded form Top-Runner)

## Slide 7: Fair Competition: “Segmentation by vehicle weight”
○ Segmentation by weight so that competition will become fair in each category
 Promoting introduction of advanced power-train and vehicles technologies by classifying vehicles into different categories by weight, transmission, fuel, and vehicle type.
FE (km/l)
In the case of a singe standard value
- Company A sells mostly compact cars that are above the standard value, so no improvement is necessary.
- Company B sells mostly larger vehicles that are below the standard value, so most car need improvement.
- Meeting the standard is possible just by increasing the sales of compact cars
In the case of a standard value for each category
- Both Company A and B must improve the fuel efficiency of cars that are below the standard
- Both companies cannot meet the standard by change of model mix and therefore, introduction of advanced technologies is necessary for all the weight class.
Single standard value
Standard value for
each weight category
Company A
Company B

## Slide 8: Fair Competition: Segmentation by Vehicle Structures (Only for N1)
For N1 vehicles, segments are defined by “several other features” in addition to “vehicles weight”, taking into consideration:
  Market of each vehicle type
  Applied technology for each vehicle type
  Specification/Vehicle structure of each vehicle type

## Slide 9: Agenda
Top Runner Approach
Fuel Efficiency regulation for HDVs ・ Simulation Test under JE05 ・ HD HEV Test
Fuel Efficiency Regulation for LDVs ・ Conventional Test Method ・ for LD HEV Test ・ Challenge for PHEV Evaluation
IPT Bus : PHEV for HDVs

## Slide 10
Urban Driving Mode = JE05 Mode (Emission Test Mode)
Interurban Driving Mode: 80km/h Constant Speed Mode with Road Gradient
Combination of Urban Driving Mode(JE05) and Inter-urban Driving Mode
Japanese test mode for HDVs(JE05)
• Stand-alone Engine Measurement Method
• Including Transient Operating Points
Engine speed
Time (s)
Engine torque
Time (s)
Conversion to Histories of
Engine Speed and Engine Torque
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Japanese test mode for HDVs(JE05)
Stand-alone engine test of fuel efficiency by JE05 mode may
require a large number of different engine types.
The manufacturers spend large resources (time, labor and money)
for constructing the testing facility and performing measurements.
Actual Engine Test of Fuel Efficiency by JE05 Mode is NOT feasible and effective.
Evaluation of Fuel Efficiency by Simulation Method
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Characteristics of Simulation Method
• Using real vehicle and engine specifications
Engine speed (rpm)
Torque (Nm)
Real Fuel consumption map
Engine parameters
Drive train parameters
• The method is an extension way of the emission test.
Low cost and Hi test efficiency
 Problems of reproducibility of driving resistance
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Simulation Method
Driving mode
Conversion program
•Determine gear-shift positions.
•Calculate engine speed and torque.
=
Urban driving mode
Interurban driving mode
Engine Operating Mode
Vehicle specifications
Fuel efficiency map
Engine speed (rpm)
Torque (Nm)
*Before simulation, perform
operation tests to create a
fuel efficiency map
Engine torque
Engine speed
Time (s)
Fuel consumption
Fuel efficiency
Computing
=
Phase of
conversion
Speed vs. time
Engine speed / torque vs. time
Phase of
calculation
of fuel
efficiency
Source: Japan Automobile Research Institute:
Survey Report on Evaluation Methods
for Heavy Vehicles, March 2003
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Simulation Method Flowchart and Equation
Urban Driving Mode
JE05 mode
Engine
Operating
Mode
Eu: Fuel
Efficiency
Interurban Driving Mode
80km/h constant speed mode with gradient
Combined
Engine
Operating
Mode
Eh: Fuel
Efficiency
E: Fuel
Efficiency
E=1 / (u / Eu + h / Eh)
E: Heavy vehicle mode fuel efficiency (km/L)
Eu: Urban driving mode fuel efficiency (km/L)
Eh: Interurban driving mode fuel efficiency (km/L)
u: Proportion of urban driving mode
h: Proportion of interurban driving mode
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: HILS Test Method
• Fuel Efficiency Test
⇒ desired simple method: Simulation Method
⇒ desired dynamo test with only engine: without electric system
• Emission Test
Structurally-complex system
Need multiple E/D for 4-wheel drive vehicles
• System Bench Method for HEV
Hardware-In-the-Loop Simulator (HILS) Test Method was developed
RESS
Inverter
M/G
E/D
Measurement of Exhaust Emission
Engine
System Bench Method
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: HILS Test Method
Chassis Base
0
500
1000
1500
2000
0
20
40
60
80
100
Speed (km/h)
Time (sec)
HEV
(Hybrid Electric Vehicle)
Fuel Consumption Ratio
Run JE05
RESS
Vehicle Model
Torque
Engine speed
Fuel Consumption
Driver model
Battery model
Inverter
Motor model
Engine model
Get E/G rpm, E/G Torque
Exhaust Emission
E/D
Measurement of Exhaust Emission
Engine
Hybrid ECU
imput Vehicle Parameters
・Gear Ratio, eff.
・Eng. spec
・Vehicle spec etc.
HILS (Hardware In the Loop Simulator)
Virtual JE05 Running on CPU

## Slide 17: Test Procedure for Hybrid HDVs
2nd step is same as Simulation Method
Vehicle Specification
Vehicle weight, Driving Resistance, Full load engine torque, Motor characteristics, Battery characteristics, etc.
Urban Driving Mode
Interurban Driving Mode
Engine Operating Mode
1st Step
Hybrid ECU (Real)
Simulated driving
by HILS Program
to determine
Engine Torque &
Engine Speed
Input
Connect
2nd Step
エンジン燃費マップ
Engine torque
Engine speed
Time (s)
Input
*Before simulation, perform
operation tests to create a
fuel efficiency map
=
Fuel consumption
Fuel efficiency
HILS
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: HILS System
Engine
TM
MG
Inverter
Capacitor
HEV model
Main parameters
- Engine (Torque map)
- MG (Torque map, Electric-power consumption map)
- RESS (Internal resistance, Open-circuit voltage)
- Vehicle mass
- Inertia
- Gear ratio
- Transmission efficiency
Driver model
Acceleration
& Braking
Digital signal processor
Interface
Actual ECUs
24V Power Supply
0
500
1000
1500
2000
0
20
40
60
80
100
Vehicle Speed (km/h)
Time (sec)
Reference vehicle speed
(JE05 driving cycle)
Simulation results
Torque
sec
rpm
sec
Calculated fuel economy with F.C. map or Measure exhaust emissions with an engine unit
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Agenda
Top Runner Approach
Fuel Efficiency Standard for HDVs ・ Simulation Test Method ・ for HD HEV Test
Fuel Efficiency Standard for LDVs ・ Conventional Test Method ・ for LD HEV Test ・ Challenge for PHEV Evaluation
IPT Bus : PHEV for HDVs

## Slide 20
Current Test Procedures for LD Vehicle
Vehicle’s driving wheels placed on virtual road surface (rollers).
Exhaust emission and fuel economy measured when operating vehicle in fixed pattern.

## Slide 21
Operation Mode
【Japan】
【 US】
【Europe】
Average 22.7km/h
Average 77.7km/h
Average 31.5km/h
Average 33.6km/h
Distance traveled：8.172km
Average speed：24.4km/h
Maximum speed：81.6km/h
Tests corresponding to traffic conditions of the respective areas and operation modes are conducted.

## Slide 22
(1) Exhaust emission measurement
[Technical Standard (Attachment 42)]
① Mode test is conducted several times. Relation between current balance (ΔSOC) and exhaust emission weight are obtained.
② When statistical significance can be recognized for each exhaust emission component, exhaust emission weight of the prescribed tests shall be corrected to an exhaust emission weight corresponding to a current balance of zero, based on the inclination of the linear regression formula (correction factor).
③ When there is no statistical significance, corrections do not need to be made.
0
ΔSOC (Current balance) [Ah]
Emission weight [g/km]
The current balance is corrected to zero based on relational expression with Δ SOC, considering effects by battery’s state of charge (SOC).
(2) Fuel consumption measurement [TRIAS (5-9-2007)]
① Fuel consumption shall be calculated by carbon balance method using exhaust emission value corrected to a current balance of zero, similar to exhaust emission.
Correction of current balance
Test procedures for HEV

## Slide 23: From vehicle with internal combustion engine to HEV, Plug-in HEV
Reduces of petroleum energy consumption
Replaces petroleum energy with electricity
GAS
GAS
Vehicle with internal combustion engine
HEV
Plug-in HEV

## Slide 24
Characteristics of Plug-in Vehicles
Charge Depleting (CD) mode: Vehicle is operated by consuming electric energy supplied from external source ) (while reducing battery’s state of charge (SOC))
Charge Sustaining (CS) mode: By fossil combustion power(Engine + regenerated electric energy), operation of the vehicle is controlled so the SOC value remains constant.
Battery’s state of charge
SOC (%)
0
Distance (km)
A
Charge Depleting (CD) mode
Charge Sustaining (CS) mode
All Electric Range (AER) type control
Blended type control
20
80
Normal hybrid vehicles
60
40
100
+
Operation of PHEV vehicles change significantly after reaching A km
Plug-in range
(Charge Depleting Range)
ΔSOC= -
ΔSOC= -
ΔSOC= 0
ΔSOC= 0
1st test cycle
2nd test cycle
3rd test cycle
4th test cycle
A’

## Slide 25
Challenges in evaluation of Plug-in HVs
1. Definition of Plug-in range (CD range)
Plug-in range(CD range) does not always show the total work of charged electric power( How can we define capacity of electricity?).
- How can we estimate the changing point (A or A’) from test result?
2. Combination of two different performances of CD mode/CS mode)
How can we incorporate utility factor in the process of combination of two different performance of ?
How can we accommodate further and rapid improvement of Plug-in performance in the near future (mainly achieved by new technology on battery power intensity or cost down)?
3. Consumer Information
How can we inform consumers of the multi-layered performance of Plug-in HV without confusion?
The actual performance differs depending on ways of use.

## Slide 26: Agenda
Top Runner Approach
Fuel Efficiency Standard for HD Vehicle ・ Simulation Test Method ・ for HD HEV Test
Fuel Efficiency Standard for LD Vehicle ・ Conventional Test Method ・ for LD HEV Test ・ Challenge for PHEV Evaluation
IPT Bus : PHEV for HD Vehicle

## Slide 27: IPT Hybrid Bus: “Plug-less” Plug-in for HD Vehicle
Power Unit
Lithium Ion Battery Unit

## Slide 28
IPT Hybrid Bus
Diesel Engine
Air Conditioner
IPT Unit
Battery
Power Supply
Up & Down
(180mm – 50mm)
IPT Secondary Coil
Inverter
Motor
IPT Primary Coil
Big Power Quick Charge
On Board Secondary Coil
Concrete-covered Primary Coil

## Slide 29
3.実証試験概要 【走行路】
8.8km / RT by HV drive
Depot
Charge Station
第一ターミナル
写真
国際線ターミナル
写真
3.1km / lap by EV drive
Driving Demonstration Test
Haneda Airport Shuttle Bus

## Slide 30: Vehicle Energy Source Shift
Internal Combustion Engine Vehicle
Gasoline
Diesel
Etc.
Full Electric Vehicle
Now
Near Future
Far Future
PHEV
IPT
Need more
Power Density
Energy Density
for Battery.
PHEV is EV with On-board Re-charger

## Slide 31
Distance
long
short
City
HWY
t
v
v
t
Delivery
Urban area
Suburbs
Intercity
Driving Mode
Right Vehicle to Right Place
HEV
Diesel
PHEV

## Slide 32
Thank you all for listening so attentively
For further questions:
Akihiko HOSHI
Environment Division
Road Transport Bureau
Ministry of Land, Infrastructure, Transport and Tourism
E-mail: hoshi-a2rd@mlit.go.jp
Tel: +81 3 5253 8604