## Slide 1
1. Contents of Study :
- Comparison of lateral displacement of Sine with dwell test
measured/calculated by
A ; GPS system
B ; Vx, Vy measured by optical sensor
C ; ∫∫ ay C.G. dt ( as defined in the regulation )
- GPS systems : (the detail of specification; refer to the Appendix)
The Lateral Displacement Measured by GPS
Compared with Other Methods
Manufacture:A
Manufacture:B
Make
Oxford Technical Solutions
Racelogic
Model
RT3002
VBOX 2 SX
Positioning
L1/L2 Kinematic
DGPS
Accuracy
2 cm
20 cm
Resolution
1 cm
Sampling f
100 Hz
20 Hz
- 1 -
31/10/2007
Table 1 : Specification of GPS system
GTR-ESC-2008-01

## Slide 2
The Lateral Displacement Measured by GPS
Compared with Other Methods
2. Test Procedure :
- Test Procedure : Sine with dwell test
- Vehicle speed : 80 km/h
- Lateral Displacement : 1.07 sec. after steer-in
- Test vehicles :
Manufacture A
Manufacture B
RWD 4.6L V8
RWD 3.5L V6
2.970
2.650
FR
1126
903
RR
1042
784
FR
245/45R19
225/45R18
RR
245/45R19
245/45R18
Weight [Kg]
Tire
Engine
Wheelbase [m]
- 2 -

## Slide 3
The Lateral Displacement Measured by GPS
Compared with Other Methods
GPS
(A)
VX,VY, Yaw
(B)
∫∫AY
(C)
0 50 100 150 200 250 300
4
3
2
1
0
Lateral Displacement (m)
Steering Wheel Angle (deg)
GPS
(A)
VX,VY, Yaw
(B)
∫∫AY
(C)
0 50 100 150 200 250 300
4
3
2
1
0
Lateral Displacement (m)
Steering Wheel Angle (deg)
Manufacture A
Manufacture B
5.0 x ( 0.3 G Steering Wheel Angle (SWA))
3. Test Results (1)
- 3 -
Fig.1 Lateral displacement of Sine with dwell test (at 1.07 sec)

## Slide 4
The Lateral Displacement Measured by GPS
Compared with Other Methods
-5 ~ -7 cm ( -1.7 ~ -2.2 %)
0 ~ +5 cm ( 0 ~ +1.5 %)
3. Test Results (2)
0 50 100 150 200 250 300
0.4
0
-0.4
Displacement difference (m)
Steering Wheel Angle (deg)
Manufacture A
GPS results is smaller
than others
GPS – (Vx,Vy)
GPS – ∫∫AY
Displacement difference (m)
0 50 100 150 200 250 300
0.4
0
-0.4
Steering Wheel Angle (deg)
Manufacture B
GPS results is smaller
than others
GPS – (Vx,Vy)
GPS – ∫∫AY
Difference between GPS results and double integral of Ay at 5.0x(0.3g SWA)
- 4 -
Fig. 2 Comparison of lateral displacement between GPS result and others

## Slide 5
4. Conclusion
GPS system can be allowed as the alternative measuring method
for type approval testing provided the manufacture shows the
evidence of their GPS system data equivalent with double integral
of Ay.
The Lateral Displacement Measured by GPS
Compared with Other Methods
5. Reference
The difference between GPS results and double integral of
Ay at 5.0x(0.3g SWA) can be considered as equivalent for both GPS systems.
2) The tendency of the difference was observed between GPS result and others depends on the model of GPS system.
- 5 -