## Slide 1
Proposal on the requirements for the determination of the ocular points when the driver seat has fixed seat-back angle or when the design torso line cannot be set at 25°
Informal document No. GRSG-95-27
(95th GRSG, 21 – 24 October 2008
agenda item 7)
Transmitted by the expert from the European Commission (EC)

## Slide 2
Introduction
This short presentation is aimed at describing the calculation process of the variation in height of the driver’s ocular points OD and OE for a seat back angle ranging from 5 ° to 40 °.
Driver’s ocular points OD and OE have been defined in Directive 71/127/EEC and UNECE Regulation No 46 taking into account a design seat back angle of 25°
Simplified corrections are proposed in accordance with the method used to check the rearward field of vision.
Vertical coordinate corrections should be Introduced in new Annex 11 to UNECE regulation No. 46
Ref: Bosch Memento de tachnologie automobile

## Slide 3
50th Percentile Male Hybrid III test Dummy
Body dimensions have to be obtained from dummy manufacturer
Length of the torso from the H point to the shoulder (start of neck).
Z2=J+I-C=200.7+337.8-86.4= 452.1mm
TEST PARAMETER DESIGNATION in mm
H-Point Height (Ref) (C) 86.4 ±2.5
Shoulder to Elbow Length (I) 337.8 ± 7.6
Elbow Rest Height (J) 200.7 ± 10.2

## Slide 4
From trigonometry
cos25o=Z3/Z2 ,
Z2=452.1mm is found from the user’s manual for the 50th male hybrid III test dummy so Z3=409.74mm for Z0=635mm
It is assume that the head is 90o vertical to the X axle
Then Z1=Z0-Z3=635-409.74= 225.26mm
The equation which links the seat back angle with the height variation ΔΖ:
ΔZ=225.26+ 452.1cosθ-635
Where θ is the variable
Calculation procedure
Z0=635mm
Eyes
H point
25o
Z2
Z1:height from neck to eyes
Z3
25o
Z
X

## Slide 5
Results
θ values: 5° to 40° step of 1°, in
ΔZ=225.26+ 452.1cosθ-635
The table on the right hand site shows the vertical coordinates correction ΔΖ (in mm) from 5° to 40° seat angle
The graph below demonstrates the variation of ΔΖ against degrees

## Slide 6
Comparison with previous proposal
The point of reference of the previous proposed correction for ΔΖ is unclear and all ΔΖ’s are negative which is unrealistic if we consider the starting reference point is at 25°.
The current proposal is presenting a realistic movement of the seat from 5° to 40° with a positive and negative variation.