Proposal for draft Corrigendum 2to Revision 2 of Regulation N°44

A.	PROPOSAL

Paragraph 7.1.4.4.1.1., add the footnote at the 550 dimension in Figure 1 :

7.1.4.4.1.1. Forward facing child restraints: the head … is 840 mm.

* / For the purpose of the test specified in paragraph 7.1.4.1.10.1.1., this dimension shall be  500  mm.

B.	JUSTIFICATION

During its 33rd session the GRSP accept a document for Revision 1 - Amendment 5

Supplement 6 to the 03 series of amendments - Date of entry into force: 12 August 2004

without reference to the footnote.

This footnote was added during the 32nd session of GRSP. See report TRANS/WP.29/32 page 22.

7.1.4.1.10.2. For ISOFIX child restraint system of other size classes with the anti-rotation device in use."

Paragraph 7.1.4.4.1.1., figure 1, insert a reference to a footnote 5/ to the 550 dimension, and insert the corresponding footnote 5/, to read:

_____________

"5/ For the purpose of the test specified in paragraph 7.1.4.1.10.1.1., this dimension shall be 500 mm."

All technical services are applying the requirement of the footnote on the current tests.