## Slide 1
<number>
Current Status of Discussion on New Standards for High-Pressure Hydrogen Containers in Japan
Japan Automobile Standards Internationalization Center (JASIC)
24-26 September, 2008
UN/ECE/WP29/AC3 GRSP HFCV-SGS 4th meeting
SGS-4-05
Notes: <number>

## Slide 2
<number>
* Japan has been discussing the new standards according to the original schedule.
In future, Japan plans
* To develop the draft Japanese standards by Oct. 2008 by focusing on standardization in Japan, with a view to issuing the standards in Mar. 2010 (a change to be made to the standards: from the current 35 MPa to 70 MPa);
* To shift the focus of activities on international harmonization after completion of development of the draft Japanese standards in Oct. 2008 so that Japan can contribute to development of the draft GTR during 2009 in collaboration with ISO, SAE, etc.
Current Status of Discussion on New Standards for Containers

## Slide 3
<number>
Outline of New Standard for Containers
Current (JARI S 001)
New Standard
New standard applied
(Inner volume the same; CFRP reduced)
Current standard applied
・Safety guaranteed
・Lighter weight and Lower cost
(reduced CFRP and used lower grade)
-Maximum Working Pressure 70 MPa
-Durability strength guaranteed in consideration
of Vehicles Usage and Lifetime.
= Sequential Loading Test (scratch/over fill/low and high
temperatures/stress rupture/chemical exposure/fatigue/
proof pressure/burst)
-Burst Pressure
Working Pressure reduced (After Durability Test)
-Fatigue Life cycles reduced
-Expansion of materials selection
future standardization of materials evaluation method.
-Maximum Working
Pressure 35 MPa
-Strength guaranteed
in a brand-new cylinder
= Independent Loading Tests
-Burst Pressure
> Working Pressure x 2.25
-Fatigue Life > 11,250 Cycles
-Materials Designated
(A6061-T6,SUS316L)
Notes: <number>

## Slide 4
<number>
Draft Schedule with International Harmonization
Propose to
SAE, ISO, gtr
CY2007
CY2008
CY2009
CY2010
CY2011
CY2012
Japanese New Standards
SAE
J2579
ISO
15869
gtr
Data Acquisition of metal materials
Technical Norms
for material
Issue
2nd DIS
Rejected
Issue?
Issue
Establishment of gtr
Draft
Deliberations
Study Proposals
Data Acquisition for container@JARI
Data Acquisition @PLI
Deliberations
Issue(Step-1)
Issue(Step-2)
TIR
3nd DIS
Rejected
at Sep.2008
Harmonization
Collaborate with SAE
using each data-based
Notes: <number>