## Slide 1: Hydrogen Fuel Cell Vehicle Safety
Research to Support Rulemaking/GTR Objectives
September 2008
SGS 04 - 07

## Slide 2: Overview
GTR Action Plan
Safety Issues
Alternative Approaches
Research/Rulemaking Goals
Research Tasks
Schedule

## Slide 3: GTR Action Plan ECE/TRANS/WP.29/2007/41 (April 2007)
Objective
  Attain equivalent levels of safety to conventional gasoline vehicles
  Develop a global technical regulation concerning hydrogen/fuel cells
  Performance based and does not restrict future technologies
Content:
  Performance requirements for fuel containers
  Electrical isolation
  Maximum allowable hydrogen leakage

## Slide 4: Safety issues to be addressed
Fuel system crashworthiness
  Hydrogen leakage limits
  Electrical integrity of high voltage fuel cell propulsion system
  High pressure container safety
Safety level consistent with gasoline, CNG, conventional electric hybrids
  FMVSS Nos. 301, 303, 304, and 305

## Slide 5: Approaches to address fuel system crashworthiness
Hydrogen leakage limits
  Hydrogen (SAE) vs. helium surrogate (SAE, Japan, OICA, FMVSS)
  High pressure vs. low pressure and scaling up (SAE)
Electrical integrity of high voltage fuel cell propulsion system
  Active fuel cell with hydrogen onboard vs.
  Inactive fuel cell, system “off” (SAE, AIAM, Japan)
High pressure container safety
  Cumulative life cycle and extreme use durability (SAE) vs. discrete testing (i.e., FMVSS, CSA/NGV2, HGV2, ISO, EIHP, etc.)
  Localized flame impingement (SAE) vs. bonfire (FMVSS, etc.)
  High pressure (FMVSS No. 303) and/or low pressure (SAE,GM) – vulnerability to impact is greater at low pressure

## Slide 6: Issues Associated with Each Fueling Approach for Crash Testing
High pressure hydrogen
  + Electrical system is operational
  + Worse case for leak rate
  - Poses additional fire hazard
High pressure helium
  + Consistent with FMVSS Nos. 301, 303
  + Non-flammable
  - Surrogate leak rate is slightly different
  - Electrical system is not operational
Low pressure hydrogen option
  + Electrical System operational
  - Must scale up leak rate to represent worse case at high pressure
  +/- Cylinders more vulnerable to impact at low pressure

## Slide 7: Research/Rulemaking goals
Conduct research to assess all proposed alternatives
  Confirm that selected alternative detects potential failure
Prescribe additional requirements if results indicate safety need, e.g.:
  Localized flame impingement test replaces bonfire test for hydrogen containers
  Extend post-crash leakage measurement beyond 60 minutes to adjust for reduced flow rate of helium through same sized orifice
Prefer selecting option that is analogous to and consistent with existing requirements
  High pressure helium
  Single crash test for both electrical isolation and fuel leakage

## Slide 8: Research Tasks to Support Rulemaking/GTR Objectives
Localized flame impingement on hydrogen storage cylinders
Cumulative cylinder life cycle testing
Comparative assessment of fueling options for crash testing
Fire safety of proposed leakage limits
Electrical isolation testing in the absence of hydrogen

## Slide 9: Localized flame impingement on hydrogen storage cylinders
FMVSS No. 304
  Requires bonfire test
  Cylinder must survive engulfing fire for 20 minutes or vent contents
Localized flame impingement (SAE)
  Real world data indicates Type IV composite cylinders do not vent in localized fire
  Lack of heat transfer to PRD
  Composite loses structural integrity, resulting in catastrophic rupture
Research Task:
  Localized fire test procedure – Developed by Powertech under contract to Transport Canada.
  Verification testing – Conducted under contract to NHTSA. Cylinders which have failed in real world fires will be tested and mitigating technologies will be assessed (heat transfer, sensing, shielding)
Possible Outcome:
  Requirement for localized flame test

## Slide 10: Cumulative cylinder life cycle testing
Generate simulated real-world life cycle data
  SAE TIR 2579 expected service and durability testing. (pneumatic gas cycling, parking, extreme temperature, flaw, chemical tolerance, burst)
  Test procedures developed under contract to DOE/NREL
  Japan considering similar requirements in new standard, JARI 001 upgrade.
Research Task:
  Initial results indicate that altering test protocol effects results
  Conduct life cycle testing on representative hydrogen storage systems, vary test conditions to represent different service conditions
Possible Outcome:
  Requirement for pneumatic rather than hydraulic pressure cycling test (FMVSS No. 304)
  Requirement for post pressure-cycle burst strength

## Slide 11: Comparative assessment of fueling options for crash testing
Fueling options advocated by industry
  High pressure hydrogen (SAE)
  High pressure helium (SAE, Japan)
  Low pressure hydrogen (SAE,GM)
Research task:
  Conduct testing to compare container vulnerability to impact at high and low pressure fill
  Conduct leakage tests of hydrogen and helium at high and low pressure fill for a range of cylinder sizes
Possible Outcome:
  Selection of most appropriate fill option for assessing pass/fail leakage and fuel system vulnerability per FMVSS crash conditions

## Slide 12: Fire safety of proposed leakage limits
Hydrogen concentrations exceed lower flammability limit in vehicle compartments
Research Task:
  Conduct hydrogen ignition tests in the trunk, engine and occupant compartments of vehicles and crash tested ICE vehicles
Outcome:
  Confirmation of the fire safety of proposed leakage limits, which are currently based on the thermal energy equivalent to gasoline

## Slide 13: Electrical isolation testing in the absence of hydrogen
Fuel cell produces no voltage when crash test is conducted using helium surrogate
  Measure isolation by applying test voltage from an external source (megohmmeter)
Research Task:
  Conduct isolation testing with no hydrogen present, using megohmmeter
Possible Outcome:
  Confirm that testing can be conducted with the megohmmeter, without inducing damage to the vehicle propulsion circuit
Notes: Fuel cell produces no voltage when crash test is conducted using helium surrogate
  Measure isolation by applying test voltage from an external source (megohmmeter)
Research Task:
  Conduct isolation testing with and without known short circuit and hydrogen present
  Conduct isolation testing with and without known short circuit, no hydrogen present, using megohmmeter
Possible Outcome:
  Confirm that testing can be conducted with the megohmmeter, without inducing additional damage to either the vehicle propulsion circuit or the test instrument

## Slide 14: R&D Timeline to Support Rulemaking Objectives

## Slide 15: Schedule
Localized flame impingement on hydrogen storage cylinder:
6 months
Cumulative cylinder life cycle testing:
15 months
Comparative assessment of fueling options for crash testing:
15 months
Fire safety of proposed leakage limits:
12 months
Electrical isolation testing in the absence of hydrogen:
12 months