## Slide 1: GTR-Development for H2- and FC-Vehicles a TÜV SÜD - opinion
SGS 4 - 09
Notes: <number>

## Slide 2: Some Thoughts on 1. Approval 2. GTR-Development
Notes: <number>

## Slide 3: 1. Approval
Notes: <number>

## Slide 4
29.07.26
Abteilung:
<number>
One of the most important Rules in Safety Technology:
Prevention is better than cure
Notes: <number>

## Slide 5
29.07.26
Abteilung:
<number>
Some experiences in the last 5 years with CNG- and LPG-vehicles in Europe:
- 6 burst incidents (Saarland-CNG, Recklinghausen-LPG, Emmendingen-LPG, Speyer-LPG, Brescia-CNG, France-CNG)
- reasons: position of PRD, LPG-tank was filled at a CNG-station, missing PRD, failing solenoid valve, too small orifice of PRD-vent line
3 crash incidents with LPG-vehicles (Rinteln, Dülmen, Thalwil-CH)
No burst of containers
Notes: Most people are frightened because of crash accidents with gas vehicles because of the risk that the container might burst.
The incidents of the last years with burst of containers show that a lack of safety of installation and quality of components might lead more often to a burst of containers.
Information of the public is very important!!!
<number>

## Slide 6
29.07.26
Abteilung:
<number>
Design, Characteristics, Compatibility, Durability
(Pressure, Temperature, Media, Acceleration, Ambient Conditions…)
II
III
IV
Component
System
I
Notes: Component:
Container, valve, PRD, filling device
Responsibility/target group: component manufacturer
System:
Gas components, safety equipment, fixation, protection devices (e.g. ventilation, temperature protection, mechanical protection, …)
Responsibility/target group: system or vehicle manufacturer
<number>

## Slide 7
Components
System
I
29.07.26
Abteilung:
<number>
III
IV
Component Safety
II
System Safety
Notes: Component Safety: design, materials, durability, pressure, temperature, media, acceleration, ambient conditions, …
System Safety: Installation and mounting, safety equipment, e.g. sensors, PRD, PRV, shut off valves, shut down system, ventilation,
Mechanical protection
Electric protection
Leak detection
Fire protection
Heat protection
<number>

## Slide 8
Components
System
I
29.07.26
Abteilung:
<number>
Design, Characteristics, Compatibility, Durability
(Pressure, Temperature, Media, Acceleration, Ambient Conditions…)
II
IV
System Safety,
Component Testing
III
System Inspection
Notes: Component testing;
e.g. cycling of container, burst test, bonfire test, etc.
System inspection:
e.g. visible inspection
Tightness test
Function/performance test – e.g. acc. OICA proposal
<number>

## Slide 9
Components
System
I
29.07.26
Abteilung:
<number>
Design, Characteristics, Compatibility, Durability
(Pressure, Temperature, Media, Acceleration, Ambient Conditions…)
II
III
Accident Prevention
IV
Limitation of Consequences
Notes: Accident Prevention, e.g.:
Suitable design, materials, etc.
Suitable equipment, e.g. safety equipment, detectors, filling interface, …
Suitable operation
Suitable maintenance
Detection of failures of safety equipment (e.g. leak sensors)
Limitation of consequences, e.g.:
Detection of system failures (e.g. leakage)
Shut off and emergency concept
Fail safe concept
Single failure concept
Excess flow valve/check valve
<number>

## Slide 10
29.07.26
Abteilung:
<number>
IV
Limitation of Consequences
Component Testing
III
System Inspection
Component Safety
II
System Safety
Components
System
I
Accident Prevention
Notes: Summary:
The GTR should contain a good balance of
Prevention measures and Measures to limit the consequences of an accident.
<number>

## Slide 11: 2. GTR-Development
Notes: <number>

## Slide 12
29.07.26
Abteilung:
<number>
I. Storage system provisions
II. Vehicle fuel system integrity provisions
III. Electric safety
DRAFT STRUCTURE of HFCV-GTR, SGS 3-10, dated 2008-05-15
Notes: Problem: which provisions shall be covered in Part I and which Part II
Both parts cover system requirements.
???
<number>

## Slide 13
29.07.26
<number>
Questions arised during GTR-Discussions:
I. Storage system provisions
1. Scope and Purpose
2. Application
3. Definitions
4. General Requirements
5. Performance Requirements
6. Test conditions and procedures
7. Annexes
components and system requirements?
Which components? Container, valve, PRD, filling device?
Who is adressed? Component manufacturer or vehicle/system manufacturer?
protection against overpressure
Potential ignition sources
Mechanical protection, …
Part I or II?
Documentation?
Functional safety/quality of ECUs?
…
Burst ratios, fire protection, …
Notes: Bisher sind Details für Prüfungen von H2-Systemen nach dem OICA-proposal erarbeitet, aber es ist noch nicht klar, was ein storage system sein soll, was es umfasst, was ein vehicle fuel system ist, etc.
Es ist noch nicht einmal klar, ob der Container überhaupt erfasst werden soll (Japan?)
Es ist nicht klar, an wen sich die Provisiosn richten: Behälter-, Ventil-, System-, Fahrzeughersteller?
Es sind störfallbegrenzende Maßnahmen vorgeschlagen, aber noch keine Basisanforderungen zur Störfallvermeidung, die zu einem sicheren System führen (Prävention) und den Stand der Technik festlegen sollen.
Es muss der Scope und die wesentlichen Maßnahmen festliegen, bevor Funktionsprüfungen an einem nicht spezifizierten System (was das Sicherheitsniveau betrifft) beschlossen werden.
<number>

## Slide 14
29.07.26
Abteilung:
<number>
Proposal: Part I: basic requirements for accident prevention for system and components
I. Storage system provisions
1. Scope and Purpose
2. Application
3. Definitions
4. General Requirements
5. Performance Requirements
6. Test conditions and procedures
7. Annexes
System and component requirements
CGH2 and LH2
H2-system excluding propulsion s. or other consumers
System, e.g. mechanical, electrical, functional r.
Components, e.g. P, T, Material, Media, function, etc.
System, e.g. overpressure/temperature, leakage, ignition sources, single failure, monitoring, vehicle integration, shut off strategy
Components (container, valve, PRD, filling device)
Documentation system
Documentation components
Notes: Aufnehmen: Systemanforderungen und Komponentenanforderungen
Trennen: Anforderungen für System – Anforderungen für Komponenten, da verschiedene Verantwortlichkeiten
Harmonisierung Tank, Hauptventil, PRD, und Fülleinrichtung bzw. Füllbedingungen: muss enthalten sein! Sonst können auch Störfall-Versuche keine Aussage über das System herstellen.
<number>

## Slide 15
29.07.26
Abteilung:
<number>
II. Vehicle fuel system integrity provisions
1. Scope and Purpose
2. Application
3. Definitions
4. General Requirements
5. Requirements and test procedures - in-use
5.1. Performance requirements
5.2. Test conditions and procedures
6. Requirements and test procedures - post crash
6.1. Performance requirements
6.2. Test conditions and procedures
7. Annexes
Proposal: Part II: requirements and test procedures for limitation of consequences
OICA-Proposal?
Further requirements,
e.g.
Visible inspection
Tightness test
Notes: Setzt Basisanforderungen an Tank und seine Absperrung voraus
<number>

## Slide 16
29.07.26
Abteilung:
<number>
III. Electric safety
1. Scope and Purpose
2. Application
3. Definitions
4. General Requirements
5. Requirements and test procedures - in-use
5.1. Performance requirements
5.2. Test conditions and procedures
6. Requirements and test procedures - post crash
6.1. Performance requirements
6.2. Test conditions and procedures
7. Annexes
ELSA
Notes: <number>