# UN/SCETDG/36/INF.55

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-sixth session

Geneva, 30 November – 9 December 2009

Item 5 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL

REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

# Amendment to ST/SG/AC.10/C.3/2009/45 - De minimis quantities of dangerous goods

# Transmitted by the expert from the United States of America

Background

1.	Regarding ST/SG/AC.10/C.3/2009/45 - “De minimis quantities of dangerous goods”, the following revised proposal is presented in response to comments received during the present session.

Proposal

2.	Amend Chapter 3.5.1 to include the following provisions:

“3.5.1.4	Excepted quantities of dangerous goods assigned to codes E1, E2, [E4, and E5] are not subject to these Regulations provided that:

(a)	The maximum quantity of material per inner packaging receptacle is limited to 1 ml for authorized liquids and gases and 1 g for authorized solids; materials;

(b)	The provisions of 3.5.2 are met, except that an intermediate packaging is not required if the inner packagings are securely packed in an outer packaging with cushioning material in such a way that, under normal conditions of transport, it cannot break, be punctured, or leak its contents; and for liquid dangerous goods, the outer packaging contains sufficient absorbent material to absorb the entire contents of the inner packagings;

(c)	The provisions of 3.5.3 are complied with; and

(d)	The aggregate quantity of dangerous goods maximum net quantity of dangerous goods per package does not exceed 100 g for solids or 100 ml for liquids and gases.”.

[(e)	The number of packages in any freight vehicle, railway freight wagon or multimodal freight container does not exceed 1 000.]

_________________