| UNITED NATIONS |  | ST |
| --- | --- | --- |
|  | Secretariat | Distr. GENERAL ST/SG/AC.10/C.3/2009/52 ST/SG/AC.10/C.4/2009/9 18 September 2009 Original: ENGLISH |

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

| Sub-Committee of Experts on the Transport of Dangerous Goods Thirty-sixth session Geneva, 30 November – 9 December 2009 Item 10 of the provisional agenda | Sub-Committee of Experts on the Globally Harmonized System of Classification and Labelling of Chemicals Eighteenth session Geneva, 9 – 11 December 2009 Item 3 of the provisional agenda |
| --- | --- |

ISSUES RELATING TO THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION AND LABELLING OF CHEMICALS (GHS)

Hazard communication issues: Pictogram for gases under pressure

Transmitted by the experts from Germany and the United Kingdom and

the European Industrial Gases Association (EIGA)

# Introduction

During the last meeting a proposal by EIGA to exempt packagings bearing a class 2 label in accordance with the Model Regulations from also bearing the GHS pictogram for gases under pressure was discussed (ST/SG/AC.10/C.4/2009/1). The proposal was not adopted but another proposal was made by the expert from Germany. The Sub-Committee of experts on the GHS (GHS Sub-Committee) invited the expert from EIGA and from Germany (and other experts interested in the subject) to present a revised proposal taking into account the comments received during the last meeting (see paragraph 31 of the report of the GHS Sub-Committee on its seventeenth session).

# Different meanings of the symbol "gas cylinder"

Under the GHS, for the purposes of supply and use, the symbol “gas cylinder” is applied to all gases under pressure regardless of their other properties such as flammability, oxidizing properties or health hazards.

For the transport of dangerous goods the symbol “gas cylinder” (gas cylinder on a green background with figure “2” in bottom corner) is applied only to non-flammable, non-toxic gases. Other gases have either a “flame” or a “scull with crossbones” as the symbol (and figure “2” in the bottom corner of the pictogram).

Examples that illustrate the assignment of pictograms under the GHS for supply and use and for the transport of dangerous goods are shown in the following table:

| Gas | GHS pictogram(s) for supply and use | TDG pictogram(s) |
| --- | --- | --- |
| Hydrogen |  |  |
| Nitrogen |  |  |
| Oxygen |  |  |
| Fluorine |  |  |
| Phosgene |  |  |

For transport a gas is indicated always by figure “2” at the bottom of the primary risk label (and only for non-flammable, non-toxic gases by the symbol "gas cylinder"). For supply and use a gas in general is indicated by a pictogram with the gas cylinder.

# General approach for the assignment of pictograms under the GHS

The GHS assigns pictograms to most categories but not to all. With regard to physical hazards no GHS-pictogram is assigned to the following hazard classes:

Explosives of division 1.5 and 1.6 and flammable gases of category 2

If the general idea was that a pictogram is not assigned only in those cases where a hazard category is considered to be "less hazardous", it could be questioned whether the pressure hazard of a gas under pressure is actually greater than for example its flammability hazard (when assigned to category 2 of flammable gases).

# Relation to transport

The approach of assigning a pictogram for the purposes of transport but not for the purposes of supply and use under the GHS is applied in other categories as well, namely for explosives of division 1.5 and 1.6.

# Proposal

Remove the pictogram "gas cylinder" for the purposes of supply and use from the GHS as shown in the following table in chapter 2.5:

Table 2.5.2: Label elements for gases under pressure

|  | Compressed gas | Liquefied gas | Refrigerated liquefied gas | Dissolved gas |
| --- | --- | --- | --- | --- |
| Symbol | No symbol Gas cylinder | No symbol Gas cylinder | No symbol Gas cylinder | No symbol Gas cylinder |
| Signal word | Warning | Warning | Warning | Warning |
| Hazard statement | Contains gas under pressure; may explode if heated | Contains gas under pressure; may explode if heated | Contains refrigerated gas; may cause cryogenic burns or injury | Contains gas under pressure; may explode if heated |

The following consequential amendments would result:

Chapter 2.5, Paragraph 2.5.4.1, Decision logic 2.5 for gases under pressure:

Replace the symbol "gas cylinder" with “No symbol” (5 times)

Annex 1, Table for Gases under pressure:

Replace the pictogram "gas cylinder" with “No pictogram” (4 times)

Annex 2, A.2.5:

Replace the symbol "gas cylinder" by "No symbol"

Annex 3, Gases under pressure:

Replace the text "Gas cylinder" by "No symbol" and remove the symbol "gas cylinder" (2 times)

# Justification

For the purposes of supply and use the message that there is a gas under pressure is conveyed by the hazard statement. The following table shows the resulting labelling elements for hazard communication (only the hazard statements for "gas under pressure" are shown in this table):

| Gas | GHS pictogram(s), signal word and hazard statement | TDG pictogram(s) |
| --- | --- | --- |
| Hydrogen |  | Danger |  |
| compressed or refrigerated liquefied | Contains gas under pressure; may explode if heated or Contains refrigerated gas; may cause cryogenic burns or injury |  |
| Nitrogen |  | Warning |  |
| compressed or refrigerated liquefied | Contains gas under pressure; may explode if heated or Contains refrigerated gas; may cause cryogenic burns or injury |  |
| Oxygen |  | Danger |  |
| compressed or refrigerated liquefied | Contains gas under pressure; may explode if heated or Contains refrigerated gas; may cause cryogenic burns or injury |  |
| Fluorine |  | Danger |  |
| compressed | Contains gas under pressure; may explode if heated |  |
| Phosgene |  | Danger |  |
| compressed | Contains gas under pressure; may explode if heated |  |

Removing the pictogram "gas cylinder" from the GHS for the purposes of supply and use would have the following advantages/consequences:

(a)	The number of pictograms to be applied is reduced;

(b)	The information about the pressure hazard is still communicated via the hazard statement;

(c)	The inconsistency with regard to the different meanings of the symbol "gas cylinder" under the GHS and TDG would be avoided;

(d)	Transport is not affected and consistency with transport is maintained all the same.

________________

# Footnotes

In accordance with ST/SG/AC.10/C.4/34, para. 31.