## Slide 1: Cost and benefits of minimum mandatory railway accessibility criteria for Persons with Reduced Mobility
Gilles Gardiol
gilles.gardiol@era.europa.eu
UNECE – 19 November 2009

## Slide 2: Foreword
The presentation is based on the cost/benefit analysis performed by AEIF, under a mandate by the European Commission, in 2004-5
The Agency « inherited » all AEIF work
Future Agency work on PRM may re-use, alter or complement any of the presented elements
06/10/2009
Interoperability Committee workshop
<number>
Notes: <number>

## Slide 3: Table of contents
Introduction on EU railway legislation & PRM TSI
Few words on the Impact Assessment (IA) performed by AEIF
Methodology for IA (reference vs project, station category)
Main parameters for the railway accessibility of PRM
Year 2005: Situation in EU27 + Norway + Switzerland
  PRM in railway traffic, PRM Stations and RST
Population trends and PRM
Stations: cost impacts, threshold for distance between 2 “PRM” stations, implementation trends over 40 years
Rolling stock: cost impacts, implementation trends over 40 years
Benefits
Conclusions
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: <number>

## Slide 4: Interoperability EU railway regulations
e.g. An emergency lighting system of sufficient intensity and duration is compulsory on trains
PRM TSI section 4.2.2.5: Vehicle access steps shall be illuminated to a minimum of 75 Lux, measured across 80 % of the width of the
step by a light placed within or immediately adjacent to it.
Impact assessment
PRM TSI case
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: Essential Requirement 2.4.1 of Annex III to Directive 2001/16/EC modified by Directive 2004/50/EC  to be replaced by reference to 2008/57/EC
<number>

## Slide 5: IA methodology
Slide <number>
UNECE - Workshop on passenger accessibility of heavy rail systems- 19 Nov. 2009
Notes: (based on PRM definition in 2001/85/EC on Buses and Coaches)
Persons with Reduced Mobility’ (PRM) means all people who have difficulty when using trains or the
associated Infrastructure. This includes the following categories :
— Wheelchair users (persons who due to infirmity or disability use a wheelchair for mobility)
— Other mobility impaired including:
— people with limb impairment;
— people with ambulant difficulties;
— people with children;
— people with heavy or bulky luggage;
— elderly people;
— pregnant women.
— Visually impaired.
— Blind people.
— Hearing impaired.
— Deaf people.
— Communication impaired (meaning persons who have difficulty in communicating or understanding
the written, or spoken language, and including foreign people with lack of knowledge of the local
language, people with communication difficulties, people with sensory, psychological and intellectual
impairments).
— People of small stature (including children).
Impairments may be long-term or temporary, and may be visible or hidden.
<number>

## Slide 6: Basic Parameters per subsystem and potential cost drivers
Passenger vehicles
Stations
— Parking facilities for PRM
— Doors and single level entrances
— Passenger routes, main walking routes (obstacle-free route)
— Floor surfaces
— Tactile information
— Guiding paths
— Glass door and wall markings
— Toilets
— Furniture
— Ticketing counter or vending machines/Information counters
— Ticket control machines
— Seats
— Wheelchair spaces (+ 2-way communication PRM-Driver/staff)
— Doors
— Lighting
— Toilet
— Clearways
— Customer information
— Height changes
— Handrails
— Wheelchair accessible sleeping accommodation
— Step position for vehicle access and egress
— Lighting
— Visual information: signposting, pictograms, dynamic information
— Spoken information
— Emergency exits, alarms
— Geometry of footbridges and subways
— Stairs
— Handrails
— Ramps, escalators, lifts, travelators
— Platform heights and offsets
— Platform widths and edges of platforms
— Ends of platforms
— Boarding aids
— Level track crossings
Slide <number>
UNECE - Workshop on passenger accessibility of heavy rail systems- 19 Nov. 2009
Notes: TSI 4.1.2.3.1: A minimum of one obstacle free route shall be provided that interconnects the following points and services
if provided:
— Stopping points for other connecting modes of transport within the station confines (for example, taxi,
bus, tram, metro, ferry etc.);
— Car parks
— Accessible entrances and exits
— Information desks
— Other information systems
— Ticketing facilities
— Customer assistance
— Waiting areas
— Left luggage facilities;
— Toilet facilities
— Platforms
<number>

## Slide 7: PRM population for the railway traffic: an attempt for EU estimates (year 2005)
29% of PRM in the EU population according
to physical
attributes
(Year 2005)
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Various sources were used: Eurostat, national sources, ...
Notes: IA Section 6.1.3
<number>

## Slide 8: Year 2005: Situation in EU27 + Norway PRM according to age category
Combining PRM age categories (<14 and > 55 years old) and PRM due to physical attributes, more than 50% of the EU population could be considered as PRM.
structure of the whole population – EU25+Norway (year 2005)
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>

## Slide 9: Year 2005: Situation in EU27 + Norway PRM due to specific situations during a journey
People with heavy luggage and/or with children
Travellers in an EU country with a different language
e.g. London
(railway traffic) | Business, school, work | Holiday, Tourism | Family, Shopping | Unknown
Italy | 46% | 23% | 31% | 
Poland | 47% | 53% |  | 
UK | 75% | 20% |  | 5%
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA Section 6.1.5.1, UK data based on one large operator
<number>

## Slide 10: PRM with high disabilities in railway traffic: few examples at national level
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
year 2004
Notes: IA Section 6.2.1
Germany: 40 000 wheel chair users, 4 trips per year each
Netherlands: WCU trips = 0,017% of the total passenger trips
<number>

## Slide 11: PRM in railway traffic: example with a city: London
Source: London Transport Report 2004
No wheel chair user on national rail
Very few using the underground/DLR
Similar statement for other PRM persons
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA Section 6.2.1
<number>

## Slide 12: Year 2005: Situation in EU27 + Norway + Switzerland
PRM stations with obstacle-free route:
21% on the whole network
43% on the TSI scope (TEN network)
very high differences across countries
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA section 6.3.2.
<number>

## Slide 13: Year 2005: Situation in EU27 + Norway + Switzerland
PRM features in RST:
Less information than for stations
PRM feature = WCU boarding device and/or a WCU toilet
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA section 6.4.3
<number>

## Slide 14: Average number of railway trips per inhabitant
Lower number of railway trips for PRM age categories  Railway trips are performed mainly with non PRM users, an age category intended to decrease from 56% to 45% of the total population between 2000 and 2050
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
PRM
PRM

## Slide 15: Population trends (based on EU15)
Evolution of EU15+Norway population – Eurostat basic scenario
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Age | 2000 | 2040
0-14 | 63 (17%) | 51 (14%)
15-54 | 210 (56%) | 165 (45%)
>55 | 102 (27%) | 148 (41%)
Total | 376 | 364
Notes: IA Section 6.1.6
<number>

## Slide 16: Impact on stations: 1 stepstation size breakdown
large : the 5% of stations carrying 50% of the passenger traffic
medium : the next 25% of stations in a country carrying 35% of the traffic
small : the remaining 70% of the stations carrying 15% of the traffic.
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Country-RUs/IMs | Stations with less than 1000 passengers per day (all entries/exits) | 
 | Number of stations | Relative share
DK – DSB | 143 | 68%
DE - DB Ag | 3475 | 69%
GB – ATOC | 1838 | 73%
IT – RFI | 1780 | 77%
BE - SNCB / NMBS | 430 | 80%
PL - PKP | 1205 | 86%
Notes: IA section 5.2.2
<number>

## Slide 17: Impact on stations: 2nd step PRM station configuration
e.g. for a middle size station:
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA section 5.2.3
Small station: 2 platforms, each one with a length of 300m
Large station: 5 platforms, each one with a length of 500m
<number>

## Slide 18: Impact on stations: Unit cost per equipment type
PH= platform height
Several solutions for the same purpose  grouping of alternatives
Notes: IA section 5.2.5
<number>

## Slide 19: Impact on stations: Average investment cost per station size
Alter-natives
Notes: IA section 5.2.6
<number>

## Slide 20: Impact on new small stations: Threshold issue for accessibility
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
For new stations: TSI section 4.2.3.1.
New stations with a throughput of less than 1 000 passengers per day (combined total of passengers embarking and disembarking) are not required to have lifts or ramps where these would otherwise be necessary to achieve full compliance with this clause if another station within 30 km on the same route provides a fully compliant obstacle-free route.
In such circumstances the design of new stations shall incorporate provision for the future installation of a lift and/or ramps to make the station accessible to all categories of PRM.
For existing stations: TSI section 7.3.1
When renewed or upgraded, existing stations that have a daily passenger flow of 1 000 passengers or less, combined embarking and disembarking, averaged over a 12 month period are not required to have lifts or ramps where these would otherwise be necessary to achieve full compliance with this clause if another station within 50 km on the same route provides a fully compliant obstacle-free route. In such circum-stances the design of stations shall incorporate provision for the future installation of a lift and/or ramps to make the station accessible to all categories of PRM.
Notes: Discussion behind the figures:
The first assumption (page 57 IA) was that 25% of the small stations were at least at 50km from a PRM station. 25% was an agreed value with experts, but no evidence for this.
The final TSI states a threshold of 30km (after discussion with social partners), which means accordingly a higher share of small stations under the scope of the TSI, so a cost impact increase. The impact of this higher value was not estimated.
<number>

## Slide 21: Impact on stations: Rates of new and upgrade stations
Annual rates for EU25+Norway
New stations: 22
Upgraded existing stations: 200
Project scenario: 50% of these stations will be under the TSI scope
Note:
From 1960 to 2000, the number of stations decreased with an annual average of 1.3% (1.1% for 1990-2000)
Rate of closure of stations for the project scenario: 1% per year
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: New stations: IA Section 8.1.2
Upgraded stations: IA Section 8.1.3
Station closure: IA Section 6.3.3.
<number>

## Slide 22: Stations implementation according to assumptions on stations renewal
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA Section 6.3.3: stations trends 1960-2000: from 41685 to 24491 (scope: 14 MS, representing 75% of the total stations)
<number>

## Slide 23: Impact on stations: Global costs impacts, EU25+NO
Annual average CAPEX and OPEX (average over 40 years)
New stations
not discounted
Total: 6 to 24 M€, per station: 0.4 to 1.7 M€
discount rate 8%
Total: 2 to 10 M€, per station: 0.2 to 0.7 M€
Upgrading of existing stations
not discounted
Total: 70 to 163M€, per station: to 0.3 to 0.7M€
discount rate 8%
Total: 28 to 70 M€, per station: 0.1 to 0.3 M€
06/10/2009
Interoperability Committee workshop
<number>
Notes: Section 9.2.3: new stations
Section 9.3.3: existing stations  mainly the small stations are impacted, therefore the average cost impact per station which is lower than the average cost impact for New stations
<number>

## Slide 24: Impact on rolling stock: Assumptions for PRM configuration in RST
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Wheelchair area impact
The wheelchair area has an impact on seat capacity. It was assumed that, in EMUs/DMUs, the 2 WCU per 4-car train are at the same location in order to allow 2 WCU to travel together and to install in this case only 1 universal toilet per train (less cost impact in this case). There are the same assumption for a loco hauled train, except that a 8-car train will carry 2 WCU.
Notes: IA section 5.3.3
<number>

## Slide 25: Impact on rolling stock: Assumptions for PRM configuration in RST
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
PRM equipment for communication :
- PIS (Passenger Information System)
- Emergency communication between WCU and onboard staff
Notes: IA section 5.3.3
<number>

## Slide 26: Rolling stock impacts: Average cost impact per vehicle
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Gap issue
Manual ramp=500€ (1 per train), OPEX=15% p.a, lifetime=10 years
Bridging plate=5000€ (2 per train), OPEX=20% p.a, lifetime=15 years
Onboard lift = 30 000€ (2 per train), OPEX = 20% p.a, lifetime = 15 years
Passenger Information System
Total=7200€ per car
visual=5700€ per car
audio=1500€ per car
Emergency communication with WCU
7500 € per WCU area
WCU toilet
no significant change in investment, but decrease seat capacity
Notes: IA section 5.3.5
See also section 10.2.1.1 which provide a good overview of the average alternative costs per car
<number>

## Slide 27: Rolling stock impact: seat capacity
06/10/2009
Interoperability Committee workshop
<number>

## Slide 28: Rolling stock impacts: Rates of new and upgraded vehicles
Total passenger cars in EU25+Norway
about 100 000 vehicles in 2004
50 000 coaches
50 000 vehicles in trainsets
Annual rate of new vehicles :
2% of existing fleet for coaches, 3% for EMU/DMU cars
-> about 2 500 new vehicles per year
Annual rate of renewal/upgrading RST :
coaches : 3 % EMU/DMU : 4 % (AEIF questionnaire)
-> about 3 000 renewed/upgraded vehicles per year
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>

## Slide 29: Rolling stock implementation according assumption rates for fleet renewal
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>

## Slide 30: Impact on rolling stock: Global costs impacts, EU25+NO
Annual average CAPEX and OPEX (average over 40 years)
New passenger rolling stock
not discounted
Total: 2 to 27 M€, per car: 1 to 11 thousand €
if onboard lift in all trains: 180M€, per car: 73 thousand€
discount rate 8%
Total: 0.7 to 8 M€, per car : 0.2 to 0.7 M€
Upgrading of existing rolling stock
not discounted
Total: 20 to 68M€, per car : to 7 to 23 thousands €
discount rate 8%
Total: 10 to 38 M€, per car : 3 to 12 thousands €
06/10/2009
Interoperability Committee workshop
<number>
Notes: Section 10.2.3: new rolling stock
Section 10.3.3: existing rolling stock
<number>

## Slide 31: Annual global impact on stations and rolling stock (EU25+NO)
1) Annual average capital and operational expenditures (over 40 years)
2) During a period of approximately 20 years (assumption: vehicles retrofit if they have not reached the middle of their lifetime)
Slide <number>
UNECE - Workshop on passenger accessibility of heavy rail systems- 19 Nov. 2009
Notes: The majority of the cost (from 50% to 75%) for both infrastructure and rolling stock is to accommodate level access for persons with walking difficulties.
<number>

## Slide 32: Benefits ? Yes, but how to quantify them ?
Very few studies focused on the quantification of new PRM travel
When such studies exist, they have general assumptions not proven, e.g.:
“We were not able to find any information regarding the previous situation of new (PRM) passengers. However it is possible to assume that 50% was made by taxi and 50% was not made at all. This change will most likely lead to a significant change in the environmental impacts of road transport.
Source: ECORYS desk research study for AEIF”
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: Section 13
13.5.3: PDFH values time differently according to where the time is spent : as waiting or walking represents, for the average passenger, a greater inconvenience than sitting more or less comfortably in a train that is riding to destination, the corresponding values of time are higher
<number>

## Slide 33: Benefits linked with the value of time
Other studies tried to quantify the impact on journey time due to increase or decrease in station accessibility and interchange time between platforms/main hall of a station
Passenger Demand Forecasting Handbook (ATOC)
“PDFH shows that stations (access, egress, interchange) are a weak spot of railway transportation, with walk and wait times valued twice a high as in-vehicle time, not to mention extra penalties due to stairs”
QUITS report (ISIS for European Commission, 1997)
“values of time for wait and walk should slightly increase (by about 30%) compared to in-vehicle time”
Their conclusions are not consistent, they were not used by AEIF.
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA section 13.5.3: PDFH values time differently according to where the time is spent : as waiting or walking represents, for the average passenger, a greater inconvenience than sitting more or less comfortably in a train that is riding to destination, the corresponding values of time are higher
IA section 13.5.6
<number>

## Slide 34: Benefits …
Note: from this source, PRM are related to physical disabilities
67.7% of the population (non PRM) do not travel by train
87.5% in case of PRM
Assumption: improvement in the railway system could equalise the behaviour of PRM and non PRM
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: IA section 6.2.1
In Italy, 67.7% of the non disable population does not use the train  32.3% of the non disable population use it.
16.5% of the disable population use the train  which kind of improvements in the railway shall be performed to get the same share of the population using the train, whatever they are disable or not ?
<number>

## Slide 35: Benefits when looking at the age of the traveller
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: Section 15.4
<number>

## Slide 36: Benefits
Very few studies quantify PRM benefits
A model to analyse the benefits should include:
The transport previously used by the “new railway-using PRM”
The impact on value of time in stations (access, egress, interchange) for all users
The demographic trends
The trends in travel propensity according to age
The trends in disability according to age
The change in PRM behaviour with an improved accessibility
...
Slide <number>
UNECE - Workshop on passenger accessibility of heavy rail systems- 19 Nov. 2009
Notes: Mention London Transport study, maybe (impact on PRM-friendliness on “normal” users...)
No other tangible elements ? (even if just details ?)
<number>

## Slide 37: Conclusion
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>
Notes: « across the EU », but within the scope indicated in the TSI (i.e. not everywhere)
<number>

## Slide 38
Thank you for your attention!
UNECE Workshop on transport accessibility - 19 Nov. 2009
Slide <number>