| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/17 17 December 2008 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-seventh session

Geneva, 10 - 13 March 2009

Item 4.2.11 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Supplement 2 to the 03 series of amendments to Regulation No. 27

(Advance warning triangle)

Submitted by the Working Party on Lighting and Light-Signalling (GRE) (/

The text reproduced below was adopted by GRE at its sixtieth session.  It is based on ECE/TRANS/WP.29/GRE/2008/31, as amended by Annex III to the report.  It is submitted to WP.29 and AC.1 for consideration (ECE/TRANS/WP.29/GRE/60, para. 22).

Insert a new paragraph 2.9., to read:

"2.9.	"Colour of the reflected/fluorescent light of the device." The definitions of the colour of the reflected/fluorescent light are given in paragraphs 2.30. and 2.32. of  Regulation No. 48."

Paragraph 7.2.1.2., amend to read:

"7.2.1.2.	When the retro-reflecting device is illuminated by the CIE standard illuminant A, with an angle of divergence of 1/3° and an illumination angle V = H = 0°, or, if this produces a colourless surface reflection, an angle V = ± 5°, H = 0°, the trichromatic co-ordinates of the red reflected luminous flux shall be within the limits according to paragraph 2.30. of Regulation No. 48."

Annex 5,

Paragraph 2.1.1., amend to read:

"2.1.1.	… within the colour limits defined in paragraph 2.30. of Regulation No. 48."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.