| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2009/79 9 April 2009 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-forty-eighth session

Geneva, 23 - 26 June 2009

Item 4.2.13 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 1 to Supplement 33 to the 03 series of amendments to Regulation No. 37

(Filament lamps of power-driven vehicles and their trailers)

Submitted by the Working Party on Lighting and Light-Signalling (/

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-first session.  It is based on GRE-61-03, not amended.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/61).

Annex 1,

The list of categories of filament lamps and their sheets, amend to read:

"…

| Group 2 |
| --- |
| Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps: |
|  | Category |  | Sheet number(s) |  |
|  | C5W |  | C5W/1 |  |
|  | H6W |  | H6W/1 |  |
|  | H10W/1 |  | H10W/1 to 2 |  |
|  | HY6W |  | H6W/1 |  |
|  | HY10W |  | H10W/1 to 2 |  |
|  | HY21W |  | H21W/1 to 2 |  |
|  | ... |  | … |  |

"

Sheet H10W/1, the table, amend to read:

"…

| Cap: | H10W/1 | BAU9s | in accordance with IEC Publication 60061 (sheet 7004-150A-1) |
| --- | --- | --- | --- |
|  | HY10W | BAUZ9s | in accordance with IEC Publication 60061 (sheet 7004-150B-1) |

…"

The new sheets H10W/1 to 2, between sheet H6W/1 and sheet H21W/1, amend to read (see next pages):

"	CATEGORIES H10W/1 AND HY10W	Sheet H10W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament lamp

| Dimensions in mm | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
|  | min. | nom. | max. |  |
| e | 14.25 | 15.0 | 15.75 | 15.0 ( 0.25 |
| Lateral deviation 1/ |  |  | 0.75 | 0.4 max |
| ß | 82.5° | 90° | 97.5° | 90° ( 5° |
| (1, (2 2/ | 30 ° |  |  | 30° min. |
| Cap: | H10W/1: | BAU9s | in accordance with IEC Publication 60061 (sheet 7004-[...]) |
|  | HY10W | BAUZ9s | in accordance with IEC Publication 60061 (sheet 7004-[...]) |
| ELECTRICAL AND PHOTOMETRIC CHARACTERISTICS |
| Rated values | Volts | 12 | 12 |
|  | Watts | 10 | 10 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 12 max. | 12 max. |
|  | Luminous flux | H10W/1 | 200 ( 12 % |  |
|  |  | HY10W | 120 ( 17 % |  |
| Reference luminous flux at approximately 13.5 V | White: 200 lm |
|  | Amber: 120 lm |

CATEGORIES H10W/1 AND HY10W	Sheet H10W/2

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	In the area between the outer legs of the angles (1 and (2, the bulb shall have no optically distorting areas and the curvature of the bulb shall have a radius not less than 50 per cent of the actual bulb diameter.

3/	Over the entire length of the cap there shall be no projections or soldering exceeding the permissible maximum diameter of the cap.

4/	The light emitted from filament lamps of normal production shall be white for category H10W/1 and amber for category HY10W.

5/	The light emitted from standard filament lamps shall be white for category H10W/1 and amber or white for category HY10W. "

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.

# Text boxes

β

H10W/1

γ1

γ2

Reference axis

Reference plane

e

28.0 max.

Ø 9.25 max.

4/, 5/

X

X

HY10W

3/