## Slide 1: Proposal of Warning Principles
<number>
November 13, 2009, Geneva
UNECE/WP29/18th ITS Informal Group
Informal document No. ITS-18-05
(18th ITS, agenda item 4.)

## Slide 2: Activities so far
Establishment of ITS Informal Group in 2002 : to consider necessity of regulatory framework in WP29
Activities in 2004-2006 :
  Common understanding of driver assistance systems
  Exchange of information and views on technology trend
Preparation of draft warning principles in 2007-2008 : to ask IHRA-ITS WG to prepare draft warning principles
Proposal by ITS Informal Group in 2009 : to provide proposal of warning principles and to suggest how to deal with this document in the next WP29
<number>

## Slide 3: Main changes from IHRA draft
Expansion of vehicle category : to apply high-priority warning principles for not only passenger cars but other vehicle categories such as trucks
Rewritten of Figure 1 : to ensure the definition of duration for high-priority warnings
Treatment of illustrated values : to treat them as reference values
Rearrangement of statement of principles : statement No.3 for spacial cues to hazard location and statement No.4 for proximity of hazard
<number>

## Slide 4: Introduction
Purpose of this document : to provide basic recommendations for the design of high-priority warnings on ADAS
  Better understanding from drivers
  Reduced confusion
  More accurate and consistent expectations
Level of warning : to focus on high-priority warnings that require the driver to take immediate action or decision to avoid crash event
<number>

## Slide 5: Driver perception-response
Rewritten of Figure 1 : to ensure the definition of duration for high-priority warning
<number>

## Slide 6: High-priority warning should be noticeable in the driving environment
Displayed at least two modalities – auditory or haptic supplemented by visual warning
Primary colour of visual warning should be mostly red
Visual warnings should be visible from the driver's normal relevant viewpoint
Auditory warnings should be enough noticeable for the driver to the signals, but not cause startle effect
Haptic warnings should be sufficiently intense so that driver can feel them during foreseeable driving situations
<number>

## Slide 7: High-priority warning should be distinguishable from other messages in the vehicle
High-priority warning messages should be clear to drivers and understood without confusion
High-priority warnings should be immediately recognizable
High-priority warning signals should be designed to avoid potential conflict
<number>

## Slide 8: High-priority warning should provide spatial cues to the hazard
High-priority warnings should inform drivers of the general direction of the hazard
High-priority warnings should not orient the driver inappropriately – away from the hazard or appropriate response options
<number>

## Slide 9: High-priority warning should inform the driver of proximity of the hazard
High-priority warnings inform about the proximity of the hazard
If possible, high-priority warnings suggest the appropriate avoidance response
High-priority warnings should be effective without in-depth training
<number>

## Slide 10: Supplement for Principle No.4 : High-priority warnings inform about the proximity of the hazard
Notice of the proximity of the hazard is more important than that of the content of the hazard in a short time
The driver should understand the content of the hazard immediately when he or she looks ahead
<number>

## Slide 11: High-priority warning should elicit timely response or decisions
Warnings should allow drivers sufficient opportunity to perform an appropriate avoidance
Timing should also account for the need to limit the occurrence of nuisance alarms – balance between providing greater protection and occurrence of false or nuisance alarms
<number>

## Slide 12: Multiple warnings should be prioritized
Prioritization should be based on the criticality and urgency ratings of the messages, and high-priority warnings are both critical and urgent
Prioritization helps to determine when, where and how system messages are delivered.
High-priority warnings should be displayed during maintaining its highest priority
<number>

## Slide 13: Supplement for Principle No.6 : Prioritization of high-priority warnings
Being hard to make ordering among high-priority warnings, all the simultaneous different high-priority warnings should be presented to the driver
<number>
The driver should prioritize hazards after he or she gets high-priority warnings
Oncoming
Vehicle
Forward
Collision
Lane
Departure
Own
vehicle

## Slide 14: False/nuisance warnings rate should be low
High-priority warnings should not be issued when the situation is not critical (avoid false alarms)
High-priority warnings should be issued when there is a hazard (avoid misses)
Adjustable warning thresholds may be used to reduce nuisance alarms
<number>

## Slide 15: System status and degraded performance of high-priority warnings should be displayed
Drivers should be informed whenever the system is malfunctioning or is performing outside of its operating conditions
Drivers should be informed whenever the high-priority warning system is off, if the system is default-on and on/off switch is provided
<number>

## Slide 16: Thank you for your attention
<number>