## Slide 1: NL Proposal for Amending Reg 51-3 Annex 3 Clarification issued by the Netherlands GRB 50; September 2009 ref: ECE/TRANS/WP.29/GRB/2009/4
Informal document No. GRB-50-05
(50th GRB, 1 – 3 September, 2009, agenda item 3.c))

## Slide 2: To avoid confusion
Our intention is to amend the coming new annex 3 of R51.03
This method is currently in force as method B in annex 10 of R51.02
After consultation of the ECE secretariat, this proposal has been forwarded as amendment based on the text of R51.02 method B
It is certainly not our intention to interfere with the running double testing period for monitoring

## Slide 3: Background of this proposal?
Following the analysis of the GRBIG ASEP expert group
Following the advice of the GRB informal group ASEP
Following the discussion in GRB 49

## Slide 4: ASEP WG: analysis stringency
Stringency in this issue means: effectiveness
and more specific
- Accuracy of the prediction model
- Capability to set meaningful demands
Outcome analysis of ASEP WG:
Recommendation to GRB: skip border 2 m/ss in Annex 3

## Slide 5: Why skipping?
2 m/s2 boundary forces vehicles to higher gears and so to low(-er) revs in the Annex 3 test situation.
Test result Annex 3 is anchor point for ASEP (revs, Lwot).
Anchor point ASEP not in balance in the middle of the map, but in the low rev area.
‘Higher area’ bigger  prediction less accurate
Prediction less accurate  ASEP less accurate
(ASEP based on a prediction model)

## Slide 6: Boundary of 2 m/s2 forces the ASEP limit line to the left
Anchor point ASEP with 2 m/s2 boundary

## Slide 7: Intention of this proposal: go back to the original anchor point (as based on urban statistics)
Anchor point ASEP
without 2 m/s2 boundary

## Slide 8: Effect of skipping the 2 m/s2 boundary
Marginal effect on Annex 3 nor on limitation annex 3 (because of Kp factor)
Positive effect for quality Annex10:
Anchor Point more in balance: moving towards the middle of the engine map
And: prediction capability more accurate

## Slide 9: Examples:
Effect of removing 2 m/s2 boundary
vehicle | PMR (kW/t) | Test result Annex 3 | Limit ASEP @ R51.02
200-14 | 166 | - 0,3 | - 5,6
200-09 | 159 | - 0,6 | - 3,3
200-06 | 141 | + 0,5 | - 3,7
200-02 | 105 | - 0,1 | - 0,4
Most vehicles in the dBase (Since they do not reach > 2 m/s2 in gear i) |  | 0 | 0

## Slide 10: END of presentation