## Slide 1: NL ASEP proposal Presentation to GRB version 01-09 issued by the Netherlands GRB 50; September 2009
Informal document No. GRB-50-14
(50th GRB, 1 – 3 September, 2009, agenda item 3.c))

## Slide 2: ASEP Working Group
A method in discussion in the ASEP Working Group
(developed and proposed by OICA)
Germany and Netherlands raised the issue of stringency of this method: weakening present limit up to 10 dB
Netherlands decided to bring in an alternative ASEP method
(ref: ECE/TRANS/WP.29/GRB/2009/5)

## Slide 3: NL proposal: summary
It is based on the following elements:
an anchor point (determined from measurements of Annex 3)
a not to exceed point (Annex 3 limit value plus a ‘value’)
above the anchor point: a straight line between the anchor point and the not to exceed point
below the anchor point: a line with a fixed slope
a bonus for silent vehicles
a margin (to allow for uncertainty of single measurements)
Essential:
Right end of limit line based on a Not To Exceed Level

## Slide 4: Comparison between NL and ADBO ASEP methods
Note ADBO = ASEP method “As Developed By OICA” in the ad hoc WG
Same in both methods:
- Area of control (marginal difference) both based on 99% of all urban driving
Anchor point (same place and value)
A margin
Bonus silent vehicles
Difference in slope below and above anchor point
Difference:
Limitation line above anchor point
Potential differences:
Value of slope below anchor point
The value of the margin

## Slide 5: Difference in limitation line above anchor point
The NL proposal is based on a NTE level (= limit Annex3 + [8] dB)
The ADBO proposal is based on a slope
- slope ADBO is based on regression
- with a maximum of X+Y dB/1000 rpm)
The maximum allowable noise:
NL = fixed (NTE level)
ADBO = depending on engine speed range and allowable slope

## Slide 6: examples
Vehicle 99-09
Pmr 65 kW/t
Vehicle 200-14
Pmr 166 kW/t

## Slide 7: Confrontation of NL method with ASEP dBase
method | number of vehicles in dBase failing the limit
R51.02 | 22%
ASEP NL | 26%
Vehicles that pass R51.02 but fail NL ASEP are:
Vehicles with non linear sound behavior, tuned to R51.02
Vehicles with extremely steep sound slope, tuned to R51.02
Border line vehicle (one)
Vehicles that fail R51.02 but pass NL ASEP are:
- Border line vehicles (all)

## Slide 8: Comparison of NL method and ADBO method
The NL ASEP proposal is able to distinguish noisy from silent vehicles and adds a certain requirement in addition to Annex 3. Especially vehicles from which the sound behavior is tuned to the current method are detected.
Normal vehicles pass the NL ASEP proposal fairly easy.
method | number of vehicles in dBase failing the limit
R51.02 | 22%
R51.03 Annex 3 (+ German limit proposal) | 13%
ASEP ADBO (+ OICA limit proposal for ASEP) | 2%
ASEP NL | 26%

## Slide 9: (super) sport cars
In the dBase we found no justification for an extra allowance compared to normal vehicles.
If there is a justification, we could discuss it

## Slide 10: NL Proposal: relation with EU monitoring
After the monitoring phase there will be an analyses, discussion and a decision about the Annex 3 limits.
The NL ASEP proposal can be fine tuned on the outcome

## Slide 11: Our Concern
Certainly not the (super)sportcars
Every new technology drops down: (Airco, ABS, ESP, Launch C. etc.)
So: also ‘Sound Design’
Sporty cars
GTI’s
Convertibles
The ‘SEAT Leons’
Every car can be sold in a silent ánd a noisy version (LEGALY)
And they will be sold:
Outside you can hear there is a customer demand

## Slide 12: THANK YOU