## Slide 1: ASEP -- Proposal for CVT --
GRB informal meeting #14
28-29 January 2009
JASIC
GRBIG-ASEP-14-006

## Slide 2
Revision of the OICA method for CVT
Definition of classical CVT
1
2

## Slide 3: Vehicle 1-10
Gear：D-range , Annex3,i : D-range
OICA proposal compensate tyre noise only at the anchor point.
There is the influence of tyre noise at every point as well as at the anchor point, because the relationship between vehicle speed and engine speed is not liner in case of CVT.
Consideration for revising the OICA proposal on D-range test for CVT

## Slide 4: Revised OICA proposal for D-range test
Vehicle 1-10
0.7 dB
Influence of tyre noise
A
B
rpm
dB
B
A
Same engine speed but different vehicle speed
Should use maximum vehicle speed within ASEP test for the calculation of the anchor point

## Slide 5: Calculation procedure for limit line
 | MT, AT & locked CVT | CVT D-range
Annex 3 test (gear i, D) | From Annex3 test results Lwoti,annex3 nBB,woti,annex3 vBB,woti,annex3 | From Annex3 test results LwotD,annex 3 nBB,wot D,annex3 vBB,wotD,annex 3
【Step-1】 Anchor point gear i | Lanchor,i = Lwoti,annex3 nanchor,i = nBB,woti,annex3 vanchor,i = vBB,woti,annex3 | 
【Step-2】 Anchor point gear k | Lanchor,k = 10 *log(10(Lwotk/10) - 10(Lcruise/10) + 10(32*log∆V+Lcruise)/10) ∆v=ik/ii (=vBB,wot k/vBB,woti,annex 3) where ik = gear ratio of the tested gear k ii = gear ratio of gear i | Lanchor,D = 10 *log(10(Lwotk/10) - 10(Lcruise/10) + 10(32*log∆V+Lcruise)/10) ∆v=vBBmax/vBB,wot D, annex 3 where vBBmax = maximun vehicle speed during ASEP test
【Step-3】 Sound Slope | Regression analysis based on measured data. | Regression analysis based on measured data.
【Step-4】 Limit Line | Lref = Lanchor,k + Slope*(nBB - nBB,wot i,annex3)/1000 + X | Lref = Lanchor,k + Slope*(nBB - nBB,wot D,annex3)/1000 + X

## Slide 6: Amendment for text
Based on the Chairman’s draft proposal,
4.1. Determination of the anchor point for each gear ratio
...................................
The sound level of the anchor point in gear k is calculated by:
Lanchor,k = 10 *log(10(Lwotk/10) - 10(Lcruise/10) + 10(32*log∆V+Lcruise)/10)
∆v=ik/ii (=vBB,wotk/vBB,woti,annex 3)
In case of vehicles with CVT's non-locked gear ratios, ∆v shall be used as follows;
∆v=vBBmax/vBB,wotD,annex 3 where vBBmax = maximun vehicle speed during ASEP test

## Slide 7: Revised OICA proposal for D-range test
Vehicle：ASEP 1-10 (original)
Vehicle：ASEP 1-10 (rev.)
Vehicle：ASEP 1-12 (original)
Vehicle：ASEP 1-12 (rev.)

## Slide 8: Revised OICA proposal for D-range test
Vehicle：ASEP 1-14 (original)
Vehicle：ASEP 1-14 (rev.)
Vehicle：ASEP 1-16 (original)
Vehicle：ASEP 1-16 (rev.)

## Slide 9: Proposal for definition of classical CVT
Both nBB on Annex3 test and on wot test
from vaa=20km/h are larger than 0.85 nBB max

## Slide 10
Typical characteristics for CVT
MT(Vehicle:107-6)
CVT(Vehicle:1-10)
Vaa=20km/h
Annex3
Annex3
Vaa=20km/h

## Slide 11
Typical characteristics for CVT
MT(Vehicle:107-6)
CVT(Vehicle:1-10)
Vaa=20km/h
Annex3
Annex3
Vaa=20km/h
-x%
(1-x/100)
nBB max
nBB max

## Slide 12
Vehicle 1-10
572 rpm
(13 %)
532 rpm
(12 %)
Range of engine speed for CVT
511 rpm
(11 %)
1005 rpm
(20 %)
Vehicle 1-12
538 rpm
(12 %)
467 rpm
(11 %)
Vehicle 1-14
225 rpm
(5%)
24 rpm
(1 %)
Vehicle 1-16

## Slide 13
Typical characteristics for CVT
MT(Vehicle:107-6)
CVT(Vehicle:1-10)
Vaa=20km/h
Annex3
Annex3
Vaa=20km/h
-15%
0.85
nBB max
nBB max
Both nBB on Annex3 test and on wot test
from vaa=20km/h are larger than 0.85 nBB max