Proposal for correction of document ECE/TRANS/WP.29/GRPE/2009/2

A. PROPOSAL FOR AMENDMENTS

Paragraph 2,

“Equation A13-4” amend to read “Equation A13-3”

“Equation A13-5” amend to read “Equation A13-4”

“Equation A13-6” amend to read “Equation A13-5”

Paragraph 4.1., amend to read: (underlined part)

“An example of input data necessary for the calculation of shift speeds is shown in table A13-1 A13-2. The upshift speeds for acceleration phases for the first gear and higher gears are calculated using equations 6-1 and 6-2.  The denormalisation of engine speeds can be performed by using the equation n = n_norm x (s – nidle) + nidle.”

Paragraph 4.2., amend to read: (underlined part)

“The downshift speeds for deceleration phases can be calculated with equations 6-3 and 6-4.  The ndv values in table A13-1 A13-2 can be used as gear ratios.  These values can also be used to calculate the affiliated vehicle speeds (vehicle shift speed in gear i = engine shift speed in gear i / ndvi).  The corresponding results are shown in tables A13-2 A13-3 and A13-3 A13-4.”

The numbering of table A13-3, amend to read: (underlined part)

Table A13-3 A13-4: Engine and vehicle shift speeds according to table A13-2

B. JUSTIFICATION

The proposal is simply to correct the typographical errors in the original document ECE/TRANS/WP29/GRPE/2009/2 as shown in the following pages.

JAPAN proposal for correction of working document for gtr No. 2 (WMTC)

Japan has noticed some numbering errors in the document ECE/TRANS/WP.29/GRPE/2009/2 which refers to the gearshift prescription for gtr No.2. (re-issued on 04.11.2008)

Japan would like to point out as following.

continued to the next page

- - - - -