## Slide 1
GRPE Session 13-16 jan 2009
GFV Group
Geneve, 13 Jan 2009
Regulation No. 115 changes

## Slide 2: Issues
This presentation tackles the following issues:
Scope
Emissions test procedure
Switch over time
Chassis dynamometer setting

## Slide 3: Scope
1.4 This Regulation applies to retrofit systems intended to be fitted on
petrol vehicles of categories M1 and N1 type-approved pursuant to Regulation No. 83, 05 and later series of amendments;
(petrol and diesel) engines for use in vehicles of categories M and N type-approved pursuant to Regulation No. 49, 04 and later series of amendments;
petrol vehicles of categories M1 and N1 type-approved pursuant to Directive 98/69/EC or later EC Directives and Regulations amending or repealing the Directive 70/220/EC;
(petrol and diesel) engines for use in vehicles of categories M and N type-approved pursuant to Directive 1999/96/EC or later EC Directives and Regulations amending or repealing the Directive 88/77/EC;
Justification
In order to avoid the long list of exclusions, Aegpl proposes to turn them into a positive description of the application field, including an explicit reference to EC Regulations and Directives.

## Slide 4: Emissions test procedure Non-intrusivity definition
6.1.2.2 In order to prove that the retrofit system is "non intrusive", as defined in paragraph 2.1.5., the system manufacturer shall provide data and/or engineering evaluations which adequately demonstrate that the performance of original air and petrol feed system to the engine are not affected by the installation of the retrofit system. For the approval of a retrofit system as “non-intrusive”, the flow chart provided in figure 1 shall apply.
Justification
AEGPL is firmly convinced that the “non-intrusive” concept should be kept because there are systems that, by design, do not affect the original emission performance of the cars.
In other words, their mechanical components and electric/electronic devices are designed also with the view to avoiding any disturb to the original petrol cars components and devices.
However, in order to prevent any misinterpretation and to ensure an harmonized approach by all TAA, AEGPL proposes to improve the non-intrusivity definition and, hence, the related characterization assessment.

## Slide 5: Emissions test procedure Non-intrusivity assessment
NON INTRUSIVE
YES
YES
NO
The installation of the retrofit system produces an important restriction of the section of any air inlet pipes
or
The length of any air inlet pipes has been substantially increased
INTRUSIVE
The technical documentation provided by the retrofit system manufacturer (data, calculations, tests results ..) is sufficient to prove that the retrofit system installation has not affected significantly the fluidynamic properties of the air/petrol feeding system
The technical documentation provided by the retrofit system manufacturer (data, calculations, tests results ..) about the electrical/electronic devices of the retrofit system is sufficient to prove that the system does not affect the electrical/electronic characteristics of the air/petrol feeding system
Witnessed power and/or emission tests demonstrate that the parent vehicle performances on petrol are almost the same with or without the retrofit system
Further data and/or tests required by the type-approval are sufficient to prove that the retrofit system does not affect significantly the fluidynamic properties and the electrical/electronic characteristics of the air/petrol feeding system.
NO
INTRUSIVE
NON INTRUSIVE
NO
NO
NO
NON INTRUSIVE
YES
YES
YES
Figure 1
NON-INTRUSIVE RETROFIT SYSTEM APPROVAL – FLOW CHART

## Slide 6: Emissions test procedure Petrol tests
6.1.2.5.1.3. Subject to the requirements of paragraph 6.1.2.5.1.5. the tests shall be repeated three times with the reference petrol. The test vehicle(s) equipped with the retrofit system, shall comply with the limit values according to the type approval of the vehicle(s) including the deterioration factors applied during the type approval of the vehicle(s).
6.1.2.5.1.4 Notwithstanding the requirements of paragraph 6.1.2.5.1.3., for each pollutant or combination of pollutants, one of the three test results may exceed, by not more than 10 per cent, the limit prescribed, provided the arithmetical mean of the three results is below the prescribed limit. Where the prescribed limits are exceeded for more than one pollutant, it is immaterial whether this occurs in the same test or in different tests.
6.1.2.5.1.5. The number of emission tests prescribed in paragraph 6.1.2.5.1.3. can be reduced in the conditions hereinafter defined:
- only one test is performed if the result obtained for each pollutant subject to limitation is less than or equal to 0.7 the emission limit (i.e. V1  0.70 G);
- only two tests are performed if, for each pollutant subject to limitation the following requirements are met:
V1  O.85 G and V1 + V2  1.70 G and V2  G
where:
V1: value of the emission of one pollutant obtained from the first test of the Type I performed;
V 2: value of the emission of one pollutant obtained from the second test of the Type I performed;
G: limit value of the emissions of one pollutant (CO/HC/NOx) according to the type approval of the vehicle(s) divided by the deterioration factors.
Notwithstanding the requirements of paragraphs 6.1.2.5.1.2 and 6.1.2.5.1.3, the mono-fuel vehicle may be tested with the reference petrol before the retrofit if tests after the installation of the retrofit system are not possible or may result in false results. The total vehicle mileage between the tests before and after retrofit shall not exceed [200] km.

## Slide 7: Emissions test procedure Petrol tests
Justification
The present procedures both for petrol and LPG tests are more stringent than that required by Regulation No. 83, 05 series of amendments, as fixed in paragraph 5.3.1.4. and in the related Figure 1.
In line with the statement of doc GFV-02-04 regarding the level of stringency of Regulation No 115: “It is not justified that Regulation 115 should be more restrictive than Regulation 49”, AEGPL agrees that “It is not justified that Regulation 115 should be more restrictive than Regulation 83”
An opposite approach would go well beyond the scope of Regulation N. 115 that – as any other environmental type-approval mandatory scheme – should aim at verifying minimum requirements whose compliance finally allow the sales and the use of the addressed products.
The type-approval pursuant to R. 115 doesn’t grant any economic incentive (nor automatically neither indirectly): environmental national incentives are usually designed for specific tasks, based on different environmental needs (PM in some areas, benzene or NOx in others and so on), even not covered by the Regulation 115.
Furthermore, the reasons of the LPG retrofit system purchase can be different from the environmental ones (economic, for instance) and a type-approval Regulation is not permitted to influence it beyond its scope

## Slide 8: Emissions test procedure LPG tests
6.1.2.5.1.4.2. Notwithstanding the requirements of paragraph 6.1.2.5.1.4.3., for each pollutant or combination of pollutants, one of the three test results may exceed, by not more than 10 per cent, the limit prescribed, provided the arithmetical mean of the three results is below the prescribed limit. Where the prescribed limits are exceeded for more than one pollutant, it is immaterial whether this occurs in the same test or in different tests.
Justification
The proposal aims at ensuring an alignment of the present procedure with the procedure of par. 5.3.1.4. of Regulation No. 83, 05 series of amendments. (see also justification to par. 6.1.2.5.1.5.)

## Slide 9: Emissions test procedure Flow Chart
INTRUSIVE
NON-INTRUSIVE
(See par. 6.1.2.5.1.4.)
NON-INTRUSIVITY
Characterization Tests
Par. 6.1.2.2. (see also Flow Chart - Figure 1)
Petrol tests
Type 1 test
Vehicles equipped with the retrofit system
Par. 6.1.2.5.1.3. equal to Reg. No. 83, par. 5.3.1.4. (see also related Flow Chart – Figure 1)
LPG Test
Type 1 Test
Vehicles equipped with the retrofit system
Par. 6.1.2.5.1.4.1. equal to Reg. No. 83, par. 5.3.1.4. (see also related Flow Chart – Figure 1)
YES
NOT APPROVED
APPROVED
NO
YES
NO
FIRST APPROVAL

## Slide 10: Emissions test procedure Flow Chart
NEXT APPROVALS
INTRUSIVE
NON-INTRUSIVE
Petrol Tests
Type 1 test
Vehicles equipped with the retrofit system
Par. 6.1.2.5.1.3. equal to Reg. No. 83, par. 5.3.1.4. (see also related Flow Chart – Figure 1)
LPG Tests
Type 1 Test
Vehicles equipped with the retrofit system
Par. 6.1.2.5.1.4.1. equal to Reg. No. 83, par. 5.3.1.4. (see also related Flow Chart – Figure 1)
LPG Tests
Type 1 Test
Vehicles equipped with the retrofit system
Par. 6.1.2.5.1.4.1. equal to Reg. No. 83, par. 5.3.1.4. (see also related Flow Chart – Figure 1)
YES
NOT APPROVED
APPROVED
YES
NO
APPROVED
NOT APPROVED
YES
NO

## Slide 11: Functioning on petrol – max time
6.1.2.5.1.4.1
……………………………..
If the parent vehicle(s) complies with Regulation No. 83, 05 series of amendments, or with Directive 98/69/EC, or with Regulation No. 49, 04 series of amendments, or with Directive 1999/96/EC, during the type 1 test the vehicle shall only use petrol for a maximum of 90 seconds when operating in gas mode. In the other cases, this period shall not exceed 60 seconds.
Justification
Aegpl agrees to set a maximum timeframe for the functioning on petrol when operating on gas.
This will prevent any gas system from eluding the emission requirements on gas.
As demonstrated in the GFV-02-04, if the switching over petrol is prolonged for most part of the test cycle, the emission on gas are allowed to be even worse than the limits when theoretically extrapolated to the entire cycle.
In other words, during gas feeding time the system can “consume” the “emission gain” accumulated in the petrol functioning, and this could happen for the vast majority of cars as, on petrol, these normally perform rather above the limits.
On the other hand, a right limitation should not imply a worse emission behavior of the car and should, on the contrary, permit a positive synergy between the two fuels.
The proposed timeframes permit - both on LPG and on CNG - to reduce the emissions leaving petrol sharply warp up the catalyst to a temperature suitable to ensuring the highest efficiency for the propane and methane oxidation.
The same arguments were brought to the attention of the European Commission and of the other experts of MVEG when the limit of 60sec was decided for Euro 5/6 cars in the Regulation (CE) 692/2008.
So, our proposal is in line with what was already established for cars native on gas, for which a different design option in the engine/catalyst system could even be taken in order to minimize the activation time of the catalyst for those specific hydrocarbons.
In the end, it worth being highlighted that, within foresaid maximum limit, the system manufacturer will be led to minimize the functioning on petrol as to get the best result in CO2 emission for the specific application, when possible.

## Slide 12: Chassis dynamometer setting
Justification
The next table show the cumulative positive brake power (CPBP for here on) of the vehicle (Pegeout 207 1250kg) calculated for both fuels (additional weight: LPG 60kg, CNG 160kg):
 | CNG |  | LPG |  | 
CASE A | 3067 | 100 | 2935 | 100 | coast-down from manufacturer before retrofit with f0 corrected; corresponding ECE inertia + gas system weight
CASE B | 3336 | 109 | 3336 | 114 | ECE table values before retrofit; corresponding ECE inertia
CASE C | 3548 | 116 | 3415 | 116 | ECE table values before retrofit with f0 corrected; corresponding ECE inertia + gas system weight
CASE D | 3873 | 126 | 3649 | 124 | ECE table values of one (LPG) or two (CNG) ref. class above; corresponding ECE inertia of one (LPG) or two (CNG) ref. class above
The case A is to be considered the “real case” because it is based on coast-down of the original car whereas only the rolling resistance have been upgraded linearly according to the new mass of the vehicle.
In facts, since the installation of the retrofit system doesn’t affect the original shape of the car, the other coefficients (speed-related) have been left unchanged.
The conclusions are:
  the use of table values corresponding to the vehicle before the retrofit corrected with the additional weight or the use of the table values for the next higher reference mass class would significantly overestimate the influence of the added weight;
  when available, the use of coast-down corresponding to the vehicle before the retrofit corrected with the additional weight would represent the “real case”.
  if coast-down coefficients are not available, the use of table values corresponding to the vehicle before the retrofit slightly overestimate the influence of the added weight but represents the only possible choice.
We must know however that option A is not possible on chassis dynamometers that use a set of flywheels to simulate the vehicle inertia since it is often only possible to select the legislated inertia values. If so, the table values corresponding to the vehicle before the retrofit will apply.

## Slide 13: Chassis dynamometer setting
6.1.2.5.1.2. Setting of the dynamometer
  Using of coast-down factors/coefficients of the original vehicle:
  In case coast-down coefficients of the original vehicle are known, the following conditions shall apply:
  the parent vehicle mass shall be measured with the retrofit system installed on the vehicle including the LPG tank fully filled up or shall be calculated as the sum of the original vehicle reference mass and the mass of the retrofit system with the LPG tank fully filled up;
  the rolling resistance of the parent vehicle shall correspond to the original vehicle value proportionally adjusted to the parent vehicle mass measured or calculated as above:
    f0 correction formula: f0' = f0 + (abs(f0))*(p/m)
    where
    m=reference mass of the original parent vehicle;
    p= retrofit system mass;
  the other coefficients of the resistance of the parent vehicle shall be equal to that of the original vehicle.
  Using of the table values:
  The setting of the dynamometer shall comply with requirements of Regulation 83 according to the reference mass of the original vehicle.
  In both cases, the approval granted is valid also for any retrofit system that implies vehicle’s different reference mass requiring the use of the next two higher equivalent inertia categories or any lower equivalent inertia category.