## Slide 1: ADVANCED Driver Assistance Products for Commercial Vehicles (CV‘s) Focus AEBS Wilfried Mehr, 25.06.2009, Paris
AEBS/LDWS-01-08
Notes: <number>

## Slide 2: Current applications in the market:
8
6
5
4
3
2
1
0
Camera
Long Range
Radar
Short Range Radar
ACC
AEBS
LDW
BSD
Continental = 10 years market experience on the road
Notes: <number>

## Slide 3: Driver Assistance - “makes sense”

## Slide 4: The sensor portfolio is ready for AEBS and LDW
Radar
Camera
Technique
• 24 GHz UWB Radar / short range
Applications
• Lane Change Assist (LCA type 1)
Technique
• CMOS Camera
Applications
• LDW
• Object Detection
• Speed Limit Monitoring
Intelligent Headlamp control
Technique
• 77 GHz long-range Radar
Applications
• ACC + Stop&Go
AEBS (Advanced emergency breaking system)

## Slide 5: Radar for AEBS is mature and available in the third generation – approved by billions of Km on the road
2nd. generation ARS200
On the road since 2003
3 beams, 9° field of view, 150m
Mechanical alignment
ACC
AEBS
Third generation ARS300
On the road since march 2009
17 beams, 56° field of view, 60m
17 beams, 17° field of view, 200m
auto alignment by software
ACC + Stop&Go
AEBS

## Slide 6: The nature of AEBS in CV‘s
Due to the weight of CV‘s any collision becomes fatal. Sensors therefore must….
..classify a potential collision as fast and early as possible. Means….
..to detect objects as early as possible
..to classify relevant objects as fast as possible
..to measure range, speed and acceleration as best as possible
Range 200m
High sensitivity under all weather conditions
>50° field of view
High lateral resolution
Extended driving path prediction by stationary and moving objects
Range- and speed-measurement in one cycle.
Apply “Doppler – Effect” to achieve higher precision of the speed measurement

## Slide 7: Conclusion: The sensors are ready for the legislation
Sensors for AEBS and LDW-Systems are available in a very mature status and tested over billions of Km on the road.
The environment sensor for an AEBS must have a certain performance to support a adequate functionality – Reduced specifications would question the benefit of an AEBS.
We are ready for
Vision Zero!