## Slide 1
New EU Regulation on General Safety Implementation of Tyre Aspects
Presentation to joint GRB/GRRF meeting.
Working Paper No. STD-01-03
1st STD meeting, 23 July 2009,
agenda item 2

## Slide 2: Overview
Background.
What was agreed in the GSR Co- decision Process.
What remains to be done.

## Slide 3: Background
Current EU type approval standards for tyres contained in Directive 92/23/EEC (similar to UNECE Regulations 30 and 54).
Directive 2001/43 added rolling noise limits.
UNECE Regulation 117 copied 2001/43 noise limits and subsequently added new wet grip requirements.

## Slide 4: Background
As part of agreement which led to 2001/43, Commission was asked to consider more ambitious noise limits.
Also, in order to meet CO2 emission targets it was decided to introduce tyre rolling resistance limit values.
Both of the above needed to be achieved without sacrificing safety (wet grip performance)

## Slide 5: Background
Instead of revising the existing 92/23 Directive, it was decided to put the essential tyre provisions) into the new ‘General Safety Regulation’ (GSR).
The main political aspects of the GSR would be agreed by European Parliament and Council (co-decision).
Technical aspects would, where possible, refer to UNECE Regulations.

## Slide 6: Progress of Co-Decision Procedure
Proposal published May 2008.
Parliament 1st reading agreement March 2009.
Council Adoption June 2009.

## Slide 7: Summary of GSR Requirements on Tyres
General tyre requirements to refer to UNECE Regs 30 and 54.
Reduction in noise limits - by average of 4 db (A).
New limits on rolling resistance
New wet grip requirements.
Tyre Pressure Monitoring Systems to be mandatory for cars.

## Slide 8: Tyre noise proposals (C1 tyres)
Tyre class | Limit value db(A) |  | 
 | old | new | difference
C1A (≤ 185mm) | 72-74 | 70 | 2-4
C1B (185-215mm) | 75 | 71 | 4
C1C (215-245mm) | 76 | 71 | 5
C1D (245-275mm) | 76 | 72 | 4
C1E (> 275mm) | 76 | 74 | 2
Additional 1 db(A) allowed for snow or extra load tyres
Old/new values not exactly comparable since tyre width categories have changed
Notes: The difference may be greater than that indicated in the final column since the category boundaries have changed slightly

## Slide 9: Tyre noise proposals (C2 and C3)
Tyre class | Limit value db(A) |  | 
 | old | new | difference
C2 | 75 | 72 | 3
C2 snow | 77 | 73 | 4
C2 traction snow traction | N/A | 73 75 | 
C2 special | 78 | 74 (75 for traction) | 3-4
C3 | 76 | 73 | 3
C3 snow | 78 | 74 | 4
C3 traction snow traction | N/A | 75 76 | 
C3 special | 79 | 75 (77 for traction) | 2-4
Notes: The difference may be greater than that indicated in the final column since the category boundaries have changed slightly

## Slide 10: Tyre Rolling Resistance
New limits on rolling resistance introduced for the first time.
Limits to apply in two stages, from 2012 and 2016 (new types).
CO2 reduction contribution of around 3.9 g/km for typical car.

## Slide 11: Tyre Rolling Resistance
Proposed values based on ‘state of art’ in 2004.
56% of summer tyres in 2004 could meet proposed Phase 1 requirements; 16% could meet proposed phase 2 requirements.
26% of winter tyres in 2004 could meet proposed Phase 1 requirements; 3% could meet proposed phase 2 requirements.

## Slide 12: Tyre Rolling Resistance
Further encouragement to improve rolling resistance could be achieved by labelling scheme.
This is the subject of a separate Commission initiative.

## Slide 13: Tyre Rolling Resistance
Tyre category | Max. Rolling Resistance (Kg/Tonne) | 
 | Stage 1 | Stage 2
C1 | 12 | 10.5
C2 | 10.5 | 9
C3 | 8 | 6.5
Notes: C1 = car tyres, C2 =light commercial tyres, C3 =heavy commercial tyres

## Slide 14: Tyre wet grip requirements
Introduced to ensure that safety standards are maintained.
Identical to the current requirements in UNECE Regulation 117.
Mandatory for new C1 tyre types from 2012 and existing types from 2014.
Intention is to extend requirements to C2 and C3 tyres when standards are finalised.

## Slide 15: Implementation (tyre requirements)
Item | new types | existing types*
Rolling resistance –P1) | 2012** | 2014 (2016 for C3 tyres)
Rolling resistance-P2) | 2016** | 2018 (2020 for C3 tyres)
Rolling noise | 2012** | 2016
*30 month sell-off period allowed
**One year later for vehicle installation requirements

## Slide 16: Points of Concern for Parliament
Parliament would only allow extra allowances for non-standard tyres (snow, traction, special , extra-load) if these categories were precisely defined.
Since we will be referring to UNECE Regulations, it is necessary to agree such changes at UNECE level.

## Slide 17: Other Outstanding Issues
Current Timetable allows sell-off period of 30 months after last production date. Parliament requested cost-benefit study to see if this could be reduced.
Clarification required on whether 1kg/tonne RR allowance for snow tyres applies to both phase 1 and phase 2.

## Slide 18: What remains to be done?

## Slide 19: Issues for Discussion at GRB/GRRF
Tyre definitions (R30, 54, 117)
Rolling resistance test methods (R117)
New noise limit values (R117)

## Slide 20: Tyre Definitions
To cover snow tyres, traction tyres, special use tyres, extra load tyres and professional off-road tyres
Definitions to be precise and based on physical and/or performance requirements
Definitions agreed for R117 should also be transferred into R30 and R54

## Slide 21: Rolling Resistance Test Methods
Use of ISO standards
Need to be repeatable and reproducible for use in a Type Approval environment.

## Slide 22: New noise limit values
New ‘phase 2’ values need to be compatible with values in GSR
Accept that some Contracting Parties may wish to stay with Phase 1 for the time being – Regulation should allow for this.

## Slide 23: Proposed Timetable
Initial agreement at September GRB/GRRF meetings.
Adoption at March 2010 WP29 (with possibility of final review at February GRB/GRRF sessions)

## Slide 24
Enterprise and Industry Directorate General
European Commission
THANK YOU
for your attention