## Slide 1: Informal Joint Working Group of GRB and GRRF
Geneva 16-17 November 2009
3rd STD meeting
STD-03-04

## Slide 2: Use of RR coefficient value
Regulation on CO²
  692/2008 (Euro 5 & Euro 6)
    Annex I appendix 3 § 6.6.1 (Ref. to ISO 28580)
    Annex III § 3.5 (Ref. to ISO 28580)
    Annex XVIII § 6.6.1 (Ref. to ISO 28580)
    Annex XIX § 6.6.1 (Ref. to ISO 28580)
  R101 draft amendment ECE/TRANS/WP.29/2009/76
    Annex 6 § 1.3.5 (Ref. to ISO 28580)
Regulation Labelling of Tyres
  ST14024/09 - 2009/10/02&05
    Annex I Parts A (Ref. to R117)
GSR
  661/2009
    Annex II Parts B (Ref. to ISO 28580)

## Slide 3: France proposal
Make only reference to R117 and not ISO
  Comitology ?
In amendment of R117-Rev1
  Only test methodology in the main text of R117 as in other regulations
If needed
  Annex 8 on Interlaboratory comparison procedure (informative)
  Annex 9 on alignment procedure (informative)
In justification document
  GRFF sub-group : TSG (Technical Services Group)

## Slide 4: DIFFERENCES ISO / FRENCH PROPOSAL
ISO requests a reference laboratory:
  Proposal: The 1958 agreements recognizes the Technical Services as equivalents, then no leadership can exist.
  For this reason we suggest to refer (if needed) to assigned consensus values agreed by the Technical Services through an interlaboratory comparison.
ISO defines four methods for measuring the rolling resistance:
  Proposal: No change.
ISO defines the characteristics of the machine:
  Proposal: No change, nevertheless the load values for measuring the parasitic losses have to be confirmed.
ISO defines the test conditions:
  Proposal: No change

## Slide 5: DIFFERENCES ISO/FRENCH PROPOSAL
ISO has a requirement on the « reproducibility » for the reference laboratory and another for the candidate laboratory:
Proposal: Only one value is kept σm = 0.075 for passenger car and 0.06 for larger trucks and buses tyres.
ISO requests a number of measurements more than 1 if the reproducibility value is not fulfilled :
Proposal: No change
ISO defines a method of alignment between the reference laboratory and a candidate laboratory:
Proposal: No technical changes except:
  Interlaboratory comparison and alignment procedure in informative annexes of R117
  The reference laboratory is replaced by reference to assigned consensus values agreed by the Technical Services through an interlaboratory comparison.
  The number of tyres could be higher [at least 2] in order to cover a large range of rolling resistance coefficients including some « steady » tyres used for monitoring the drift of the machine.
Note: This alignment method can also be used to align a candidate laboratory to any Technical Service.

## Slide 6: Annex 8 (informative) Interlaboratories tests

## Slide 7: France proposal
Principle
MS1 MS2 MS3 MS4 ….
Technical
Service 1
Technical
Service 2
Technical
Service 3
Technical
Service 4
appoints
Inter-laboratory comparison (TSG)
assigned (reference) values
Open Questions : Criteria and procedures for assigned reference value definition,
organization and funding, new entrants: => TSG organisation by GR
Alignment if needed
If needed

## Slide 8: Output from interlaboratory comparison
From ISO 5725
  Trueness analysis
  Precision analysis
If needed for application of annex 9
  Assigned (reference) values for each reference tyre based on general average of Technical Service results for this reference tyre

## Slide 9: Annex 9 (informative) Alignment procedure

## Slide 10: Alignment Process
1st step: Determination of the assigned values:
  Each Technical Service measures similar set of tyres covering the range of rolling resistance coefficients.
  The «general average » of rolling resistance of each tyre becomes the assigned value for this tyre.
2d step: Alignment (if needed) of each Technical Service:
  A linear regression is performed from the measured values by the Technical Service versus the assigned values as following :

## Slide 11: Alignment Process
CR TSi
CRa TS
(y, x) = (RR( TSi, Tym), RR(TS, Tym))
CR1aTy1
Assigned values
CR2aTy2
CR3aTy3
CR4aTy4
CR4aTy4
CR3aTy3
CR2aTy2
CR1aTy1
Measured values
Technical Service alignment
CR TSi = A1 CRa TS + B1

## Slide 12: France proposal
Principle
MS1 MS2 MS3 MS4 ….
Technical
Service 1
Technical
Service 2
Technical
Service 3
Technical
Service 4
appoints
assigned (reference) values
Machine A Machine B Machine C Machine D ….
alignment
alignment
If needed

## Slide 13: Alignement Process
3rd step: Determination of the linear regression between a candidate laboratory and a Technical Service.
- Both the candidate laboratory and the Technical Service measure a set of tyres and a linear regression is performed from the measured values.

## Slide 14: Alignement Process
CR candidate
CR TSi
(y, x) = (RR( CDT, Tyn), RR(TSi, Tyn))
CR1Ty1
Measured values
CR2Ty2
CR3Ty3
CRaTy4
CR4T’y4
CR3T’y3
CR2T’y2
CR1T’y1
Measured values
Candidate laboratory measurements versus Technical Service measurements.
CR CDT = A2 CR TSi+ B2

## Slide 15: Alignment Process
4th step: Alignment of the candidate laboratory:
From the 2d Step, the relationship between one Technical Service and the reference assigned consensus values agreed by the Technical Services through an interlaboratory comparison is:
CR TSi = A1 CRa TS + B1
From the 3rd Step, the relationship between one Technical Service and the a candidate laboratory is:
CR CDT = A2 CR TSi+ B2
Then the final relationship between the candidate laboratory and the reference assigned consensus values is:
CR CDT= A2 (A1 CRa TS + B1) + B2 = A CRa TS + B