## Slide 1: Performance as Test Procedures of the PDB and ODB Tests for the Light and Heavy Cars
5th Meeting of the Informal Group on Frontal Impact
<number>
May 25, 2009
JAPAN
Informal document No. GRSP-45-16
(45th GRSP, 25-29 May 2009
agenda item 16(a))
Notes: <number>

## Slide 2: Objective
<number>
  To examine effects on light and heavy cars when the test conditions prescribed in ECE R94 are replaced by PDB test.
Notes: <number>

## Slide 3: Test Matrix
<number>
Test Vehicles | Mini-Car A |  | Mini-Car B |  |  |  | Minivan |  | Passenger Car | 
Test Conditions | 60PDB | 64ODB* | 60PDB | 64ODB* | 56ODB (ECE R94) | 50CTC | 60PDB | 64ODB* | 64ODB* | 50CTC
Test Weight (kg) | 1144 |  | 1120 |  |  |  | 2110 |  | 1313 | 
Dummies (DR&PA) | H3 50% Male |  | H3 50% Male |  |  |  | H3 50% Male |  | H3 50% Male | 
* Conducted in JNCAP
60PDB: PDB barrier - 60km/h - 50% overlap - 150mm ground clearance
64ODB: EEVC barrier - 64km/h - 40% overlap - 200mm ground clearance
56ODB: EEVC barrier - 56km/h - 40% overlap - 200mm ground clearance
50CTC: Mini-Car B vs Passenger Car - 50km/h - 50% overlap
Notes: <number>

## Slide 4: Test Vehicles
<number>
Mini-Car A
Mini-Car B
Front Rail and Bumper Cross Beam
Front Rail and Lower Cross Beam (w/o Bumper Cross Beam)
Notes: <number>

## Slide 5: Test Vehicles
<number>
Passenger Car
Minivan
Front Rail, Bumper Cross Beam, and Sub-Frame
Front Rail and Bumper Cross Beam
Notes: <number>

## Slide 6: Geometory Conditions
<number>
Mini-Car B vs Passenger Car
83 mm overlap
110 mm
Mini-Car B's Front Rail
Upper: 495 mm, Lower: 311 mm
Passenger Car's Front Rail
Upper: 523 mm, Lower: 412 mm
26 mm
Rail (CTR) to Rail (CTR): 110mm
Rail (Inside) to Rail (Inside): 26mm
Passenger car
Mini-Car B
Passenger car
Mini-Car B
Notes: <number>

## Slide 7: Barrier Deformation
<number>
Mini-Car A
60PDB
64ODB (EEVC Barrier)
The front plate broke wide open.
The lower part of the honeycomb bottomed out completely.
Notes: <number>

## Slide 8: Vehicle Deformation
<number>
Mini-Car A
60PDB
64ODB (EEVC Barrier)
The front rail was rarely deformed.
The bumper cross beam was bent significantly.
The front rail was deformed.
Notes: <number>

## Slide 9: Vehicle Deformation
<number>
Mini-Car A
In both 60PDB and 64ODB, the front rail front-end was deformed to the right of the vehicle.
In 60PDB, due to the part of the front rail left undeformed, the deformation of the bumper cross beam was larger around its center.
In 64ODB, the front rail was deformed in the axial direction, and the deformation of the bumper cross beam was larger at its right outer edge.
60PDB
Right
Left
Rear
Front
64ODB (EEVC Barrier)
Notes: <number>

## Slide 10: Barrier Deformation
<number>
Mini-Car B
60PDB
64ODB (EEVC Barrier)
56ODB (EEVC Barrier)
The front plate broke wide open.
The lower part of the honeycomb bottomed out completely.
The lower part of the honeycomb bottomed out.
Notes: <number>

## Slide 11: Vehicle Deformation
<number>
Mini-Car B
60PDB
50CTC
64ODB (EEVC Barrier)
56ODB (EEVC Barrier)
The front rail was rarely deformed.
The lower cross beam was bent significantly.
The front rail was deformed.
The front rail was deformed.
The front rail was deformed.
Notes: <number>

## Slide 12: Vehicle Deformation
<number>
Mini-Car B
60PDB
64ODB
56ODB
64ODB and 50CTC showed similar deformation modes.
While the deformation in 56ODB was smaller than 64ODB and 50CTC, its deformation mode was similar to theirs.
Only 60PDB showed the deformation mode that differed from the other three tests: The front rail was not deformed in the axial direction, and its front-end was deformed to the outside of the vehicle.
50CTC
Right
Left
Front
Rear
Notes: <number>

## Slide 13: Barrier Deformation
<number>
<number>
Minivan
60PDB
64ODB (EEVC Barrier)
The front plate broke wide open.
Deformation reached the right edge of the barrier.
The honeycomb bottomed out completely.
Notes: <number>

## Slide 14: Vehicle Deformation
<number>
Minivan
60PDB
64ODB (EEVC Barrier)
The front rail was slightly deformed; only its end was deformed downward.
The sub-frame was bent significantly.
The front rail was deformed.
Notes: <number>

## Slide 15: Vehicle Deformation
<number>
Minivan
60PDB
64ODB (EEVC Barrier)
In both 60PDB and 64ODB, the front rail front-end was deformed to the right of the vehicle.
In 60PDB, due to the part of the front rail left undeformed, the deformation of the bumper cross beam was larger around its center.
In 64ODB, the front rail was deformed in the axial direction, and the deformation of the bumper cross beam was larger at its right outer edge.
Right
Left
Rear
Front
Notes: <number>

## Slide 16: Dummy Injury Criteria
<number>
Mini-Car A
Driver
Passenger
60PDB showed a slightly higher HIC, while 64ODB showed a slightly higher Head Gs.
No significant difference was observed between the two tests for Neck, Chest, and Legs.
The criteria were sufficiently met for all injury indices.
64ODB showed higher levels for Head and Neck.
No significant difference was observed between the two tests for Chest and Legs.
The Head Gs criterion was exceeded in both tests.
Notes: <number>

## Slide 17: Dummy Injury Criteria
<number>
Mini-Car B
Driver
Passenger
The Head injury level became lower in the order of 60PDB, 64ODB, 56ODB, and 50CTC.
Neck injury level was almost same between 60PDB and 50CTC.
No significant difference was observed among 60PDB, 64ODB, and 50CTC for Chest and Legs.
The criteria were sufficiently met for all injury indices.
60PDB showed the highest level for Head.
Neck injury level was approximately same between 64ODB and 50CTC.
No significant difference was observed among the four tests for Chest and Legs.
The criteria were sufficiently met for all injury indices.
Notes: <number>

## Slide 18: Dummy Injury Criteria
<number>
Minivan
Driver
Passenger
Overall, injury levels tended to be lower in 60PDB, though no significant difference was observed.
The criteria were sufficiently met for all injury indices.
No significant difference was observed between the two tests for any injury index.
The criteria were sufficiently met for all injury indices.
Notes: <number>

## Slide 19: Summary
<number>
  The bottom-out of the EEVC barrier was observed with the mini-car even under the 56ODB conditions (the current ECE R94).
  No bottom-out of the PDB was observed, even in the crash with Minivan (heavy car, 2,110 kg). However, the front rail of Mini-Cars and Minivan stuck into the PDB, deforming its front block significantly (causing its front plate to break wide open).
  In Mini-Car B, the mode of the vehicle deformation was similar between ODB and CTC, but only mode of the vehicle deformation in PDB was different.
  Significant differences were seen in the deformation of the front rail between PDB versus ODB and CTC. Deformation in 60PDB was extremely smaller than that in 56 & 64 ODB and 50CTC.
  Overall, the vehicle deformation of Mini-Cars tended to be larger in 64ODB and 50CTC than in 60PDB (the intrusion into the lower part of the cabin [brake pedal and toe board, etc.] tended to be large in 64ODB and 50CTC).
  Overall, the vehicle deformation of Minivan tended to be larger in 64ODB than in 60PDB.
Notes: <number>

## Slide 20: Summary
<number>
  Dummy injury criteria: In Mini-Cars, no significant difference was observed among 60PDB, 64ODB, and 50CTC for Chest and Legs (in Mini-Car B, the Head injury level tended to be higher in 60PDB than 64ODB, 56ODB, and 50CTC). The criteria were sufficiently met for all injury indices, except Head Gs of the passenger dummy in Mini-Car A.
  In Minivan, overall, injury levels for the driver dummy tended to be lower in 60PDB than 64ODB, though no significant difference was observed. As for the passenger dummy, no significant difference was observed between the two tests for any injury index. In both tests, the criteria were sufficiently met for all injury indices of both dummies.
  The EES in 60PDB was around the same level for Mini-Cars and Minivan.
  The EES in 64ODB was higher for Minivan than Mini-Cars. However, when the EEVC Barrier deformation energy was actually measured, the EES difference between Minivan and Mini-Cars was not as large as when it was calculated using the constant value of 45 kJ.
Notes: <number>

## Slide 21: Conclusion
<number>
  The dummy injury levels indicate that the replacement with PDB cannot be expected to improve “self protection”.
    No significant difference was observed between PDB and ODB in dummy injury levels in the both of Mini-cars and Minivan.
  In the Car to Car test in this study, comparing ODB and PDB, deformation mode of the front rail in CTC was closer to ODB than that in PDB. The difference in deformation of the front rail was remarkable.
  With Minivan (heavy car, 2,110 kg), while the bottom-out was observed in ODB, no bottom-out was observed in PDB. Overall, the vehicle deformation tended to be smaller in PDB.
Notes: <number>

## Slide 22: Calculation Method for EEVC Barrier Energy
<number>
450
650
330
75
75
90
200
mounting flange
steel strip
EEVC Barrier Spec. (Side View)
Va
Unit (mm)
Vb
σb: 1.711 MPa
σa: 0.342 MPa
Energy (E) is calculated from deformation volume (V) and honeycomb stress ():
Equation for the true value of energy
Equation for energy used in this study
Due to difficulties in measuring the deformation volume separately for the main body and the bumper in the area below the red dotted line, the energy absorbed by the entire barrier was calculated simply as follows (the result is estimated to be slightly smaller than the true value):
Q. How is the energy absorbed by EEVC Barrier calculated?
Vab
σa: 0.342 MPa
Notes: <number>

## Slide 23: Appendix
<number>
Notes: <number>

## Slide 24: Vehicle Severity (EES)
<number>
Suppose the deformation energy of EEVC Barrier is 45kJ (UTAC Proposal) :
The deformation energy of EEVC Barrier was actually measured.
64ODB showed the highest EES.
The EES in 60PDB was around the same level for Mini-Cars (light cars) and Minivan (heavy car).
The EES in 64ODB was higher for Minivan than Mini-Cars. However, when the EEVC Barrier deformation energy was actually measured, the EES difference between Minivan and Mini-Cars was not as large as when it was calculated using the constant value of 45 kJ.
Notes: <number>

## Slide 25: Vehicle Deformation
<number>
Passenger Car
50CTC
64ODB (EEVC Barrier)
Notes: <number>

## Slide 26: Vehicle Deformation
<number>
Passenger Car
50CTC
64ODB (EEVC Barrier)
Notes: <number>

## Slide 27: Dummy Injury
<number>
Passenger Car
Driver
Passenger
Notes: <number>

## Slide 28: Vehicle Deformation
<number>
Mini-Car A
60PDB
64ODB
(EEVC
Barrier)
There were big differences in the deformation of the front rail. In 60PDB, the front rail was deformed very slightly.
The intrusion into the upper part of the cabin (instrument panel, A-pillar, etc.) tended to be large in 60PDB, while that into the lower part of the cabin (toe board, etc.) tended to be large in 64ODB.
Notes: <number>

## Slide 29: Vehicle Deformation
<number>
Mini-Car B
60PDB
64ODB
(EEVC
Barrier)
56ODB
(EEVC
Barrier)
Overall, vehicle deformation in 64ODB tended to be large.
60PDB showed the smallest deformation of the front rail.
50CTC
Notes: <number>

## Slide 30: Vehicle Deformation
<number>
Minivan
60PDB
64ODB
(EEVC
Barrier)
Large difference in the deformation of the front rail: Smaller in 60PDB.
Overall, vehicle deformation tended to be small in 60PDB.
Notes: <number>