## Slide 1
<number>
Status Report on
Flexible Pedestrian Legform Impactor Technical Evaluation Group (Flex-TEG) Activities
Transmitted by the expert from Japan
Informal document No. GRSP-45-26
(45th GRSP, 25-29 May 2009,
agenda item 4(a))
26th May 2009
Notes: <number>

## Slide 2
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
8th Flex-TEG meeting
Date : 19th May 2009
Place: TUV Rheinland Group, Cologne, Germany
A. Konosu （Chairperson/J-MLIT/JARI）
B. Been （Secretariat/FTSS-Europe）
O. Zander (BASt)
P. Lessmann (BGS)
O. Ries (ACEA/VW)
R. Fleischhacker (ACEA/Porsche)
T. Kinsky and B. Dreyer (ACEA/Opel)
A. Sipido (ACEA/Ford)
C. Hess and M. Netter (ACEA/Audi)
Y. Takahashi (JAMA/HONDA)
W. Liebers (TUV)
K. Wolff (Continental)
S. Mueller (MESSRING)
C. Roesch (Cellbond)
M. Burleigh (FTSS-Europe)
Total: 17 persons
Attendances
Notes: <number>

## Slide 3
<number>
Main Agenda of the 8th Flex-TEG meeting
5. Flex-GTR-prototype Technical Evaluation Test Results
5.1. Japan Reports (Technical Evaluation)
5.2. BASt and ACEA Reports (Technical Evaluation)
5.3. FTSS Reports (Electrical Parts Update Information)
6. Dynamic Calibration Method for Flex-GTR-prototype
6.1. JAMA-JARI Reports (Study for the Inverse Test)
6.2. BASt Reports (Tentative Corridor for the Inverse Test)
7. Injury Criteria and Thresholds
7.1. Review of Human Tibia Injury Threshold value
7.2. Review of Human MCL Injury Threshold value
7.3. Finalization for Injury Threshold Values for the Flex-GTR-prototype
8. Evaluation Test Schedule for the Flex-GTR-prototype
10. DRAFT Proposal for gtr 9 amendments using Flex-PLI requirements
10.1. DRAFT Proposal for gtr 9 amendments by adding Flex-PLI requirements, Japan (voluntary activity)
11. Working schedule for the Flex-TEG
9. ISO MME code for Flex-PLI
9.1. Suggestion for the ISO MME code for Flex-PLI, MESSRING
Notes: <number>

## Slide 4
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
Evaluation Results on the Flex-GTR-prototype regards to the Repeatability and Reproducibility were presented from Japan, ACEA and BASt.
Flex-GTR-prototype (SN01, SN02, SN03)
SN01
SN02
SN03
5. Flex-GTR-prototype Technical Evaluation Test Results
Repeatability and Reproducibility
Pendulum Test
Good and/or Acceptable Level, in general (Japan)
Inverse Test
Good and/or Acceptable Level, in general (ACEA, BASt)
Simplified Car Test
Good and/or Acceptable Level, in general (Japan)
Actual Car Test
Good and/or Acceptable Level, in general (Japan)
Good and/or Acceptable Level. However, not acceptable level (reproducibility) was also observed in some cases (ACEA, BASt)
Repeatability and Reproducibility of the Flex-GTR-prototype were Good and/or Acceptable level, in non vehicle tests and in simplified car tests.
However, in the actual car test, not acceptable level on the Reproducibility were found in some cases (ACEA, BASt).
Japan stated that it is better to separate the Impactor effect and/or the other effects (test conditions, car parts, etc.) because other effects tend to be involved in the actual car test results.
Sensitivity value of one of a gage (Tibia-3) of the Flex-GTR-prototype (SN03) was strange. It was recommended to re-obtain the value and/or replace to a new gage.
Notes: <number>

## Slide 5
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
5. Flex-GTR-prototype Technical Evaluation Test Results, contd.
Comparability between the Flex-GTR-prototype and Flex-GT
In general, Flex-GTR-prototype outputs are higher than the Flex-GT ones. (Japan, ACEA and BASt)
It is recommended to separate the Impactor effect and/or the other effects (test conditions, car parts, etc.) because other effects tend to be involved in the actual car test results.
Comparability of the Flex-GTR-prototype outputs between the Symmetric Left and Right Bumper Corner Impact Test
Simplified Car Test
Good and/or Acceptable Level (Japan)
Actual Car Test
Evaluation Results on the Flex-GTR-prototype regards to the Comparability outputs between the Symmetric Left and Right bumper corner impact tests were presented from Japan, ACEA and BASt.
Some symmetries were observed (ACEA/BASt)
TEG members discussed a possible consideration of this difference into the threshold values for the Flex-GTR-prototype, also in the respective transformation equations from human thresholds to impactor criteria.
Evaluation Results on Comparability between the Flex-GTR-prototype and Flex-GT were presented from Japan, ACEA and BASt.
Notes: <number>

## Slide 6
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
6. Dynamic Calibration Method for Flex-GTR-prototype
Evaluation Results on the Inverse Test were presented by JAMA-JARI. From their point of view, it takes much time and costs compare to the pendulum test, besides it looks not to have so much merits compare to the pendulum test.
BASt and ACEA stated that main merit of the Inverse Test is impactor condition, i.e. impactor condition is identical in both the inverse test and the car test (free flight, fully assembled, maximum loads, traces, etc.). Better calibration for the impactor is possible.
ACEA emphasized their long experience with the Inverse Testing for several years.
Additionally, BASt proposed tentative certification corridors for the inverse certification.
After the discussion, detailed investigations will be done by several TEG members, and then TEG will decide whether to accept the inverse test as the Flex-GTR-prototype calibration test method or not at the next (9th) TEG meeting.
Notes: <number>

## Slide 7
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
7. Injury Criteria and Thresholds
Proposal values for the Injury Criteria and Threshold values for the Flex-GTR-prototype
Tibia Bending Moment (for Flex-GTR-prototype)
380 Nm (JAMA proposal)
302 Nm (BASt proposal)
MCL Elongation (for Flex-GTR-prototype)
21 mm (JAMA proposal)
Injury Criteria and Threshold values for the Flex-GTR-prototype were proposed by JAMA and BASt respectively.
After the discussion, the JAMA proposed threshold value for the MCL was tentatively agreed.
ACEA stressed that thresholds are directly linked to the discussion on technical feasibility (is part of the TOR of TEG)
On the other hands, as for the threshold value for the Tibia was offered to conduct corroboration study by JAMA and BASt ( + experts ) in order to propose one agreeable value by the next (9th) TEG meeting.
Notes: <number>

## Slide 8
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
TEG member discussed and then agreed above technical evaluation tests schedule.
8. Evaluation Test Schedule for the Flex-GTR-prototype
Jan.
Feb.
Mar.
Apr.
2009
Flex-GTR-proto (SN01), Off-board
Flex-GTR-proto (SN02), M=BUS
Flex-GTR-proto (SN03), Slice
Flex-GTR-proto (SN04), M=BUS
BASt/BGS
ACEA
BASt/BGS
ACEA
BASt/BGS
JAMA
JAMA-1
JAMA-2
May.
Jun.
July.
Aug.
2009
JAMA-3
JAMA-4
JAMA-5
JAMA-6
JAMA-7
JAMA-8
Flex-GTR-proto (SN01), Off-board
Flex-GTR-proto (SN02), M=BUS
Flex-GTR-proto (SN03), Slice
Flex-GTR-proto (SN04), M=BUS
ACEA-4
ACEA-6
ACEA-8
ACEA-2
ACEA-3
ACEA-5
ACEA-7
ACEA-1
FTSS & MESSRING (Demonstration)
At the latest
At the latest
At the latest
NHTSA
KATRI
can use the Flex-GTR-proto (SN01) after the July 2009
Notes: <number>

## Slide 9
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
TEG discussed the ISO MEE code for Flex-PLI measurement items, which was suggested by MESSRING, and then TEG agreed the contents.
The code is going to be submitted to ISO working group of MME code.
9. ISO MME code for Flex-PLI
9.1. Suggestion for the ISO MME code for Flex-PLI, MESSRING
Notes: <number>

## Slide 10
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
Japanese DRAFT Proposal for gtr 9 amendments adding Flex-PLI requirements was explained.
The draft is going to be submitted to 45th GRSP by J-MLIT.
In order to finalize the draft contents by Sep. 2009, chairperson offered to all of the TEG members to review the technical part of the contents.
10. DRAFT Proposal for gtr 9 amendments using Flex-PLI requirements
10.1. DRAFT Proposal for gtr 9 amendments by adding Flex-PLI requirements, Japan (voluntary activity)
Informal documents of 45th GRSP from Japan
(GRSP-45-8 to GRSP-45-11)
http://www.unece.org/trans/main/wp29/wp29wgs/wp29grsp/grspinf45.html
Notes: <number>

## Slide 11
<number>
Latest Flex-TEG Activities (8th Flex-TEG meeting)
By the end of August, 2009 (at the latest)
TEG members are going to continue their technical evaluation tests on the Flex-GTR-prototype.
9th Flex-TEG meeting
Early September, 2009
Flex-TEG members are going to investigate details of the inverse test in order to decide on the acceptance the test for the calibration test.
11. Working schedule for the Flex-TEG
Technical Evaluations: finalization
Tibia Threshold Values: finalization
Inverse Test: finalization
TEG discussed and then agreed the above TEG working plan and schedule.
JAMA and BASt (+ experts) are going to collaborate to make one agreeable Tibia Threshold Value for the Flex-GTR-prototype.
Review of the TOR of the TEG activities
Notes: <number>

## Slide 12
<number>
Thank you for your attentions!
Notes: <number>