## Slide 1
Draft Proposal ECE-R 100
protection against electric shock
Heiko Mertens chairman of GRSP inf. group on electric safety (ELSA)
inf. document GRSP - 45 - 3
Informal document No. GRSP-45-28
(45th GRSP, 25-29 May 2009
agenda item 18)

## Slide 2
history
  12/2006: German proposal to GRPE, Japan presents strategy
  01/2007: GRPE is not longer responsible
  03/2007: WP.29 agreed responsibility to GRSP
  10/2007: USA propose amendment (FMVSS 305)
  11/2007: WP.29 agreed new inf. group ELSA for GTR HFCV
  ELSA:
    Experts of Canada, CLEPA, China, EU-Commission, France, Germany, ISO, Japan, Korea, OICA , Techn. Service, USA
    6 meetings (01/2008 – 04/2009)

## Slide 3
terms of reference
  ECE-R100 (German proposal), attachments 101, 110 and 111 (Japan), FMVSS 305 (USA)
  two modules:
    “in-use“: normal operation (type approval)
    “post-crash“: after defined crash (self certification)
  time frame:
    short-term: ECE-R 100 (“in-use“)
    medium-term: GTR HFCV (“in-use“ and “post-crash“)

## Slide 4
scope
  The following prescriptions apply to safety requirements with respect to the electric power train of road vehicles of categories M and N, with a maximum design speed exceeding 25 km/h, equipped with one or more traction motor(s) operated by electric power and not permanently connected to the grid and the high voltage components and systems which are galvanically connected to the high voltage bus of the electric power train.

## Slide 5
Voltage thresholds
  Class A circuits: ≤ 30 V AC (alternating current) (no requirements) or ≤ 60 V DC (direct current)
  Class B circuits : > 30 and ≤ 1000 V AC or > 60 and ≤ 1500 V DC

## Slide 6
requirements
  protection against direct contact (e.g. test wire in passengers compartment)
  protection against indirect contact (e.g. enclosure)
  isolation resistance (e.g. 100Ω/V for DC buses, 500 Ω/V for AC buses)
  protection of rechargeable energy storage system against excessive current (e.g. fuses)
  functional safety (e.g. avoid vehicle movement during charging)

## Slide 7
Identification
  Approval mark:
  Warning symbol:
  Isolation color of voltage class B wires: orange

## Slide 8
next steps
  adoption of ECE-R 100
  further activities on “post-crash”
  incorporation “in-use“ and “post-crash“ into GTR HFCV

## Slide 9
back-up
  test probes
  shared responsibilities
  introduction of ECE-R 100 into EU type approval system

## Slide 10
test probes

## Slide 11
ECE-R 100
ISO, IEC, SAE
shared responsibilities

## Slide 12
introduction of ECE-R 100 into EU type approval system
  Electrical safety had become an issue in draft of general safety regulation
  EU commission intend to decide up to October 2009 about inclusion of ECE-R 100 (workplan January 2009)
  Actual ECE-R 100 is only related to battery electric vehicles