## Slide 1: 45th GRSP Session Status report of Informal Group on CRS
Pierre CASTAING
Chairman
Informal document No. GRSP-45-29
(45th GRSP, 25-29 May 2009
agenda item 15(a))

## Slide 2: Terms of Reference - Approved ToR
The informal group shall consider the development of a new regulation for “Restraining devices for child occupants of power-driven vehicles” for consideration by GRSP.
The basis of the discussion will be informal documents No. GRSP-42-2 and GRSP-42-27.
A step by step approach shall be implemented
  Phase1: Develop definitions, performance criteria and test methods for ISOFIX Integral “Universal” CRS
In its work, the informal group will take into consideration amongst others the technical expertise of EEVC WG18, EEVC WG12, ISO TC22/SC12, NPACS as well as the results of the discussions held in the informal group and at GRSP.
If necessary, the informal group shall develop complementary test methods and propose alternative judgement criteria.
The target completion date for the informal group shall be the forty-sixth session of GRSP (December 2009) for this first phase.

## Slide 3: Meetings
3Oth January 2008 – OICA – PARIS
1st April 2008 – CLEPA – BRUSSELS
13th May 2008 – SMMT – LONDON
18th June 2008 – CCFA – PARIS
2nd September 2008 – BMVIT – VIENNA
7th October 2008 – ACEA – BRUSSELS
25th November – BNA – PARIS
21st January – BASt – KOLN
11th March 2009 – OICA – PARIS
22nd April 2009 – Test Achat – BRUXELLES

## Slide 4: List of issues & Priorities
Test bench – Priority 1
Classification of CRS – Priority 1
Dummies – Priority 1
Dynamic tests – Priority 1
Components tests – Priority 2
Labelling – Priority 2
Ease of Use / Misuse – Priority 2
Control Of Production – Priority 2
Interoperability with vehicle – Priority 1
Child comfort and health harmlessness – Priority 2
Other
Test bench – Priority 1
Classification of CRS – Priority 1
Dummies – Priority 1
Dynamic tests – Priority 1
Components tests – Priority 2
Labelling – Priority 2
Ease of Use / Misuse – Priority 2
Control Of Production – Priority 2
Interoperability with vehicle – Priority 1
Child comfort and health harmlessness – Priority 2
Other

## Slide 5: Present status
Develop definitions, performance criteria and test methods for ISOFIX Integral “Universal” CRS
Test bench
Classification
Dummies
Dynamic tests
Interoperability with vehicle

## Slide 6: Test bench
The test bench will be based on NPACS bench with Isofix and belt anchorages having same the centreline
There is no need for a dashboard
Seat cushion technical characteristics to be defined based on NPACS bench
Test bench orientation:
  0°
  90°
  180°

## Slide 7: Test bench – Open questions
Head Restraint on the bench?
  Not defined up to now for phase 1
Relative positions of adult seat belt anchorages versus Isofix anchorages positions. (Interoperability with vehicles)
  To be validated in phase 2 for non integral ISOFIX CRS
Isofix anchorages - location of 3rd alternative point? (Interoperability with vehicles)
  Not defined up to now for phase 1
  No solution short term (EEVC WG18 and Swedish research in progress) link with ECE R14

## Slide 9: Classification
Based on stature and maximum weight
Not based on availability of dummies
For Isofix Integral “Universal” CRS limited by (Interoperability with vehicles):
  Maximum dynamic load sustainable by vehicles anchorages
  Maximum space offered by Isofix fixtures

## Slide 10: Classification

## Slide 11: Draft matrix of classification
Size in Cm | Isofix Integral Universal | Orientation | Maximum Weight Child + CRS | Side protection
40-80 | Yes | RF |  | Yes
75-90 | Yes | RF |  | Yes
85-105(8) | Yes | RF or FF | 22 + 10? | Yes
100-130 | Tbd | Tbd |  | Yes
130-150 | Tbd | Tbd |  | Tbd

## Slide 12: Classification
Rearward Facing CRS with support leg to be included in “universal”
Needs standard interface between vehicle floor and support leg contact surface
Interfacing vehicle floor & support leg
  ISO/TC22/SC12 works on this issue (proposal in July)

## Slide 13: Dummies
Q series not Qs for dynamic tests
Use of geometric dummies for size classification

## Slide 14: Dynamic tests
Frontal impact
  Do we have to change the pulse ?
    Final decision to be done on pulse
Lateral impact
  Simple approach in a first step.
    Decision taken
Rear impact
  Keep as it is
    Decision taken

## Slide 15: Frontal impact
Do we have to change the pulse ?

## Slide 16: Lateral impact
Informal Group has review all existing methods to determine the one to be retained
Australian Standard AS/NZ 1754 & 3629.1 - 2004
Fixed Door; P3 Dummy
V 32 km/h ; Pulse 14 – 20 G
ISO - 2008
Moving Door; Q3 Dummy
V 24-26 km/h ; , Door angular velocity corridors for RF and FF seats

## Slide 17
NHTSA Research
Takata linear side impact test device
Moving sled into fixed impactor; Hybrid III 3y & Qs3
V 32 km/h ; Door Velocity 25 km/h.
BRITAX – ADAC
Fixed Door 80° ; Q3 Dummy
V 29 km/h ; Pulse 15 G
ADAC Procedure within EU Consumer tests
Opel Astra Body 80°; Fixed Door; Q0 – Q6 and P10
V 28 km/h ; Pulse 18 G

## Slide 18: Lateral impact
Informal Group has consider first methods delivering required energy level and:
  Promoting energy absorption in the seat
  Including measurable performance criteria
Supported by ISO/TC22/SC12 (Alternative1)
  To provide essential input parameters only of a CRS side impact test method

## Slide 19: Lateral impact configuration

## Slide 20: Input parameters
90° rotation of the test bench on ECE R44 sled
Fixed door panel on the stopping block
Moving Isofix anchorages
ECE R44 rear impact pulse
Management of intrusion distance

## Slide 21: Interoperability with vehicle
Load level in Isofix anchorages
  Definition of a maximum permissible load level on current ECE R14 Isofix anchorages
    Maximum weight / g level
A proposal to reach more flexibility in the application of ISOFIX child restraint could be (Classification):
  A definition of a total weight for the couple [Child + CRS]
  A permissible weight of the child is then depending on child restraint system weight.

## Slide 22: Decisions
Scope: Isofix “universal” integral CRS
Classification based on standing height and maximum permissible weight (Child + CRS)
Q series dummies + special dummies for sizing
NPACS test bench with common centreline
Simple front, side and rear impact test methodology
CRS with support leg qualified as “universal” if interface between floor and support leg defined by ISO

## Slide 23: Draft Regulation
01 April 09
AGREEMENT
CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS /
Regulation No. XXX
UNIFORM PROVISIONS CONCERNING THE APPROVAL OF CHILD RESTRAINT SYSTEM USED ONBOARD OF MOTOR VEHICLES.
UNITED NATIONS
SCOPE
This Regulation applies to ISOFIX Universal Integral child restraint systems for child occupants of power driven vehicles.