|  | United Nations | ST/SG/AC.10/C.3/2010/49 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 7 September 2010 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Thirty-eighth session

Geneva, 29 November–7 December 2010

Item 4 of the provisional agenda

Listing, classification and packing

Special provision 272

Transmitted by the expert from Germany

1.	SP 272 states that “This substance shall not be transported under the provisions of class 4.1 unless specially authorized by the competent authority (see UN 0143).” SP 272 is assigned to:

UN 3319 NITROGLYCERIN MIXTURE, DESENZITIZED, SOLID, N.O.S with more than 2% but not more than 10 % nitroglycerin, by mass; and

UN 3344 PENTAERYTHRITE TETRANITRATE (PENTAERYTHRITOL TETRANITRATE; PETN) MIXTURE, DESENSZITED, SOLID, N.O.S. with more than 10% but not more than 20 % PETN, by mass.

2.	The reference to UN 0143 does not apply to UN 3344. The corresponding entry for UN 3344 would be UN 0150. Therefore it is proposed to add a reference to UN 0150 to SP 272 as follows:

“272	This substance shall not be transported under the provisions of class 4.1 unless specially authorized by the competent authority (see UN 0143 or UN 0150).”

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2009-2010 approved by the Committee at its fourth session (refer to ST/SG/AC.10/C.3/68, para. 118 (b) and ST/SG/AC.10/36, para. 14).