|  | Nations Unies | ST/SG/AC.10/C.3/2010/67 |
| --- | --- | --- |
|  | Secrétariat | Distr. générale 14 septembre 2010 Français Original: anglais |

Comité d’experts du transport des marchandises dangereuses
et du Système général harmonisé de classification
et d’étiquetage des produits chimiques

Sous-Comité d’experts du transport des marchandises dangereuses

Trente-huitième session

Genève, 29 novembre-7 décembre 2010

Point 4 de l’ordre du jour provisoire

Inscription, classement et emballage

Disulfure de diméthyle (numéro ONU 2381): risque subsidiaire de la classe 6.1

Communication de l’expert de l’Allemagne

Introduction

1.	Le disulfure de diméthyle est un liquide volatil inscrit au chapitre 3.2 du Règlement type, sous le numéro ONU 2381, qui est actuellement affecté à la classe 3, liquides inflammables, groupe d’emballage II.

2.	Ces dernières années, on a déploré, à bord de bateaux, plusieurs cas de personnes qui ont présenté des symptômes aigus d’empoisonnement (nausées, maux de tête, évanouissements, problèmes respiratoires), après avoir respiré pendant peu de temps des vapeurs de disulfure de diméthyle qui s’étaient accidentellement échappées de la cargaison.

3.	S’appuyant sur les résultats d’expériences des scientifiques estiment que le disulfure de diméthyle répond au critère de classement dans la division 6.1, groupe d’emballage II, en raison de sa toxicité à l’inhalation, conjuguée à sa volatilité. Une CL50 de 805 ppm pendant quatre heures peut être considérée comme équivalant à une CL50 de 1 610 ppm après une heure d’exposition, compte tenu du paragraphe 2.6.2.2.4.5 du Règlement type. Sur la base d’une pression de vapeur de 2 930 Pa à 20 °C, la concentration de vapeur saturée de disulfure de diméthyle à 20 °C et à la pression atmosphérique normale est calculée comme étant de 113,30 g/m3, ce qui correspond à 26 000 ppm. Les critères d’affectation à la division 6.1, groupe d’emballage II sont donc remplis: V ≥ CL50 et CL50 ≤ 3 000 ml/m3.

4.	Conformément au paragraphe 2.0.3 du Règlement type (Ordre de prépondérance des caractéristiques de danger), le disulfure de diméthyle devrait rester dans la classe 3, avec l’adjonction du risque subsidiaire 6.1. Le numéro ONU 2381 devrait donc être modifié comme indiqué ci-dessous. En conséquence, le disulfure de diméthyle ne relèverait plus de l’instruction de transport T4 mais de l’instruction T7, ce qui nécessiterait de prévoir une période de transition aussi dans le Règlement type.

5.	On trouvera la fiche de renseignements du disulfure de diméthyle mise à jour dans l’annexe au présent document.

Proposition

6.	Dans la liste des marchandises dangereuses du chapitre 3.2, modifier le numéro ONU 2381 comme suit:

| No ONU | Nom et description | Classe ou division | Risque subsidiaire | Groupe d’emballage | Dispositions spéciales | Quantités limitées et quantités exceptées | Emballages et GRV | Citernes mobiles et conteneurs pour vrac |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Instructions d’emballage | Dispositions spéciales | Instructions de transport | Dispositions spéciales |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
| 2381 | Disulfure de diméthyle | 3 |  | II |  | l L | E2 | P001 IBC02 |  | T4 | TP1 |

7.	Ajouter une nouvelle disposition spéciale dans le 4.2.5.3, ainsi conçue:

«TP XX Les instructions relatives aux citernes mobiles figurant dans le Règlement type annexé à la seizième édition révisée des Recommandations relatives au transport des marchandises dangereuses pourront continuer à s’appliquer jusqu’au 31 décembre 2016.».

Annexe

Data sheet to be submitted to the United Nations for new or amended classification of substances 	[English only]

Submitted by……..GERMANY	Date …..31 August 2010

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1. SUBSTANCE IDENTITY

1.1	Chemical name	Dimethyl disulphide

1.2	Chemical formula 	C2 H6 S2

1.3	Other names/synonyms	Methyldithiomethane

1.4.1	UN number 	2381	1.4.2		CAS number 	624-92-0

1.5	Proposed classification for the Recommendations

1.5.1	Proper shipping name (3.1.2)  DIMETHYL DISULPHIDE

1.5.2	Class/division   3	…. subsidiary risk(s)   6.1

packing group   II

1.5.3	Proposed special provisions, if any 	354

1.5.4	Proposed packing instruction(s)		P001

Section 2. PHYSICAL PROPERTIES

2.1	Melting point or range ………..-87.4 °C

2.2	Boiling point or range ………...109.6 °C

2.3	Relative density at :

2.3.1……15 °C

2.3.2……20 °C		1.063

2.3.3……50 °C

2.4	Vapour pressure at :

2.4.1……50 °C		kPa

2.4.2……65 °C		kPa

20 °C		2.93 kPa

2.5	Viscosity at 20 °C ……………….

2.6	Solubility in water at 20 °C ……..2500 ppm

2.7	Physical state at 20°C (2.2.1.1)	liquid

2.8	Appearance at normal transport temperatures, including colour and odour
yellow liquid, odour threshold in air 6 ppm

2.9	Other relevant physical properties

Section 3. FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3) 16 °C cc

3.1.2	Is combustion sustained? (2.3.1.3)

3.2	Autoignition temperature 	°C

3.3	Flammability range (LEL/UEL) %

3.4	Is the substance a flammable solid? (2.4.2)	no

3.4.1 If yes, give details

Section 4. CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?	no

If yes, state:

4.1.1	Inhibitor/stabilizer used

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.1) no

4.2.1	If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.4) no

4.3.1	If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.1) no

If yes, state:

4.4.1	Exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ..................°C

Is the temperature control required? (2.4.2.3.4) yes/no

4.4.2	Proposed control temperature for a 50 kg package		°C

4.4.3	Proposed emergency temperature for a 50 kg package		°C

4.5	Is the substance pyrophoric? (2.4.3) 	no

4.5.1 	If yes, give details

4.6	Is the substance liable to self-heating? (2.4.3) 	no

4.6.1	If yes, give details

4.7	Is the substance an organic peroxide (2.5.1) 	no

If yes state:

4.7.1	Exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package? ……………°C

Is temperature control required? (2.5.3.4.1) 	yes/no

4.7.2	Proposed control temperature for a 50 kg package		°C

4.7.3	Proposed emergency temperature for a 50 kg package		°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.4) 	no

4.8.1	If yes, give details

4.9	Does the substance have oxidizing properties (2.5.1)	no

4.9.1	If yes, give details	.

4.10	Corrosivity (2.8) to:

4.10.1 ……mild steel 	mm/year 	at 	°C

4.10.2 ……aluminium	mm/year  	at	°C

4.10.3 ……other packaging materials (specify)

mm/year	at	°C

mm/year	at	°C

4.11	Other relevant chemical properties

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.1)    190 mg/kg	Animal Species	Rat

5.2	LD50, dermal (2.6.2.1.2)   >2000 mg/kg	Animal Species	Rabbit

5.3	LC50, inhalation (2.6.2.1.3)	mg/l		Exposure time	4 hours

or	805	ml/m3	Animal species	Rat

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.3)	26000 ml/m3

5.5	Skin exposure (2.81) results	 moderately irritating	Animal Species:	Rabbit

5.6	Other data

5.7	Human experience

Workers exposed to 0.31 ppm complained of headaches.

Section 6. SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)
Estinguish fire using water spray. Cargoes in tanks exposed to heat may explode suddenly in or after a fire – keep tanks cool with water, fight fire from a protected position.

6.1.2	Spillage
Wear suitable protective clothing and self-contained breathing apparatus. Avoid all sources of ignition, spillage may evolve flammable vapours. Provide good ventilation. Clean area thoroughly with water.

6.2	Is it proposed to transport the substance in:

6.2.1	Bulk Containers (6.8)	yes/no

6.2.2	Intermediate Bulk Containers (6.5)?	yes/no

6.2.3	Portable tanks (6.7)?	yes/no

If yes, give details in Sections 7, 8 and/or 9.

Section 7. BULK CONTAINERS (only complete if yes in 6.2.1)

7.1	Proposed type(s)

Section 8. INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.2)

8.1	Proposed type(s)	as specified by IBC02

Section 9. MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.3)

9.1	Description of proposed tank (including IMO tank type if known)   as specified by T7

9.2	Minimum test pressure

9.3	Minimum shell thickness

9.4	Details of bottom openings, if any

9.5	Pressure relief arrangements

9.6	Degree of filling	as specified by TP2

  - Unsuitable construction materials	………………………………

_____________

# Footnotes

Conformément au programme de travail du Sous-Comité pour 2009-2010, adopté par le Comité à sa quatrième session (voir ST/SG/AC.10/C.3/68, par. 118 b) et ST/SG/AC.10/36, par. 14).

MF Tansy et al., J. Toxicol. Environ. Health, A: Curr. Iss., 8 (1981) 71-88.