## Slide 1
Geneva, 26 March 2010
The system SUW 2000 - an opportunity for railway networks having different track gauges
First session of the informal UNECE Expert Group on Unified Railway Law

## Slide 2
INTRODUCTION
rolling stock element – i.e. freight bogie (type P-053/BK) with gauge-changing wheel sets, passenger bogie (type P-057/BK) with gauge-changing wheel sets;
infrastructure element – i.e. track gauge-changing stand.
The system SUW 2000 consists of two basic components:
The Polish system SUW 2000 for automatic track gauge-changing was designed by Eng. Ryszard Maria Suwalski, D.Sc.

## Slide 3
CERTIFICATION
Certificates of conformity issued in Russia by the Certification Register on Federal Railway Transport (RC FTK):
freight bogie type 4RS/N was considered in the UIC/OSZhD Leaflet No. 516 and in the Technical Specifications of Interoperability for freight wagons (appendix Y),
Acceptances in the area of the EU:
for a passenger coach type 306 A,
for a bogie type 25 AN/S.
passenger bogie type 25 AN/S will be considered in the UIC/OSŻD Leaflet No. 524 and in the Technical Specifications of Interoperability – passenger coaches.
Plans for the time to come: to obtain a certificate issued by the German Federal Railway Office (EBA).

## Slide 4
COACH TYPE 306A – COMFORT TO CUSTOMERS
The passenger coaches type 306A are sleeping cars having the EURONIGHT standard equipped with, among others:
air-conditioning,
vacuum toilets (closed circulation WC),
business-class compartments,
soundproofed interior of car,
suspension system providing
a fully smooth run.

## Slide 5
Connections with Lithuania (PECT I) during 2000 - 2005.
OPERATION TO DATE (1)
mileage of 6 passenger coaches amounted to from 488 400 km to 625 200 km,
total number of car gauge-changing operations on the track gauge-changing stand – 5 754;
mileage of 4 freight wagons amounted to from 100 055 km to 101 137 km,
total number of car gauge-changing operations on the track gauge-changing stand – 850.

## Slide 6
Connections with Ukraine (PECT III) during 2003 – 2006 and since 31/05/2009.
OPERATION TO DATE (2)
mileage of 4 passenger coaches belonging to PKP Intercity amounted to from 136 085 km to 407 760 km,
total number of car gauge-changing operations on the track gauge-changing stand – 892;
mileage of 4 passenger coaches belonging to UZ amounted to from 135 369 km to 381 480 km,
total number of car gauge-changing operations on the track gauge-changing stand – 850,
Services were performed with temperatures from 35 to -32OC.
planned summing-up of stage 1 operation after its reopening since 31 May 2009 is to follow in November this year – after reaching the average mileage of 100 000 km.

## Slide 7
POTENTIAL APPLICATION – EURO-ASIAN TRANSPORT CORRIDORS
Interfaces of railway systems with different gauge of track in Euro-Asian transport corridors – as an effective tool for gaining interoperability in railway mode systems.

## Slide 8
WARSZAWA
MIŃSK
MOSKWA
1313 km
BERLIN
563 km
750 km
SUW 2000
Terespol
Brest
Existing state
POTENTIAL APPLICATION – PANEUROPEAN TRANSPORT CORRIDOR II

## Slide 9
WORK SIMULATION OF THE SYSTEM SUW 2000

## Slide 10
CONCLUSIONS
Use of a many-years experience of PKP with the system SUW 2000 is highly advisable.
One should arrange a close co-operation between railways and industry in favour of the system SUW 2000 implementation in both passenger and freight services in the Euro-Asian transport corridors (including PECT I, II and III situated as on the Northern and Central Axis of TEN-T).

## Slide 11
Thank you
for your
attention.