## Slide 1: Final Rulemaking to Establish 2012-2016 Light-Duty Vehicle CAFE and GHG Standards
Joint Briefing for WP29
June 2010
Informal document No. WP.29-151-05,
agenda item 6.
Notes: <number>

## Slide 2: Overview
<number>
Final Rule Overview
Key Elements of Joint National Program
Estimated Costs and Impacts

## Slide 3: Final Rule Overview
<number>
EPA and NHTSA have issued a joint Final Rule for closely-related standards that together comprise the “National Program”
Rule finalizes strong and coordinated federal GHG and CAFE standards
  Consistent with President Obama’s May 19, 2009 Announcement and the EPA-NHTSA Joint Notice of Intent
  Coordinated national standards which provide regulatory certainty and consistency for the auto industry
  Avoids separate NHTSA, EPA, and state regulations
  Automakers can meet NHTSA, EPA, and California requirements with a single national fleet
National Program will achieve substantial reductions in fuel consumption and GHG emissions

## Slide 4: EPA CO2 Standards
<number>
EPA’s standards estimated to achieve a fleet-wide level of 250 grams/mile of CO2 in model year 2016
  Standards phase in beginning in model year 2012
Fleetwide CO2 standard can be met partially through credits from improved air conditioner (A/C) operation
  A/C credits include CO2 & hydrofluorocarbon (HFC) refrigerant reductions
  HFC refrigerant is a powerful GHG
The 250 gram/mile CO2 standard corresponds to 35.5 mpg “equivalent” if all reductions resulted from fuel economy improvements
Notes: <number>

## Slide 5: NHTSA CAFE Standards
<number>
NHTSA’s final CAFE standards require vehicles to meet an estimated combined average fuel economy level of 34.1 in 2016
The difference between the EPA and NHTSA standards
  Due in part to statutory differences, A/C improvements are not credited toward compliance with the NHTSA CAFE standards

## Slide 6: Standards are Footprint Attribute-based
<number>
Each manufacturer’s standard based on the footprint of vehicles produced - actual standards are curves which equate a vehicle size to its specific CO2 or MPG target
Each company’s “standard” is footprint curve (see Appendix)
Vehicle Type | Example Models | Example Model Footprint (sq. ft.) | CO2 Emissions Target (g/mi) | Fuel Economy Target (mpg)
Example Passenger Cars |  |  |  | 
Compact car | Honda Fit | 40 | 206 | 41.1
Midsize car | Ford Fusion | 46 | 230 | 37.1
Fullsize car | Chrysler 300 | 53 | 263 | 32.6
Example Light-duty Trucks |  |  |  | 
Small SUV | 4WD Ford Escape | 44 | 259 | 32.9
Midsize crossover | Nissan Murano | 49 | 279 | 30.6
Minivan | Toyota Sienna | 55 | 303 | 28.2
Large pickup truck | Chevy Silverado | 67 | 348 | 24.7

## Slide 7: EPA Program Flexibilities
<number>
Emission banking and trading elements
Flex-fuel vehicle (FFV) credits
  MY2012 – 2015 credits similar to CAFE, MY2016+ credits based on actual E85 fuel use
Air conditioning HFC and CO2-related reduction credits
Early credit opportunities for doing better than California or CAFE
Innovative technology credits
Advance technology credits
Provisions for medium & small sales volume companies

## Slide 8: NHTSA Program Flexibilities
<number>
EPCA/EISA limit ability to offer flexibilities
Credit banking
  5-year carry-forward
  3 year carry-back
Credit trading and transferring, starting with credits earned in MY 2011, and with some EISA restrictions
  Trading -- between manufacturers
  Transferring– between a manufacturer’s car and light truck fleets
Alternative fueled vehicle credits allowed per EISA (e.g., the FFV credit)

## Slide 9: Summary of Costs and Benefits
For lifetime of 2012-2016 vehicles:
  1.8 billion barrels of oil reduced
  960 million metric tons of CO2 eq. reduced
  2016 per-vehicle costs of approximately $9,50
  Compliance costs for the industry of <$52 billion
  Total benefits of $240 billion & net benefits of $190 billion
    Using $21/ton CO2 valuation and 3% discount rate
Net present value of net benefits through 2050 with a 3% discount rate = $1.6 trillion
<number>

## Slide 10: Consumer Impacts
Main finding – payback period for MY 2016 vehicles
  Less than 3 years for buyers who pay cash
  Monthly fuel savings greater than loan payment increase by $11 to $15 per month for typical 5-year loan
Lifetime net savings of more than $3,000 using a 3% discount rate (total fuel savings of ~$4,000)
<number>

## Slide 11: HTTP://WWW.NHTSA.GOV/FUEL-ECONOMY HTTP://WWW.EPA.GOV/OTAQ/CLIMATE/REGULATIONS.HTM
Rulemaking Documents and Additional Information
<number>

## Slide 12: Appendix

## Slide 13: Standards are Footprint Attribute-based
<number>
Each manufacturer’s standard based on the footprint of vehicles produced - actual standards are curves which equate a vehicle size to its specific CO2 or MPG target
Final NHTSA Car and Truck Standard Curves:
Truck standard curves
Car standard curves

## Slide 14: EPA Standard Curves
<number>
Final EPA CO2 Standard Curves:
Truck standard curves
<number>
Car standard curves