## Slide 1: PMP Progress Report
Activities since GRPE 58
Heavy Duty Validation testing Exercise completed in October
Draft report and draft proposal to insert PN measurement into Regulation 49 prepared
2 day Informal meeting held at JRC in Ispra on 14th & 15th December to discuss results of exercise, above draft documents and VPR calibration round robin plans
Documents updated and submitted for consideration by GRPE as Informals 3 & 12, consequential amendments to Regulation 83 also prepared (Informal 4)
Informal document No. GRPE-59-27
(59th GRPE, 11-15 January 2010,
agenda item 3)

## Slide 2: PMP Progress Report
Ongoing & Future Activity
Heavy Duty Validation Exercise report & Regulation 49 Proposal to be finalised and submitted as Working Documents for GRPE 60
VPR Calibration Procedure Round Robin & Workshop scheduled to start March 2010
Heavy Duty Round Robin exercise – scheduled for completion in mid 2011

## Slide 3: PMP Informal 12 – Draft Heavy Duty Validation Exercise Report
Describes Validation Exercise. Presents results, conclusions & recommendations.
PN measurement performed well
  (DPF) Golden Engine results were from 5-8x109 (ETC & hot WHTC) through 2-3x1010 (WHSC) to 4x1011 (cold WHTC) cf ~4x1013 engine out
  Repeatability ranged from 20-70%, variability on WHSC was found to be high, due to some passive regeneration on WHSC
  Reproducibility 41-45% on WHTC, 81-86% on WHSC
  High tunnel background contributions found in some labs’ CVS systems, sufficient to influence results from low emission cycles
  PFDS and low tunnel background CVS measurements distinguishable from tunnel background across all cycles
Results from other PN measurement systems conforming to PMP measurement principles generally within 15% of Golden System results

## Slide 4: PMP Informal 12 – Draft Heavy Duty Validation Exercise Report
Recommendations
  Labs should monitor tunnel PN background and take steps to manage it by cleaning, pre-conditioning and test schedule design
  Variability in PN emissions on WHSC due to passive regeneration needs to be accounted for in setting PN limit values
  Retain 23nm PNC cut-off size
  PN sample flow extraction needs to be compensated for in controlling PFDS proportionality of sampling and (for total sampling type PFDS) in PM calculation
Plan to finalise and submit as Working Document (English only) for GRPE 60
Any further comments in writing by end of February please

## Slide 5: PMP - Informal 3 Regulation 49 Proposal
Inserts PN measurement into Reg 49 as a new, unreferenced Annex 4C
Specifies procedures for determining PN over Annex 4B (WHDC) test procedures
Details PN measurement system specification (consistent with Regulation 83, Annex 4A, Appendix 5)
Compensation for PN sample flow extraction required in controlling PFDS proportionality of sampling and (for total sampling type PFDS) in calculating PM
PN calculation as per Regulation 83, using total (equivalent) dilute exhaust mass flow, divided by density to give volumetric flow, multiplied by pcrf, PNC linearity correction factor and mean particle concentration over test

## Slide 6: PMP - Informal 3 Regulation 49 Proposal
Includes measurement of PN during periodic regeneration, with weighted average result calculated according to WHDC procedures
  Multiplicative or additive, upward or downward regeneration adjustment (k) permitted.
14% cold WHTC weighting factor used as per latest WHDC agreement
Includes some clarifications to PN measurement equipment specification
PMP – Informal 4 Regulation 83 Proposal
Makes consequential clarifications to PN measurement system in Regulation 83
Corrects Figure 13 which appears to show PM sampling probe outer, rather than inner, diameter as 12mm