## Slide 1: PMP Heavy Duty Validation Exercise
Inter-laboratory exercise at 5 labs: JRC(x2), AVL-MTC, Ricardo, UTAC, EMPA
January 2008 – November 2009
DPF equipped Golden Engine
2 Golden Systems (CVS & PFDS)
Golden Engineer
Common fuel & lubricant
Test matrix included multiple repeat WHTC (cold and hot), WHSC, ETC and ESC cycles
Informal document No. GRPE-60-16
(60th GRPE, 7-11 June 2010, agenda item 3)

## Slide 2: PM Observations
Generally well below 10mg/kWh
Minimal cycle dependency
Some high results due to high tunnel background contribution

## Slide 3: PN Emissions Levels
Highest emissions highest over cold start cycle
High temperature operation in WHSC and ESC showed some increased emissions due to passive regeneration

## Slide 4: PN Repeatability
c.20% WHTCcold, 50% WHTChot, c.20% WHTCcombined, 60-70% WHSC
Similar repeatability CVS and PFS

## Slide 5: PN Reproducibility
30-50% WHTCcold, 50-80% WHTChot, c.50% WHTCcombined, c.80% WHSC

## Slide 6: Dilution System Background Influence
In some labs’ CVS dilution systems, background levels were significant over low emission cycles

## Slide 7: WHSC Passive Regeneration Impacts
~65% of cycle in temperature window in which passive regeneration can occur
Increased emissions and variability

## Slide 8: Agreement of Different PN Measurement Systems
Calibrated systems generally agreed well with Golden System
High system background on some uncalibrated systems gave higher offsets at lower emissions levels

## Slide 9: Conclusions
  PN Measurement System performed reliably with no significant failures
  PN emission levels over cold WHTC were ~4×1011 #/kWh. At these emission levels, dilution system background is insignificant.
  PN emission levels over hot start WHTC and ETC cycles were <2×1010 #/kWh.
  Passive regeneration occurring over the WHSC and ESC cycles results in an increase of the emissions, up to 6×1010 #/kWh, and in variability due to influence of initial DPF fill state
  Background in some labs CVS dilution systems was a substantial influence on their hot start cycle results
  Alternative systems correlated closely with the GPMS
  Repeatability and reproducibility levels were similar for Full and Partial Flow Dilution Systems, ranging from:
    ~20% and ~40%, respectively, over cold WHTC ; to
    ~70% and ~80%, respectively, over WHSC, due to passive regeneration related effects

## Slide 10: Recommendations
Labs should monitor and manage tunnel background e.g. via use and cleaning of PFDS, test scheduling, tunnel pre-conditioning
Higher variability on WHSC (due to passive regeneration) needs to be allowed for in setting of PN limit values
PN sample flow extraction should be corrected for in PFDS control & PM measurement (total sampling type)