## Slide 1: Informal Group on Gaseous Fuelled Vehicles (GFV)
Report to 60th GRPE June 2010
Informal document No. GRPE-60-20
(60th GRPE, 7-11 June 2010,
agenda item 6.2)

## Slide 2: Meetings GFV Group
9th GFV meeting
  28 April 2010 Brussels (CLEPA)
10th GFV meeting
  08 June 2010 Geneva

## Slide 3: Agenda items GFV
NMHC + CH4 versus THC in R.115
  Retrofitted NG vehicles
Dual-fuel (diesel-gas) HDV
  Test requirements R.49 (OEM)
  Requirement R115 (retrofit)
Mixed-fuel (petrol-gas) LDV
Improvements of R.115

## Slide 4: NMHC + CH4 versus THC Retrofitted NG vehicles
CH4 correction factor for Retrofit NGV justified?
2 small evaluation studies performed :
  TNO: 4 vehicles – JRC: 2 vehicles
  To determine the CH4 conversion of
    a methane optimized catalyst
    a petrol optimized catalyst

## Slide 5: Result test programme
CH4 efficiency Methane Catalyst: ~ 97%
CH4 efficiency Petrol Catalyst: ~91%
Average K factor = ~0.31
Applicablility under consideration
  Legal aspects EC

## Slide 6: Dual-Fuel (diesel-gas) HDV
Growing interest for Dual-Fuel HDV
  Workshop 30-31 March 2010 Brussels
OEM requirements  R.49
Retrofit provisions  R.115 and R.49
Dual Fuel approaches for NRMM
Proposed actions in GFV group:
  Investigation of the different Dual-Fuel types and test-procedures needed
  Task-force for HD-DF
    starting with R.49
    Parallel provisions for R.115 will be investigated to.

## Slide 7: Mixed-fuel (petrol-gas) LDV
No emission requirements for petrol-gas (bi-fuel) vehicles who can use gas and petrol not only separately but also at the same time: “mixed fuel types”.
First proposal for the calculation of THC and CO2 emissions.
A special task-force will investigate technologies and test procedures

## Slide 8: Improvements R115
Ongoing activity in the GFV group to update and improve the R.115 text.
A separate proposal for clarification in R115 concerning the applicability of Euro 5 TA vehicles was tabled in the 10th GFV.
  In existing situation will R.115 suppl. 4 (retrofit) be applicable for Euro 5 from august 2010.
  The proposal for more clarification resulted in a fundamental discussion on retrofit versus OEM gas vehicle solutions of Euro 5 vehicles.
  Discussion will continue in GFV group

## Slide 9: Next GFV-meetings
GFV meeting planned in October 2010 (no date/place confirmed yet)
Request for a half-day meeting in conjuncting with 61th GRPE.
--------------