## Slide 1: Revisions To Heavy Duty Validation Report
General
Numerous clarifications to text as requested at December meeting
Partial flow systems referred to consistently as PFDS throughout
‘background’ changed to ‘tunnel background’ throughout

## Slide 2: Revisions To Heavy Duty Validation Report
Executive Summary
Exec Summary added outlining exercise and summarising conclusions
Section 3.9 – Particle Number Measurement Systems
‘Alternative’ systems renamed ‘PMP type’ systems
Description of PMP type systems tested added
Description of additional instrumentation employed added
Section 3.10.2 – Summary of Preliminary Experiments
Explanation of reason for <23nm solid particle investigations added along with reference to US study
Explanation that high WHTC >3nm results are total particles added

## Slide 3: Revisions To Heavy Duty Validation Report
Section 3.10.3 – Daily Protocol
Description of Continuity Protocol Added
Section 4 – Statistical Analyses
Terminology aligned with ASTM/ISO
Explanation of relevance of unbalanced sample equations adedd
CoV’s defined
Section 5.1 – Calibration and Validation, Mass Systems
Observations on PM reference filter weighings added (no deviation from temperature or relative to humidity requirements but reference filter mass variability sometimes on border of +/-5ug criteria)

## Slide 4: Revisions To Heavy Duty Validation Report
Section 5.2 – Calibration and Validation, Number Systems
Description of Golden System calibration added
Penetration measured with both monodisperse & polydisperse aerosol
Dilution ratio measured using HC tracer + FID
PNC linearity via primary method (i.e v electrometer), electrospray PAO aerosol
Section 6.1 – Emissions Results, Full Flow & Partial Flow PM
Purpose of PM measurements in this programme clarified (not making recommendations)
Observations clarified as being observations of this programme only

## Slide 5: Revisions To Heavy Duty Validation Report
Section 6.3 – Emissions Results, Gaseous Emissions
Observations on raw v dilute differences and CO and HC diluent background levels noted
Comparison of variability to LD_ILCE added, comparison with WHDC data to be added
Section 9.1 – Discussion and Overview, Particulate Measurement
Filter loading recommendation deleted
Tunnel background discussions, e.g. comparison with PM emissions results, clarified as being observations of this programme only
Clarified that PFDSs used in this programme were relatively new and clean
Clarified that, after exclusion of outliers all PM results were below Euro VI 10mg/kWh limit
Comments on suitability of PFDS over CVS redrafted. PFDS may be preferable due to greater ease of controlling tunnel background. Where CVS used labs should take care to minimise tunnel background

## Slide 6: Revisions To Heavy Duty Validation Report
Section 9.3 – Simultaneous PN and PM Measurement
Recommendations added for;
  1 Hz PN sample flow signal (or feeding back sample flow) to increase accuracy of flow rate control
  Compensation for PN sample extraction in controlling PFDS proportionality
  Compensation for PN sample extraction in PM calculation for total sampling type PFDSs
Section 9.10 – Alternative Approach To Sampling for PN Measurements
Clarified that discussion of fixed DF approach is an observation on a potential alternative technique which may be worthy of further research in future, not a recommendation.

## Slide 7: Revisions To Heavy Duty Validation Report
Section 10.7 – General Conclusions
Clarified that PM consistently below 10mg/kWh, and therefore measurement technique is suitable for assessing compliance with Euro VI limits
Clarified that PM measurements in this programme were generally not distinguishable from tunnel background
Section 11- Recommendations
Recommendations added that;
  PN Tunnel background should be monitored and minimised
  PN tunnel background subtraction should be permitted for CoP & ISC
  Higher PN variability on WHSC needs to be considered in limit value setting
  Retain 23nm PNC cut-off for heavy duty as well as light duty
  Compensate for PN sample flow extraction in controlling PFDS proportionality & PM calculation (total sampling type PFDSs)

## Slide 8: Revisions To Regulation 49 Proposal
Compensation For Particle Number Sample Extraction
Where PN sample >0.1% of dilute exhaust gas flow, flow rate used for maintaining proportionality must be compensated by feeding back sample or mathematical correction.
PN sample flow signal (or PN sample – equivalent returned flow) signal must be 1Hz and accurate to 0.1% of dilute exhaust flow rate
For total flow type PFDS, PM must also be corrected for PN sample extracted
Time Alignment
Time alignment procedure redrafted for consistency with WHDC using ‘transformation time’ (t50)

## Slide 9: Revisions To Regulation 49 Proposal
Determination of Particle Numbers
Clarified that instantaneous particle concentrations should be corrected to standard conditions
Periodic Regeneration Results
Additive regeneration adjustment (k) added as an option as per WHDC
Weighted WHTC Result
Cold start weighting factor changed to 14% in line with latest WHDC discussions

## Slide 10: Revisions To Regulation 49 Proposal
Equipment Specification
Clarification inserted that sampling should be from a homogeneous flow
Particle sampling probe/point and transfer tube inner diameter deleted
Clarification added common or separate pre-classifiers may be used for PM and PN
EN 1822 reference updated and equivalent standards accepted
Calibration URL reference updated
Clarification added that upstream and downstream concentration measurements used in pcrf calibrations should be corrected to the same conditions
Requirement for confirmation of PND1 and ET temperatures clarified