## Slide 1: WLTP Strawman Proposal for DHC
United States Delegation
GRPE meeting in Geneva
January 15, 2010
WLTP-DHC-02-19

## Slide 2: Additional Ideas for DHC
Acknowledge that harmonization is the goal
However, there is the concern averaging and combining disparate driving traces from different nations (and road types) could be problematic for some contracting parties
  i.e. concern with averaging “apples with oranges”
Proposal
  Statistically separate similar driving patterns from different countries
  Define N “phases” (or “bags”) of driving that captures these differences
  Each nation could average the N Phases, using weights appropriate for their regions

## Slide 3: 1. Separate similar driving patterns from different countries
It is conceivable that peak driving in one country or region could be statistically similar to off-peak driving in another
It could also turn out that (Similarly,) “urban” driving in one city could be similar to “rural” driving in another
The proposal is to do a statistical analysis of the data before it is “classified” or “binned” and combined
This analysis would look for patterns of similar driving around the world and group them

## Slide 4: Similarity
Contracting parties would submit second-by-second driving data by certain criteria
  Peak vs off peak
  Local vs arterial vs motorway (other road types?)
Test statistically for differences
  Chi-Square tests?
    Applied to histograms (one-way, two-way, etc.)
    Perhaps too sensitive?
  Kolmogorov-Smirnov?
    Applied to cumulative frequency distributions
      One-way, two-way

## Slide 5: Example
India rural …
US urban off peak …
Japan urban peak …
Europe urban off-peak …
Phase 2
Phase 3

## Slide 6: 2. Define N phases of driving that captures these differences
An illustrative example
Phase 1
Phase 2
Phase 3
Phase 1
repeat
Phase 4
Phase 5
Phases should be >250 sec each

## Slide 7: 3. Each nation could average the N Phases, using weights appropriate for their regions
e.g

## Slide 8: Goal is harmonization
Country specific weighting factors should be used in the event that a single cycle cannot satisfy all needs
Will manufacturers use different engine calibrations for each region? (especially on hybrid electric vehicles)
  For conventional gasoline (petrol) vehicles, calibrations will probably not differ much – if emissions standards are similar
  US drivers (who drive mostly on highways) are still buying many Toyota Priuses (which were originally calibrated largely for urban driving)
  If manufacturers need to have separate calibration for India than U.S. (for example), perhaps that could be the best option for the consumers of those two nations
    In 2005 US consumers demanded that labels (on hybrids especially) be more representative of real world fuel economy, so EPA added extra (off cycle) phases to the FTP cycle and weighted them specifically for US driving activity

## Slide 9: Conclusions
The approach provides an alternative way to combine disparate data by first looking for similarities in the data before averaging
This alternative methodology would still provide a harmonized drive cycle based on common speed traces
  Use of common sets of weights would allow comparison across regions
Each contracting party could have different emission rates via regional weights
  Allows for harmonization as well as regional specificity or uniqueness - Very flexible!
  Engine calibrations not expected to vary widely (with similar emissions standards)
  If variations occur, then customers will likely demand it